## Slide 1: INFN Pisa activity report RHD WP5
Maria Giuseppina Bisogni
Universita’ e INFN Pisa
On behalf of
RDH PISA

## Slide 2
simulazione e misura della distribuzione dell’attività ß+ prodotta
Simulazione Monte Carlo
La PET per il monitoraggio della terapia con particelle cariche
Misura sperimentale
protons
Sistema PET
V. Rosso, A. Kraan, N. Belcari, F. Collini, A. Del Guerra,
S. Ferretti, G. Sportelli, E. Zaccaro
Uni and INFN Pisa
Notes: 2

## Slide 3
PMMA
proton
simulazione Monte Carlo del profilo (piano y-z) di attività per T= contributo dei diversi isotopi per T<120s
TPS: Syngo PT Planning VC12, Siemens)
2 Gy uniform on 27 cm3 (PTV) 3cm<z<6cm
62.3 MeV - 90.8 MeV (17 EL)
∆Tirr= 146 seconds
FLUKA: esempio di sviluppo spazile e temporale

## Slide 4
z
x
y
PMMA
proton
TPS: Syngo PT Planning VC12, Siemens)
2 Gy uniform on 27 cm3 (PTV)
62.3 MeV - 90.8 MeV (17 EL)
∆Tirr= 146 seconds
Time [s] | 15-O (%) | 11-C (%) | 10-C (%) | 8-B (%) | 14-O (%) | Other (%)
30 | 27.0 | 8.6 | 7.6 | 18.3 | 0.7 | 37.7
60 | 34.4 | 11.8 | 9.6 | 14.7 | 1.0 | 28.5
90 | 38.4 | 13.9 | 9.7 | 12.6 | 1.1 | 24.3
120 | 40.4 | 15.0 | 9.7 | 11.7 | 1.2 | 22.0
150 | 44.1 | 17.1 | 9.7 | 9.4 | 1.4 | 18.4
180 | 47.1 | 19.3 | 8.8 | 7.6 | 1.4 | 15.7
Simulazione Monte Carlo del contributo dei diversi isotopi a diversi istanti
FLUKA: esempio di sviluppo temporale

## Slide 5
Come misuriamo sperimentalmente l’attività +?
2 teste planari, ciascuna 10x10 cm2
4 moduli di rivelazione per testa
DoPET: un sistema PET in-beam

## Slide 6
  LYSO:Ce Scintillating crystals: 2 x 2 x 16 mm3 pixel
  23 x 23 pixels
PS-PMT H8500
  49 x 49 mm2 active area, 8 x 8 anodes
  12 stage dynode
Front-end:
  Resistive chain 64 inputs/8+8 outputs SCD
  2D chain 8+8 inputs/
  2+2 outputs;
  pre-amp
due teste statiche
4 vs 4 moduli
DoPET: modulo rivelazione
Notes:   SCD (symmetric charge division);

## Slide 7
Anger-like signals
LYSO1A
Host PC
USB Controller
MAINBOARD
PMT 4B
DAQ 4B
DAQ 4A
PMT 4A
DAQ 3A
Master FPGA
DAQ 2A
Anger-like signals
Timing signals
coincidence triggers
Timing signals
DAQ 1A
PMT 3A
PMT 2A
PMT 1A
DAQ 3B
DAQ 2B
DAQ 1B
PMT 3B
PMT 2B
PMT 1B
CFD
CFD
CFD
CFD
CFD
CFD
CFD
CFD
LYSO2A
LYSO3A
LYSO4A
LYSO1B
LYSO2B
LYSO3B
LYSO4B
4 vs 4
FPGA based acquisition and coincidences processing
Time window 5 ns
DoPET: Data Acquisition architecture

## Slide 8
30
60
90
120
180
240
Time [s]
TPS: Syngo PT Planning VC12, Siemens)
2 Gy uniform on 27 cm3 (PTV)
62.3 MeV - 90.8 MeV (17 EL)
∆Tirr= 146 seconds
DoPET: Presa dati al CNAO, Pavia

## Slide 9
30
60
90
120
180
240
Time [s]
calcolo ∆w50%
Dati CNAO vs simulazione MC

## Slide 10
FLUKA: esempio di sviluppo spazile e temporale
Fantoccio con cavita’: air-cavity of 34 mm diameter and 5 mm height starting at a depth of 4 cm from the beam entrance surface (PTV 3cm<z<6cm)

## Slide 11
MC PET pre-calcolata
PET misurata
CT, parametri trattamento, tempo
simulazione Monte Carlo dell’attività
TPS: distribuzione dose
Field 1
confronto
AZIONE?
Una procedura per il monitoraggio dei trattamenti

## Slide 12
9 vs 9
Area attiva 154x154 mm^3

## Slide 13
100mm
30mm
16mm
9 vs 9: prime immagini
Cavita’ riempita con soluzione contenente 18-F
Immagine non processata!

## Slide 14: INSIDE Project
CNAO
PRIN INSIDE
project:
INnovative Solutions for
In-beam DosimEtry in Hadrontherapy
Centro Fermi project:
Innovative Non Invasive Imaging of Dose Release in Hadrontherapy
INFN RDH project:
Research & Developments for Hadrontherapy
PRIN MIUR 2010-2011 - 2010P98A75
Notes: The monitoring is based on the detection of different signal produced by the beam:
Annihilation gammas from β+ emitters (PET)
Prompt charged secondaries (mainly protons)

## Slide 15
INSIDE
Innovative Solutions for In-beam DosimEtry in hadrontherapy
aims at building an in-beam, multimodal profiler for Hadrontherapy
Beam
511 keV
511 keV
prompt
proton
The monitoring is based on the detection of different signal produced by the beam:
Annihilation gammas from β+ emitters (PET)
Prompt charged secondaries (mainly protons)

## Slide 16: Multimodal approach: The INSIDE project @CNAO
PET heads
Charged
tracker
CNAO
nozzle
INSIDE prototype
In-beam dose profiling by PET activities and charged secondaries tracking .
G. Giraudo
INFN Torino
Mechanics and operation optimized to be tested (and finally operated) at CNAO
Notes: Sliding pet edges above and below the couch range 200-600 mm +/- 100 – 300 mm wrt isocenter
Charged tracker box: 900-600 wrt the beam
Chariot (mounted on wheels) to be easily placed or removed and parked outside the treatment area

## Slide 17
A. Pileiro, G. Pirrone, M.Morrocchi, A. Lodola
INFN Pisa
R. Wheadon INFN Torino

## Slide 18
G. GIRAUDO
INFN Torino
PET detector updates

## Slide 19
G. GIRAUDO
INFN Torino
PET detector updates
COOLING PLATE – NEW DESIGN
ALUMINIUM ALLOY AlSi7Mg T6  150 W/m∙K
AISI 316 L  15 W/m∙K
Tube embedded in the melted plate
found an art foundry (ITALFOND) plate in order: minimum 8 pieces

## Slide 21: Development of a 64-channel Front End ASIC
Technology | Standard 0.35um CMOS
Power supply | 3.3V
No. of channels | 64
Dynamic range |  2400 p.e.
Minimum threshold level | Single photon
SNR | 20dB
Time resolution | 500ps FWHM
Internal ADC resolution | 10 bits
Current consumption | ≤ 10mW/channel
Read-out frequency | 100 MHz
Digital links | LVDS
Main specifications of the ASIC
Detection module: 16x16 SiPM pixels read-out by four 64-channel ASICs BASIC64
The ASIC provides the energy (in digital) of the detected events and an accurate trigger signal
C. Marzocca et al.
Politecnico Bari
Italy
Notes: This is the outline of the presentation.
Fist of all, we needed an accurat model of the detector in order to perform reliable simulations at circuit level. So, the classical model of the SiPM has been modified by adding some relevant features which gives remarkable contributions to the electrical behaviour of the detector itself and, moreover we set up a suitable extraction procedure to evaluate the paramenters involved in the model.
After that, different front-end circuit solutions have been compared to find out the most suitable one, considering the SiPM characteristics. Some prototypes of the very first front-end have been realized and some results fromt their characterization will be shown.
The very first version of the f.e. has been equipped with more building blocks and a first version of the complete analog channel has been designed, realized and characterized. Also in this case some measurements results wil be provided.
Next, the design of an 8 channel test chip has been carried out, togheter with the architecture of the digital read-out section. The chip has been submitted to a MPW for fabrication at the end of July and we expect the delivery of the prototypes by the first part of October.
Eventually some possible future work will be described

## Slide 22
Front-end approach for the SiPM: two matched common-gate input buffers in parallel, one for time measurement, one for charge measurement
Fine tuning of the SiPM bias (8 bit DACs, LSB less than 10mV, one every 4 channels)
Both SiPMs “p-on-n” and “n-on-p” can be used
Input impedance of the analog channel: 50W
Integration time constant for charge measurement tint=170ns
Low threshold for fast timing: trigger validation by means of threshold on the charge level
Charge dynamic range: about 2500 p.e. (with SiPM gain 106)
“Slow” path overall gain: about 1.2mV/p.e.
Total current consumption of the analog channel 2.4 mA
64 multiplexed channels, fast-OR of the trigger output of the channels for time measurement
ADC for charge measurements with 10bit resolution
Conversion rate for events involving all the 64 channels (serial read-out): 75kHz
100MHz LVDS communication link for charge and address data
Front-end ASIC for the SiPM: main features and specs

## Slide 23
Schematic of the ASIC at top level
Design finished at schematic level
Layout of the blocks under verification (Layout Vs Schematic and post-layout simulation)
Provisional floorplan done with the 64 channels, the ADC and the digital part placed
Top level routing and final verifications to be done
Chip size: about 10mmx5mm
Possible placement of two abutted dies in a single package to have an ASIC for 128 channels
Front-end ASIC for the SiPM: status
Provisional floorplan

## Slide 24: Overall DAQ scheme
G. Sportelli, E. Zaccaro, E. Kostara
Uni and INFN Pisa
Objectives
  Provide full in –beam (full-beam ) PET system able to sustain annihilation and prompt photon rates during beam irradiation
  30 kHz/cm^2 maximum sustainable single rate
  Each 5x5 module will provide data at a rate of 720 kHz
Data packet 10 B
Expected module output bandwidth 7.2 MB/s
R. Wheadon
INFN Torino
FE
FE
FE
FE
FE
FE
FE
FE
FE
Front end board

## Slide 25
Torino electronics hardware status (FE and Tx FPGA) 23/4/2015
FE board design (Tofpet ASIC), construction and test of first prototype boards complete
Firmware and software for ML605 (2 FE boards) and SP605 (1 FE board) allow ASIC calibration and data acquisition (up to ~ 83MByte/s) via custom Gbit Ethernet link
Basic Rx firmware for Gbit Ethernet communication delivered to Pisa
Probe station testing of ASIC’s underway
FE boards and dedicated FMC adapters production underway
SP605 (Tx FPGA boards) procuration underway
Remaining work:
FE board production and calibration
Tx/Rx data transmission firmware
PET detector panel construction
R. Wheadon INFN Torino

## Slide 26: Motherboard
Hosts all the RX boards in a 3U rack
Collects and filters all detected photons
Processes coincidences in real time
Sends coincidence data to the host PC via USB 2.0
HW complete, FW/SW under development

## Slide 27: RX Board
280 mm
100 mm
Gb Ethernet
mezzanine
Cat 7
clock
cables
Cat7 cable
cheapest, lowest bandwidth
expensive, high bandwidth
MB
Connection

## Slide 28: RX HW development status today
Functional design ✔
Schematic design ✔
Mechanical design ✔
PCB design
  Functional design ✔
  IC and connectors placement ✔
  Negotiation ✔
  External company kick-start ✔
Construction and assembly ✖
Expected delivery 7/2015
Most recent results are marked in blue

## Slide 29: Current work
SoCKit board
  Finish time constraining of ethernet connection ✔
  Develop a HW/SW test framework ✖
Motherboard
  Finish hardware tests (mainly LVDS channels) ✖
  Develop clock management boot-strap ✖
  Re-implement control firmware from DoPET ✖
  Test coincidence sorting ✔
  Develop coincidence filtering ✔
RX board
  Construct and test the prototype ✖
  Develop complete firmware ✖
Most recent results are marked in blue

## Slide 30: Dose Profiler
6 XY planes with 2 cm spacing. Each plane made of 2 stereo layers of 192 0.5x0.5 mm2 square scintillating fibers
2x0.5 mm squared fibers read out by Hamamatsu 1mm2 SiPM : S12571-050P
32 SiPM feed a 32 ch ASIC BASIC32
4x4 LYSO pixellated crystals tracking planes: 50 x 50 x 16 mm3
Plastic absorber 1.5 cm thick in front of LYSO to screen electrons
Crystals read out by 64 ch Hamamatsu MultiAnode
V. Patera, Uni La Sapienza, Roma
not to scale
2 cm
19, 2 cm
19,2 cm
p
γ
γ ’
e-
Eγ ~ 1-10 MeV
Ekin ~ 30-130 MeV

## Slide 31: Dose Profiler: components

## Slide 32: Front-end board
The first prototype has been produced
192 SiPM, 6 BASIC32
Check of the board functionality: Raspberry Pi + test board, led driver
BASIC32
TEST SETUP
TEST BOARD
MASK
RASPBERRY
OPTICAL FIBER
SiPM
Adalberto Sciubba, Giacomo Traini,
Marco ToppinUni La Sapienza and INFN RM1

## Slide 33: Check of the front-end board functionality
Internal configuration of all BASIC properly performed
External trigger mode acquiring checked
Channel address and charge properly read-out
Internal trigger acquiring mode ok except for 2 SiPM
Led Light
Pedestal
STARTING PRODUCTION OF 18
FRONT-END BOARDS

## Slide 34: Next steps
Test of 150 BASIC32 with a dedicated SETUP
(in progress)
Design of FPGA prototype (in progress)
FPGA test
Marco Top

## Slide 35
INSIDE PET simulation status
Beam simulation
About 1/100 of primary hadrons
Beam time structure simulated
Time-tagged
activity scoring
Annihilation time and position
Isotopes production map
PET simulation
All the positrons are simulated.
Detector simulation.
Dose Delivery System Log Files
Analysis of Dose Delivery System (DDS) Log files:
Protons per spot
Spill time structure
FLUKA-based two steps simulation: first the treatment beam is simulated with partial statistics, then, starting from the isotopes production map, the full-statistics PET simulation of the INSIDE detectors is performed. Simulation time decreases of about 70x with respect to a conventional approach.
Validation will be performed with the beam test of 3 May 2015 at CNAO.
x-y
x-z
y-z
Example of simulated data with the geometry of the beam test at CNAO: comparison between the INSIDE simulated PET image and the simulation input activity profile analysis.
beam
beam
beam
P. Cerello, E. Forina, F. Pennazio
Uni and INFN Torino

## Slide 36
INSIDE PET sofware status
-Online monitoring and analysis or offline analysis
Automated energy window selection channel by channel
Automated time delay calibration
TOT raw [ns]
chip 7, channel 40
Data acquired at CNR Pisa with 18F-FDG planar source and INSIDE geometry of beam test at CNAO
Coincidence Time Resolution (CTR) = 425 ps
preliminary
INSIDE GUI

## Slide 37: Simulation of the performance of INSIDE Dose Profiler
What is the expected resolution in the estimation of range in the patient using charged particles (mainly protons) emitted from the target?
What is the expected performance with prompt photons?
Simulation studies using a tissue-equivalent phantom (size approximating a human head)
G. Battistoni, S. Muraro
INFN Milano

## Slide 38
Lattice Copies
Base Cell
Lattice Geometry: Optical Fiber & LYSO Crystals
Base Cell
LATTICE COPIES
Pixelated LYSO crystal, 23x23
active pixels surrounded by BaSo4
(Barium Sulfate) inactive gap.
In total 4232 pixels implemented.

## Slide 39
FLUKA simulation:
Secondary protons fluence
from C 220 MeV
into a “head-like PMMA phantom”
at 900 with respect to the beam axis
12C beam

## Slide 40
Protons
Event display:
Tracks and energy depositions
in fiber and LYSO cristal
Gamma event (Compton)
Notes: Plot dei protoni:
la linea tratteggiata e’ il protone primario.
I cerchi rossi(blu) sono i depositi X(Y) nelle fibre. Analogo codice di colore e’ usato per i piani di fibre il cui spessore e’ esagerato volutamente per motivi grafici.
Le linee continue sono il risultato dei fit al chi2 e kalman.
Le linee tratteggiate rosse sono le particelle (elettroni) che vengono dalla ionizzazione del protone.
Plot dei gamma:
Il blu e’ il fotone scattrato.

## Slide 41
The INSIDE collaboration: PI Alberto Del Guerra (University of Pisa)
University of Roma La Sapienza and INFN Roma 1
Riccardo Faccini
Cristina Morone
Vincenzo Patera
Luca Piersanti
Alessio Sarti
Adalberto Sciubba
THANKS
INFN (Milano, LNS, LNF)
Giuseppe Battistoni (Milano)
Matteo Cecchetti (Milano)
Giuseppe A. P. Cirrone (LNS)
Giacomo Cuttone (LNS)
Pablo Cirrone (LNS)
Erika De Lucia (LNF)
Fabrizio Cappucci (Milano)
Francesco Romano (LNS)
Paola Sala (Milano)
Politecnico Bari and INFN Bari
Fabio Ciciriello
Francesco Corsi
Francesco Licciulli
Cristoforo Marzocca
Gianvito Matarrese
University of Pisa and INFN Pisa
Nicola Belcari
Maria Giuseppina Bisogni
Niccolo’ Camarlinghi
Stefano Ferretti
Eleftheria Kostara
Aafke Kraan
Ben Liu
Nahema Marino
Matteo Morrocchi
Maria Antonietta Piliero
Giovanni Pirrone
Valeria Rosso
Giancarlo Sportelli
University of Torino and INFN Torino
Piergiorgio Cerello
Silvia Coli
Elisa Fiorina
Giuseppe Giraudo
Francesco Pennazio
Cristiana Peroni
Angelo Rivetti
Richard Wheadon

## Slide 42
Back up