## Slide 1: Beam-Beam Simulations to Optimize DAFNE e- Working Point
D.Shatilov (BINP), M.Zobov, C.Milardi (INFN/LNF), A.Valishev (FNAL)
April 23, 2015

## Slide 2: Motivation
Collider performance is affected by interplay of beam-beam and machine optics features
  Nonlinearities
  Coupling (including IR with solenoidal field)
  Chromaticity
  Imperfections
Our goal was to implement the complete model of DAFNE in weak-strong beam-beam simulation in order to guide parameter optimization

## Slide 3: Model Development
In 2013-2014, Lifetrac functionality was expanded to include the full treatment of machine lattice
  Tracking through arcs is performed element-by element
  Lattice is imported directly from MAD-X model
  All main magnets + multipoles, solenoids, fringe fields, orbit
  Main IP inside of a solenoid
We compare the full treatment of machine with previously used approach (arcs=linear maps)
Analysis tools – FMA, DA, Specific Luminosity and Beam Lifetime

## Slide 4: e+ Working Point Scan
e+ DQx=0.0980; Qx=0.1305
Luminosity Inverse beam sizes

## Slide 5: Electron Ring Dynamical Aperture
As=1
As=5
As=9

## Slide 6: e- Tune Scan
Luminosity Inverse beam sizes
Linear model
Nonlinear model
(0.088, 0.152)
(0.130, 0.170)

## Slide 7
BB Off BB On BB Off BB On
FMA for As = 2 sigma
(0.088, 0.152)
(0.130, 0.170)
Lp = 7.261013
Lp = 7.471013

## Slide 8: Summary
The simulated e- Dynamical Aperture is similar to that simulated and measured in previous KLOE run.
The simulation using complete machine model indicates that the present e+ working point is optimal.
For the e- ring, we suggest to move the working point to higher tunes:
  Moderate increase in luminosity is possible (up to 5%)
  More importantly, the DA will increase, which will result in better beam lifetime, injection efficiency, and background.