## Slide 1: Jennifer Activities: WP2
B factories
- results and motivation for upgrade
SuperKEB
- how to reach 40x more luminosity
Belle II
- upgrade of the Belle detector to cope with 40x more luminosity
Jennifer WP2: tasks and deliverables
Tracking
Particle ID (Alessandro Gaz)
Forward electromagnetic calorimeter (Claudia Cecchi)
Luminosity monitors (Cecile Rimbaud)
Organisation/Schedule

## Slide 2: B-factory Detectors – a huge success!
Measurements of CKM matrix elements and angles of the unitarity triangle
Observation of direct CP violation in B decays
Measurements of rare decays (e.g., Btn, Dtn)
bs transitions: probe for new sources of CPV and constraints from the bsg branching fraction
Forward-backward asymmetry (AFB) in bsll has become a powerfull tool to search for physics beyond SM.
Observation of D mixing
Searches for rare t decays
Observation of new hadrons
B0 tag
_
B0 tag

## Slide 3: Motivation for Upgrade
Measure CKM elements as precisely as possible
Overconstrain unitarity triangle
Look for deviations from SM
=> Need about 50 ab-1
F1/b = (21.±1 0.9)o
F2/a = (88.4 ±5.6)o
F3/g = (70 ±29)o
Babar/Belle
With 50 ab-1 (same central values)

## Slide 4
e- 2.6 A
e+ 3.6 A
To get x40 higher luminosity
Colliding bunches
e+ Damping ring
New beam pipes
& bellows
Replace beam pipes to suppress electron cloud (TiN-coated beam pipe with antechambers)
Redesign the lattice to squeeze the emittance (replace short dipoles with longer ones, increase wiggler cycles)
Reinforce RF systems for higher beam currents
New positron capture section
New superconducting final focusing magnets near the IP
Low emittance electron gun
KEKB to SuperKEKB
Improve beam monitors and control system

## Slide 5: Luminosity Upgrade

## Slide 6: Requirements for the Belle II detector
- gb reduced by a factor of 2: compensated by improved vertexing
radiation damage and occupancy
fake hits and pile-up noise in the EM Calorimeter
- higher rate trigger, DAQ and computing
Critical issues at L= 8 x 1035/cm2/sec
4 Higher background ( 10-20)
4 Higher event rate ( 10)
4 Special features required
Result: significant upgrade

## Slide 7: Belle II
Time-of-Flight, Aerogel
Cherenkov Counter →
Time-of-Propagation counter
(barrel),
prox. focusing Aerogel RICH
(forward)
7.4 m
RPC µ & KL counter:
scintillator + Si-PM
for end-caps
8.0 m
CsI(Tl) EM calorimeter:
waveform sampling
electronics, pure CsI
for end-caps
4 layers DS Si Vertex
Detector →
2 layers PXD (DEPFET),
4 layers DSSD
Central Drift Chamber:
smaller cell size,
long lever arm

## Slide 8
CDC
Smaller Cell size (1-20mm => 6-9 mm) all 51456 wires strung by last summer

## Slide 9
Significant improvement in z-vertex resolution
PXD: 2 layer Si pixel detector (DEPFET technology) (R = 1.4, 2.2 cm)
monolithic sensor
thickness 75 µm (!),
pixel size 50 x 55 µm² to 50 x 85µm² (depending on layer and z)
SVD: 4 layer Si strip detector (DSSD) (R = 3.8, 8.0, 11.5, 14.0 cm)
15mm
30mm
Belle
Belle II
pbsin(q) [GeV/c]
0.4
2.0
0
0.8
1.2
1.6
100
20
50
σ [µm]
PXD
PXD+SVD
Silicon Tracking System @ Belle II

## Slide 10
SVD
4 layers of double sided silicon detectors
P-strips 50 – 75 µm pitch
N-strips: 240 µm pitch
Backside side readout signal routed to frontside
by a flex circuit
Low material budget (0.58% X0 /Layer)
Readout chip: APV (originally for CMS)
Very fast readout to cope with occupancy

## Slide 11: DEPFET
Each pixel is a p-channel FET on a completely depleted bulk
Signal electrons accumulate in the internal gate and modulate the transistor current (gq ~ 400 pA/e-)
Fully depleted: large signal, fast signal collection
Low capacitance, internal amplification: => low noise
Rolling shutter mode (column parallel): 20 µs frame readout time
Sensitive area thinned to 75 µm with a rigid support frame (all silicon module)
Low power consumption within sensitive area (air cooling)
Low material to reduce multiple scattering (0.21% X0)

## Slide 12: WP2 Tasks and Deliverables
WP2 - Belle-II detector construction and test [Months: 1-48]
Task 2.1: Forward Electromagnetic Calorimeter [INFN, KEK]
Task 2.2: Tracking detectors [DESY, HEPHY, INFN, METU, IFJ, UKP, KEK]
Task 2.3: Particle Identification [INFN, JSI, KEK]
Task 2.4: Luminosity monitor [CNRS, KEK]
Number Deliverable Lead beneficiary Due Date (in months)
D2.1 FW ECL TDR 1 INFN (10) Jan 2016
D2.2 Commissioning Report FW ECL INFN (48) Mar 2019
D2.3 CDC commissioning METU (14) May 2016
D2.4 PXD White-book 2 DESY (20) Nov 2016
D2.5 SVD+PXD full commissioning DESY (30) Sep 2017
D2.6 TOP commissioning INFN (36) Mar 2018
D2.7 ARICH JSI (26) May 2017
D2.8 Diamond sensor CNRS (36) Mar 2018
WP2: 227 months of secondments (~20 FTE)

## Slide 13: Task 2.2 Tracking Detectors
Task 2.2 Tracking Detectors
Full CDC commissioning: (14) May 2016
Cosmic ray test of CDC modules in the Belle II area (6) Sep 2015
Installation of CDC chambers in Belle II (10) Feb 2106
CDC cosmic ray test inside Belle II, with and without magnetic field (12) Mar 2916
PXD Whitebook, “PXD technology, procedure and operation” (20) Nov 2016
Full integration and commissioning of SVD+PXD inside Belle II detector: (30) Sep 2017
First data with 1 VXD (4 SVD+ 2 PXD) Sector (14) May 2016
First cosmic data with SVD+PXD (16) Jul 2016
First beam data with SVD+PXD and all other Belle II sub-detectors (20) Nov 2016
A 4-layer DSSD Vertex Detector integrated in the Belle II tracking system (24) Mar 2017
Environmental monitoring for SVD and Belle II radiation protection system (24) Mar 2017
Jennifer Institutes:
HEPHY (Austria), INFN (Italy), METU (Turkey), IFJ (Poland), UKP (Czech), DESY [DESY, Uni Bonn, Uni Giessen, Uni Heidelberg, MPI] (Germany)
135 months of secondments for 2.2

## Slide 14: Beast II
Main purpose of Beast II:
Beam conditioning to start collisions
Background measurements and mitigation
Belle II commissioning with partial VXD sensors
Optimization of interlock system
Installation of
2 PXD & 4 SVD layers
(& other specific sensors for background determination)
Beast II: May – December 2017
Subtask 2.2.1: First data with 1 VXD (4 SVD+ 2 PXD) Sector

## Slide 15: SuperKEKB Cchedule
To budget problems up to 1 year delay (especially VXD installation and physics)

## Slide 16: Implications for Jennifer
Schedule changes:
CDC cosmic ray tests (Jennifer Sept. 2015) => May 2016?
CDC installation (Jennifer: January 2016) => August 2016
CDC cosmic ray tests in Belle II (Jennifer: March 2016) => December 2016
CDC fully commissioning (Jennifer May 2016) => March 2017 ?
VXD sector test (Beast II) (Jennifer: May 2016) => May 2017 ?
Full VXD cosmic test (Jennifer: July 2016) => 2nd half of 2017 ?
1st beam with VXD in Belle II (Jennifer: November 2017) => October 2018
For other tasks (PID, ECL, lumi): see next talks

## Slide 17: Conclusions
Belle II will be a key player in flavour physics and CP violation
Very challenging upgrade program of the detector
Jennifer supports essential parts of the detector upgrade program
227 months of secondments (20 FTE !)
Due to the latest schedule changes of superKEKB/Belle II some adaptations of the Jennifer deliverables (dates) are needed (mostly tracking detectors)