## Slide 1
Novel acceleration techniques
Massimo Ferrario
INFN-LNF
LNL Seminar –Legnaro, June 11, 2015

## Slide 2
Globatron: 5000 TeV, 170 B$, fixed target 3 TeV cm

## Slide 3
ADA: (Anello Di Accumulazione), 1961-1964
the first e+e- Collider

## Slide 5
“The Universe in a Nutshell”, by Stephen William Hawking, Bantam, 2001
Without further novel technology, we will eventually need an accelerator as large as Hawking expected.
Hawking: the Solartron

## Slide 6
Accelerator on a Chip?

## Slide 7
Miniaturization of the accelerating structures (resonant)
Wake Field Acceleration (transient)(LWFA,PWFA,DWFA)
2 WAYS NTA ROAD MAP
Power sources
Accelerating structures
High quality beams

## Slide 8
  Modern accelerators require high quality beams: ==> High Luminosity & High Brightness
  ==> High Energy & Low Energy Spread
  Small spot size => low emittance
  N of particles per pulse => 109
  High rep. rate fr=> bunch trains
  Little spread in transverse momentum and angle => low emittance
  Short pulse (ps to fs)

## Slide 10
Conventional RF accelerating structures

## Slide 12
High field ->Short wavelength->ultra-short bunches-> low charge

## Slide 13
Miniaturization of the accelerating structures

## Slide 18: Dielectric Photonic Structure
Why photonic structures?
  Natural in dielectric
  Advantages of burgeoning field
    design possibilities
    Fabrication
Dynamics concerns
External coupling schemes
Biharmonic ~2D structure
e-beam
Laser pulses
180 degrees
out of phase
Schematic of GALAXIE
monolithic photonic DLA

## Slide 19: Laser-Structure Coupling: TW
GALAXIE Dual laser drive structure, large reservoir of power recycles
e-beam
Laser pulses
(180 degrees
out of phase)

## Slide 20: 5th Gen Light Source: A Table-top X-ray FEL
All EM system with GV/m fields
<2 m EM undulator
(l=100 um)
<2 m 800 MeV Dielectric
Laser Accelerator (DLA)
Ultra-high brightness
electron source
Long wavelength
(5 um) laser source
GALAXIE: GV-per-meter AcceLerator And X-ray-source Integrated Experiment
Many interconnected physics challenges
40 keV quantum
SASE FEL
LCLS photons in <1m

## Slide 23
Wake Field Acceleration 1
Laser Driven
LWFA

## Slide 24
High quality beam Plasma Acceleration
Breakdown limit?

## Slide 25
Laser beam
Electron beam
1 mm
Direct production of e-beam

## Slide 40
Protons and Ions?

## Slide 42
Wake Field Acceleration 2
Beam Driven
PWFA

## Slide 44
Blumenfeld, I. et al. Energy doubling of 42 GeV electrons in a metre-scale plasma wakefield accelerator. Nature 445, 741–744 (2007).
Litos, M. et al. High-efficiency acceleration of an electron beamin a plasma wakefield accelerator. Nature 515, 92–95 (2014).

## Slide 45: Positrons and Hollow Channel Plasma
Laser Profile for J5 Bessel Focus
The physics of accelerating positrons in a plasma is different than that of electrons!
Hollow channel plasmas might be a viable method for accelerating positrons in a plasma.
A special optic called a kinoform is used to create a hollow channel plasma.
Positrons plasma acceleration is a crucial step towards a plasma based linear collider. FACET hosts the only active research on positron PWFA.
200 μm

## Slide 48
ILC – International Linear Collider

## Slide 53
High Gradient – Low e- Beam Quality
High e+e- Beam Quality – Low Gradient
High e+e- Beam Quality - High Gradient
3 Steps towards a reliable PWA

## Slide 54
PWFA
THz Source
FEL
(2colors)
EOS
Thomson X-ray
FLAME
LWFA
SPARC_LAB
Sources for Plasma Accelerators and Radiation Compton with Lasers And Beams

## Slide 55
Ti:Sa FLAME laser
Stretcher
Amplifiers
Compressor
LWFA
Electron Self Injection
And
Protons

## Slide 56
S-band Gun
Velocity Bunching
Long Solenoids
Diagnostic and Matching
Seeding
150 MeV S-band linac
12 m
Undulators
u = 2.8 cm
Kmax = 2.2
r = 500 nm
15 m
Spectrometer
Linac and FEL

## Slide 57
HB photo- injector with Velocity Bunching

## Slide 58
Free Electron Laser

## Slide 59
Thomson back-scattering source

## Slide 61
Beam Driven Plasma Wake Field Acceleration
(COMB exp.)
Notes: 61

## Slide 62
Litos, M. et al. High-efficiency acceleration of an electron beamin a plasma wakefield accelerator. Nature 515, 92–95 (2014).
4-pulses-time-structure
time
orizontal dim
In progress at SPARC_LAB

## Slide 63
Laser Comb technique:
generation of a train of short bunches
    - P.O.Shea et al., Proc. of 2001 IEEE PAC, Chicago, USA (2001) p.704. (Low charge regime only)
    - M. Ferrario, et al., Int. J. of Mod. Phys. B, 2006 (High charge, Beam Echo)
Notes: 63

## Slide 64
COMB electron beam manipulation

## Slide 65
Diagnostics Tools

## Slide 66: Four bunches: long. phase space rotation
Gun energy 5.1MeV
Charge
40pC/80pC/50pC/30pC
Bunch length on crest 2126.3 (8.7) fs
Min. bunch length
168.2 (8.7) fs
Gun ext. phase
35 deg
Energy 168-109 MeV
Energy Spread <0.8%
Measurements with 200pC

## Slide 67: Three bunches: witness position tuning
+ 1.67 ps
Reference
- 1.67 ps

## Slide 68
Sezione Banda C
Gruppo Pompe Vuoto
Permanent magnet actuator
YAG/OTR/EOS crystal actuator
Camera interazione e
Sistemi ancillari di pompaggio e iniezione gas
YAG/OTR actuator
PWFA interaction chamber

## Slide 69
Status of the COMB experiment
Vacuum chamber has been designed, ordered and already delivered. First vacuum tests (with capillary, using He and Ar) have been performed.

## Slide 70
Status of the COMB experiment
Capillary has been designed and for the moment 3D printer has been used to built it.
However, for the “real” run on the SPARC linac, only the holder will be 3D printed.
Different materials and shapes are overseen to be used, as for example glass, Macor and Sapphire.

## Slide 71
Laser Driven Plasma Wake Field Acceleration
(EXIN exp.)
Notes: 71

## Slide 73
ExIn interaction chamber
Laser pulse
e-bunch
Moving mirror with hole
Focusing parabola
Laser extraction (to diagnostics)
Laser pre-injection diagnostics
Target area
The interaction chamber is in advanced acquisition and testing stage.
Installation is scheduled within the current year.

## Slide 74: Hexapod for the positioning of the capillary
The H-824 is available in vacuum compatible version.
Six Degrees of Freedom (XYZ, Pitch, Roll, Yaw)
Vacuum Compatible Versions
Load Capacity 10 kg
Travel Ranges to 45 mm (linear), 25° (rotation)
7 Nanometer Resolution
300 Nanometer Min. Incremental Motion
Repeatability ±0.5 Micron
Very Compact Design
Self Locking to 10 kg
The hexapod is under test, in the FLAME laboratory, to characterize the features of precision in the positioning of the system

## Slide 75: Synchronization System upgrade
SPARC HALL
FLAME AREA
PC laser
Oscillator
79.33MHz
OMO
79.33MHz
FLAME oscillator
79.33MHz
RF reference
2856MHz
Optical reference
  RF reference will be substituted by fiber optical oscillator
  Fiber laser OMO (Optical Master Oscillator) installed and tested
  Systems locked through high resolution optical phase monitors (cross-correlators in house and ready to be tested)
  Fiber link stabilization is ongoing (order placed) to distribute the reference signal
  FLAME laser VS electrons estimated time jitter <50fsRMS

## Slide 76
Conclusions

## Slide 78
Thank
you

## Slide 79
Vorpal simulation: full length of capillary, case 1
Following the previous steps, the “good” simulations over a full length of a capillary. That is, the plasma is simulated to have a density ramp up, 8 mm uniform density length, and then a mirrored density down ramp.
Two cases examined based on the previous results. In the first one the beam is matched for a 1.5 mm gaussian density ramp. Results of this case are shown in this slide. Beam parameters are: 600 pC, 4 mm-mrad normalized emittance, 30 micron rms length, 2 mm waist beta (with no plasma), 110 MeV
Courtesy J. Rosenzweig and S. Barber

## Slide 80
Full VORPAL simulations with witness beam, 12 pC, 3 um sz
A 12 pC, 3 micron rms length beam propagates in the plasma, gaining 30 MeV in 8 mm of uniform density plasma (3.75 GeV/m). Emittance grows from ~ 1mm-mrad to 1.5 mm-mrad. RMS energy increases to ~ 4 percent. Note, the beam can be loaded further back in the wake to create larger energy gain.
More charge to flatten wake (watch out for noise).

## Slide 81
Vorpal simulations with witness beam, 60 pC, 6 um sz
A 60 pC, 6 um rms length beam propagates in the plasma wake, gaining 45 MeV in 8 mm of uniform density plasma (5.6 GeV/m). Emittance grows from ~ 1mm-mrad to 1.6 mm-mrad. RMS energy increases to ~ 4 percent. This beam is loaded slightly further back in the wake compared to the previous example, hence the larger energy gain
Witness beam is strongly mismatched, but causes not major problem.

## Slide 82
CPA Ti:Sapphire + harm. gen.
PBS
HWP
αBBOs
Motorized stage
PBS
half drivers energy
to the photocathode
Energy partition
Variable delay witness
Periodic multibunch drivers
HWP
Drivers and witness bunches generation
Courtesy F. Villa

## Slide 83: Comb beam manipulation
Inj. phase
Bunch spacing
Train length
Accelerating field
(inj. phase)
Energy separation
TW focusing field (~300G)
Emittance
Bunches current, length and their max compression phase
Gun focusing field (~3kG)
Emittance
Bunches current, length
Gun inj. phase and space charge
Bunches distance at the linac entrance
Energy spread
Accelerating field
(inj. phase)
Energy spread sub-bunch

## Slide 84
Laser Plasma Acceleration Workshop, May 11th 2015
Simulation settings
Lacc = 3 cm
L2 = 4 cm
L1 = 2 cm
We assume linear tapering for sake of simplicity. The incoming bunch is an ideal one with bi-Gaussian profiles, 17 fs long (FWHM), 5.5 μm wide (rms), 10 pC charge and 1 μm normalized emittance.
Andrea R. Rossi
L1
Lacc
L2
θin
θout
Capillary tips shaping can be a way to modulate both laser convergence (divergence) and plasma ramping.
Matching strategies for external injection

## Slide 85
Simulation results: matching and focusing/defocusing
Efinal=300 MeV
ΔE/E = 0.9%
εn≈ 1.1μm
σtr ≈ 5.5 μm (in/out)
A very nice matching is obtained by laser focusing method.
Beam size is reduced to matched size and then increased back to initial value in a quasi-adiabatic transformation.
Both initial and final sizes seems to be within manageability of permanent magnet quads.
Andrea R. Rossi
Energy gain is in excess of 200 MeV in a 3 cm acceleration length, which means an average electric field in excess of
7 GV/m
Energy spread is within 1% (a safe threshold for subsequent transport*) and REDUCED IN THE FINAL RAMP due to beam loading and plasma wavelength increase.
* P. Antici et al., J. App. Phys. 112, 044902 (2012).
Matching strategies for external injection
Laser Plasma Acceleration Workshop, May 11th 2015

## Slide 86: Dielectric Wakefield Accelerator
Electron bunch ( ≈ 1) drives wake in cylindrical dielectric structure
  Dependent on structure properties
  Generally multi-mode excitation
Wakefields accelerate trailing bunch
Mode wavelengths (quasi-optical
Peak decelerating field
Design Parameters
Ez on-axis, OOPIC
*
Extremely good
beam needed
Transformer ratio (unshaped beam)