## Slide 1: FTK IAPP Executive Board Meeting: 29/05/2015
Calliope-Louisa Sotiropoulou
WP5: A new approach to Image Processing

## Slide 2: A New Approach to Image Processing
WP5: Image Processing Impact of IAPP outside HEP community

## Slide 3: A New Approach to Image Processing
The FTK Processor is a very fast, powerful and efficient pattern matching machine
The particle tracking problem is in fact an image processing problem
HEP
Before Filtering
After Filtering

## Slide 4: A New Approach to Image Processing
The concept (of WP5) is to…
Use existing resources and ideas (e.g. the AMchip, AMboards) for image processing and pattern matching for different application fields
A great number of interdisciplinary applications – not limited to image processing - is available: biomedical imaging (e.g. MRI), cognitive imaging (Del Viva’s algorithm1), security (real time face recognition, personnel tracking), DNA analysis, smart cameras, data mining (e.g. data servers, search engines) etc.
1M. Del Viva, G. Punzi, and D. Benedetti. Information and Perception of Meaningful Patterns. PloSone 8.7 (2013): e69154.

## Slide 5: FTK for Image Filtering
Image Filtering  Finding Contours is the way human brain operates: New approach for image processing hardware
Major difference between HEP and Human Brain:
  For HEP we are aware a-priori of the relevant patterns
  The Human Brain is trained in real time (we are not aware of the patterns beforehand and we always adjust to new environments)
Target: Design and prototype a pattern matching machine that executes both training and filtering in real time using high performance embedded systems (FPGAs, ASICs and combination of the two - SiP / System In Package)

## Slide 6: FTK for Image Filtering
Build small arrays of pixels (3x3 for static images or 3x3x3 for movies – 3rd dimension for time) that are AM patterns (M. Del. Viva, G. Punzi)
B/W 29=512 patterns: 101-010-100, ……. , 111-011-001
4 gray level 218= 256 Kpatterns: 00,00,01-00,01,00-11,00,10 …..
B/W + time 227= 128 Mpatterns: 111,000,000 - 000,111,000 - 000,000,000
Training: Calculate the frequency of each pattern in the sample images/frames
Compute Probability Density Histograms (PDHs) for different training image sets
Select the relevant patterns to be put in the AM bank
Running stage: Send the patterns to the AM chip to be filtered

## Slide 7: FTK for Image Filtering
Choice of relative patterns: Choose the pattern set that maximizes entropy H under real constraints
Unbounded entropy
Entropy yield per unit cost and for each pattern:
Where p is the probability that a given portion of the input data matches a specific pattern, N is the maximum number of storable patterns and W is the maximum allowed total rate of pattern acceptance.

## Slide 8: FTK for Image Filtering

## Slide 9: Entropy Calculation for “relevant patterns”
16 Relevant
Patterns used
Probability distribution of the Ntot = 2^9 possible 3x3 square pixel matrices in black/white for natural images
50 Relevant
Patterns
used

## Slide 10: Current Plans 1: Use of AMchip 05 Test system
A Virtex-6 LX240T Development board with a system implemented to test the AMchip
Functions that exist:
  Pattern loading
  Pattern comparison
  Ethernet connection
  IPbus controls
  GTX transceivers etc.

## Slide 11: Image Processing Hardware
Traning:
performed by
FPGA
+
Ex. Memory
Pattern
Filtering:
performed by
AM
Chip

## Slide 12: Current Plans 1: Use of AMchip 05 Test system

## Slide 13: Current Plans 1: Use of AMchip 05 Test system
Adapt the existing system to load images and execute the training phase
  Identify all existing patterns, generate Probability Density Histograms
  Identify useful patterns
Adapt the existing system to execute pattern matching
  Load the useful patterns to the AMchip
  Execute pattern matching for various input images
  Extract contours or/and execute a post processing step (e.g. clustering)

## Slide 14: Current Plans 1: Training Phase – Calculate the frequency of each possible pattern
i. e. pattern = 11,11,11-11,11,11, 01,11,11
Each pattern = its own address
4 Gray levels 218= 256 Kpatterns (B/W movement: 227= 128 Mpatterns)
Pattern = ADDRESS
32 b × 256 k
= 500 kB
(movement
32 b ×128 M
= 500MB)
Ext Memory
2 GB
FREQUENCY = FREQ(pattern)
Each Location contains the updated frequency of a pattern. When a pattern is identified the specific pattern address is read, contents are increased by one (+1), and written back in the same location - ACCUMULATION
18 (or 27) bits
16 bits

## Slide 15: Current Plans 1: Training Phase – Updating Frequencies
Patterns that are efficient carriers of information
given the bandwidth (W) & memory limits (N)
Log(p)
W/N<p
W/N>p
f(p) = -Wlog (p)
f(p) = -pNlog (p)
DSP
pi
RAM
-log(pi)
-Wlog (p) if p>W/N
-pNlog(p) if p<W/N
Compare
To THR
Yes
Or
No
N of appearance (pattern)

## Slide 16: Current Plans 1: Running Phase – Filtering Patterns
Running Phase
Bus_layer0 Bus_layer1 Bus_layer2 …….. Bus_layer7
layer0
layer1
layer2
layer7
pattern0
pattern1
pattern2
pattern3
layer0
layer1
layer2
layer7
Patt0 Patt1 Patt2 Patt7
………
4 gray levels
GOOD for AM05 used with threshold 1 – same pattern written 8 times in the 8 columns
Each comparison we (1) compare 8 patterns (2) read for each match the bitmap (3) give INIT

## Slide 17: Future Plans: Use of an Ultrascale evaluation board and System on Chip (SiP) systems
More resources available on the FPGA device  New technology, new design approaches, greater challenges (Ultrascale)
Merge the devices on a single chip (SiP)
Targeting the development of a portable and flexible hardware accelerator (possibly with a PCI type interface) to be easily interconnected with a PC

## Slide 18: Status
Block diagram for Training phase almost complete
Work divided in two parts between P. Luciano and myself
Project and code development started
Lots of exciting work ahead of us…

## Slide 19
Thank you…