## Slide 1
Notes: Slide 1: Company Logo Full Page
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View

## Slide 2
Photon Pulse Characterization at FERMI Free Electron Laser
Marco Zangrando
On behalf of the FERMI team

## Slide 3
OUTLINE of the talk
Brightness: synchrotrons vs. FELs
FERMI FEL: layout, basic principles, and operational results
Photon Beam Transport System (PADReS): GAS-BASED DIAGNOSTICS, PRESTO, AC/DC, Coherence, WFS
Pulse length measurements: cross-correlation, SPIDER
Polarization (measurement and control)
Conclusions
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 4
BRIGHTNESS Different lightsources
Storage Rings
FELs
1010
106
FERMI
FEL-1 & 2
10 orders
of
magnitude
Courtesy of Luca Giannessi
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 5
X-RAYS Smaller and shorter
Unique new opportunities thanks to the distinct properties of FEL light:
(i) High peak power, (ii) Ultrashort and (iii) Coherent pulses
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 6
FEL USER FACILITIES Existing and in construction
LCLS
FERMI
FLASH
SACLA
LCLS II
X-FEL
PSI
PAL
DALIAN
SDUV FEL
Existing
FEL user
facilities
… in construction
Lasing expected between 2016-2018
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 7
ELETTRA The lightsources
 200 m
Linac Tunnel +
Injector Extension
Sponsored by: Italian Minister of University and Research (MIUR), Regione Auton. Friuli Venezia Giulia, European Investment Bank (EIB), European Research Council (ERC), European Commission (EC)
 100 m
Undulator Hall
 60 m
Experim. Hall
ELETTRA Synchrotron Light Source:
up to 2.4 GeV – TOP-UP mode
~800 proposals from 40 countries every year
FERMI FEL-1 & FEL-2 Free Electron Laser
100nm to 4 nm
High Gain Harmonic Generation FEL (HGHG)
~70 proposals from first two calls for experiments in 2012/2013
~50 proposals in the 3rd call (2014)
~75 proposals in the 4th call (2015)
Courtesy of Enrico Allaria

## Slide 8
FERMI Machine layout
Elastic and Inelastic Scattering
FEL1
FEL2
I/O Monitors & Gas Cells
EIS
DIPROI
LDM
Slits
Experimental Hall
Spectrometer
Switching Mirror
60m
Diffraction and Projection Imaging
Low
Density
Matter
Gun
Laser-heater
L0
L3
L2
BC1
BC2
L4
L1
Diagnostic
Beam Dump
100 MeV
300 MeV
800 MeV
1.5 GeV
200m
Linac Tunnel
1.2 GeV
1.2 GeV
1.5 GeV
Spreader
FEL1
FEL-2
Main Beam Dump
To the Beamlines
1st Dispersive
Section
Radiator Undulator
2nd Dispersive
Section
Dispersive
Section
Delay
Line
Modulator Undulator
100m
Undulator Hall
PADReS
Photon
Analysis
Delivery and
Reduction
System
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 9
FERMI FEL High Gain Harmonic Generation scheme
Radiator
Dispersive section
Modulator
An external laser interacts with the electron beam in the modulator inducing a periodic modulation of the electron beam energy.
In a dispersive region, energy modulation is converted into density modulation with significant harmonic content. Beam current modulation inherits coherence properties from the input laser.
Coherent bunching produces coherent emission in the radiator at the desired harmonic that is then amplified.
Courtesy of Enrico Allaria
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 10
FERMI FEL-1 and FEL-2
FEL-1: single stage HGHG seeded by a UV laser, covers the range 100 nm – 20 nm.
FEL-2: double cascade HGHG to reach the wavelength 20 nm – 4 nm.
FEL-1 (Nature Phot. 6, 699 (2012)) | 
Tuning range | 100-20 nm (12-60 eV)
Relative bandwidth | 1X10-3 (FWHM)
Pulse length | <100 fs
Pulse energy | 20-100 µJ
FEL-2 (Nature Phot. 7, 913 (2013), J. Synch. Rad. 22 (2015)) | 
Tuning range | 20-4 nm (60-300 eV)
Relative bandwidth | 1X10-3 (FWHM)
Pulse length | ~50 fs
Pulse energy | 5-70 µJ
Both FELs have APPLE-II undulators in the final radiator allowing polarization control.
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 11
FERMI FEL Tunability
modulator
High gain radiator tuned at nth harmonic
Seed
THG or
tunable OPA
dispersion
FEL-1: Single stage HGHG configuration, nominal range 100-20 nm - Typical energy per pulse in the range 20-100-400 µJ. Seed: third harmonic of the Ti:Sa (up to 80-90 µJ, very limited (1%) tunability. Effective tunability: frequency upconverted OPA seed laser system. Most used OPA configuration (230-260 nm)
Other OPA processes (296-360nm). This requires a change of all the seed transport optics (>10 mirrors)
FEL-2: Double stage HGHG configuration, nominal range 20-4 nm
Typical energy per pulse in the range 10-100 µJ, depending on wavelength.
FEL performances tested in the range 14.4 – 4 nm – Upgrades: additional radiator in first stage/Higher e-beam energy – Improved seed laser system
1st mod.
1st rad.
2nd mod.
2nd rad.
DS1
DS2
DL
4
20
14.4
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 12
FERMI FEL Results and status
FERMI FEL-1 and FERMI FEL-2 are both open to user experiments and provides unprecedented performances in terms of spatial and temporal coherence, wavelength and intensity stability, and spectral purity
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 13
FERMI The experimental hall
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 14
FERMI Photon transport system PADReS
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 15
PADReS Gas-based I0 monitors and absorbers
Gas absorber:
Need to align the beam w/out destroying the sample + intensity-dependent studies
Max attenuation at all λ: 10-4
Preservation of coherence, spectrum, statistics, etc.
Intensity monitors:
Measures the number of photons of each pulse
(~3% precision, 1% reproducibility)
Online and shot-to-shot
Transparent
p = 2 ∙ 10-5 mbar

## Slide 16
PADReS Energy spectrometer PRESTO
Online (non invasive)
Shot-to-Shot
~97% of FEL  beamlines
1% of FEL  YAG + triggered CCD
Resolving Power ~15000 @32.5nm (2.5meV)
Available information: λ, BW, spectral content
Spectrometer (PRESTO)
Pulse-Resolved Energy Spectrometer: Transparent and Online
250mm
60 mm

## Slide 17
FERMI FEL Pulse-resolved spectral content
FEL pulses: single mode spectra with narrow linewidth.
FEL spectra: Gaussian with both wavelength and bandwidth stability.
Calculated Fourier-limited pulse length is close to theoretical predictions suggesting a very high longitudinal coherence.
Typical seed pulses are 120 fs long with 0.9 nm spectral width.
FEL pulses inherit the coherence from the external seed laser.
The use of seed pulses close to the Fourier limit, allows the production of FEL pulses that are also close to the Fourier limit.
4.4 nm
4.0 nm
23.8 nm
43.7 nm
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 18
PADReS Split and Delay Line AC/DC
Delay: -1.5ps ≤ ∆t ≤ 30ps (for all λ)
0.1fs-resolution
ML1: ∆t1: 0.3 ÷ 1.5ns (on selected λ)
ML2: ∆t2: 0.33ns
Wavefront splitting by means
of a sharp-edge mirror
Split and delay line:
Split the beam, retard half of it, then recombine it
AutoCorrelator / Delay Creator
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 19
PULSE LENGTH First AC/DC measurements
Data analysis still in progress…
The FERMI Commissioning Team
N. Mahne, C. Svetina, L. Raimondi, M .Zangrando - PADRES
A. Ciavardini, C. Callegari, K. Prince,M. Coreno, M. Di Fraia, P. Finetti,
P. O’Keeffe, O. Plekan, T. Mazza, R. Richter - LDM
D. Garzella, A. Klisnick
Ionization of Xe to highly charged states (autocorrelation measurement)
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 20
FERMI TRANSVERSE COHERENCE Direct beam
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 21
FERMI TRANSVERSE COHERENCE Focused beam
Measurements of the transverse coherence using a mask with pairs of pinholes or slits on it (sample prepared by M. Barthelmess) – beamline DiProI
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 22
FERMI SPOT SIZES Wavefront sensors and other techniques
Spot sizes (FWHM) @32.5nm
Diffr.-limited spot: 4×5 µm2
Best spot measured: 5×5 µm2
Best spot simulated: 5.2×7.7 µm2
See L. Raimondi’s talk at 18:20
Wavefront sensors
Initial activity (2012-2014) with DESY WFS (LLG)
One WFS (Imagine Optic) operative in experimental hall (CENILS – G. De Ninno)
Another WFS realized in collaboration with DESY and LaserLab Gottingen (2015-2016)
Other techniques
PMMA and Si indentation
Pixelated-P array
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 23
SEED LASER TO ENDSTATIONS Pump-probe opportunities
Since Feb-2013 DiProI end station equipped with external user laser
DiProI Team, PADReS team, Lasers team
FEL Pulse
Laser Pulse
Two pass optical delay line ±600ps
Automatic attenuator plate and vertical horizontal polarizer
Laser shot-by-shot Intensity monitor
Pulse selector shutter
USERS-LASER DELAY BREADBOARD
FEL pulse timing is fixed by the seed pulse.
A fraction of the seed is propagated to the beamlines and used for Pump-Probe Experiments.
Large timing jitter/drift reduction expected.
FEL
Pump
L2
IR
Probe
CCD 1
L1
Sample Plane
x
y
CCD 2

## Slide 24
FEL-IR TIME ARRIVAL TR Si3N4 reflectivity
Arrival time jitter FEL-IR laser ~10±2 fs (RMS) 3µm over 100m-path length !!!
(Measured at the ½ drop point of the reflectivity curve)
Long term (~1 day) stability time zero between FEL and IR laser ~70 – 60 fs.
*
M.Danailov, et al., Optics Express 22, 12869 (2014)
Recent result @DiProi: 6.6fs RMS jitter between a NOPA Pumped by the IR seed and FEL

## Slide 25
PULSE LENGTH Cross-correlation measurements
Two cross-correlation methods have been implemented and used for measuring the FEL pulse length.
Solid state cross correlation:
temporally & spatially encode FEL in the surface of a Si3N4 target probed with an ultrashort laser pulse
Cross correlation measurement probing the intensity of sidebands in electron spectra
* In collaboration with F. Tavella team
** In collaboration with C. Callegari and LDM team
*
**
In both cases FEL pulse length has been studied as a function of seed laser parameters and FEL wavelength.
Expected FEL pulse shortening at higher harmonics (shorter wavelength) has been confirmed by measurements.
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 26
PULSE LENGTH SPIDER measurements
With two seed laser pulses one can control and change the relative time between two FEL pulses.
For coherent pulses, a fine tuning allows to control the relative phase between the two FEL pulses.
The phase locked FEL pulses are then suitable for SPIDER§ measurement (amplitude and phase).
From a single measurement of the interference spectrogram of two identical pulses (with slightly different time and wavelength) the SPIDER algorithm reconstructs the intensity and phase profiles in the temporal domain.
§“Spectral Phase Interferometry for Direct Electric-field Reconstruction …” . OPTICS LETTERS 23, 792 1998
*G. De Ninno et al., Nat. Commun., 6, 8075 (2015)
Spectral measurements at different seed laser delay give the wavelength separation.
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 27
POLARIZATION MEASUREMENT Setup
Groups from XFEL, LOA and SLAC were invited by FERMI to collaborate with different hardware or as observers (Coordinated by E. Allaria)
Different polarization modes measured with 3 different techniques
… and different wavelengths 26nm/32.7nm and 52nm
P04 group @ PETRA III: Leif Glaser, Frank Scholz, Jörn Seltmann - European XFEL: Jens Buck (WP-74), Alberto De Fanis (WP-85), - Patrick Gessler (WP-75&76), Jan Grünert (WP-74), Markus Ilchen (WP-85), Tommaso Mazza (WP-85), Michael Meyer (WP-85) Universität Kassel: André Knie FERMI: Enrico Allaria, Mauro Trovò, Giovanni De Ninno, Primož Rebernik, David Gauthier, Carlo Spezzani, Bruno Diviacco, Simone Di Mitri, Guiseppe Penco, Luca Giannessi, William Fawley, Marco Zangrando, Nicola Mahne, Cristian Svetina, Lorenzo Raimondi, Flavio Capotondi, Paola Finetti, Carlo Callegari, Marcello Coreno, Cesare Grazioli, Oksana Plekan, Barbara Ressel, Antti Kivimäki, Laboratoire d'Optique Appliquée (LOA): Benoît Mahieu, Guillaume Lambert, Boris Vodungbo, Philippe Zeitoun, Jan Luning SLAC: Zhirong Huang, Yuantao Ding, Alberto Lutman, Stefan Moeller
LOA
polarimeter
X-FEL
E-TOF
LDM
E. Allaria et al., Phys. Rev. X 4, 041040 (2014)

## Slide 28
POLARIZATION MEASUREMENT e-TOF polarimeter
LOA
polarimeter
X-FEL
E-TOF
LDM
A single shot polarimeter based on angle resolving electron spectrometer has been developed by J.Viefhaus’ group at DESY
Theory predicts specific electron distributions over the 16 detectors depending on the used gas and FEL polarization.
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 29
POLARIZATION MEASUREMENT EUV and Visible light polarimeters
LOA
polarimeter
X-FEL
E-TOF
LDM
Optical polarimeter for EUV sources (LOA): 4 coated grazing incidence mirrors used as phase retarder for s and p field components and a 45° mirror used as a polarized.
Setup installed at FERMI: suitable for characterizing 26nm and 32nm with circular and vertical polarizations.
Proper fit of the measured detector signal as a function of the detector angle β  FEL polarization state
Measuring the polarization of fluorescence light emitted in the visible range following suitable X-UV excitations  FEL polarization state
Optical transitions selected:
He + λ1He1s(1)3p(1)He1s(1)2s(1)+λ2
Polarization measured in the visible with standard optical methods using a retarder (λ/4) and a polarizer. Acquisition are done by scanning the polarizer angle for various values of the retarder angle.
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 30
POLARIZATION MEASUREMENT Results
Measurements of the degree of polarization with different polarimeters has shown a good control of the polarization* allowing switching from linear to circular in the whole spectral range of operation.
* E. Allaria et al. Phys. Rev. X 4, 041040 (2014)
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 31
POLARIZATION CONTROL Cross-polarized undulators
Axis of Linear Polarization (°)
Bunch ID
Linearly polarized emission can be generated using undulators polarized left and right.
A crucial aspect for the quality of the final polarization is the possibility to have the same level of power from the two kinds of undulators. This can be easily controlled by acting on the seeding parameters.
First experiment has been done with first five radiators in circular right polarization and the last one in circular left.
By changing the last phase shifter it is possible to change the direction of the linear polarization.
E. Ferrari et al., Sc. Reports 5, 13531 (2015)

## Slide 32
CONCLUSIONS of the talk
FERMI FEL-1 and FERMI FEL-2 are open to user experiments, providing unprecedented performances in terms of longitudinal coherence, wavelength stability and spectral purity
With the improved control on the machine we are demonstrating the feasibility of new classes of experiments where coherence plays a major role, and that were so far accessible only to optical lasers
Dedicated diagnostics are available to help machine and experimental physicists carrying out experiments taking advantage of the peculiarities of such an FEL source
More in general, seeded FELs are extremely flexible tools opening new perspectives in the use of short wavelength free electron lasers

## Slide 33
33
Allaria E., Bencivenga F., Callegari C., Capotondi F., Castronovo D., Cinquegrana P., Craievich P., Cudin I., Danailov M.B., De Monte R., Demidovich A., D'Auria G., Dal Forno M., De Ninno G., Di Mitri S., Diviacco B., Fabris A., Fabris R., Fava C., Fawley W.M., Ferianis M., Ferrari E., Finetti P., Froehlich L., Furlan Radivo P., Gaio G., Gauthier D., Gerusina S., Giannessi L., Gobessi R., Ivanov R., Kiskinova M., Kurdi G., Loda G., Lonza M., Mahne N., Mahieu B., Manfredda M., Masciovecchio C., Mazzucco E., Predonzani M., Principi E., Nikolov I., Parmigiani F., Penco G., Plekan O., Prince K.C., Raimondi L., Rossi F., Roussel E., Rumiz L., Serpico C., Sigalotti P., Scafuri C., Spampinati S., Spezzani C., Sturari L., Svandrlik M., Svetina C., Trovò M., Vascotto A., Veronese M., Visintini R., Zangrando D., Zangrando M. and MANY MORE including users, collaborators, visitors, administrative people…
THANK YOU
Notes: The generation of two-color FEL pulses by the same electron bunch at FERMI-FEL has opened unprecedented opportunity for jitter-free FEL pump-FEL probe time resolved coherent diffraction imaging (CDI) experiments in order to access spatial aspects in dynamic processes. This possibility was first explored in proof-of-principle resonant CDI experiments using specially designed sample consisting of Ti grating. The measurements performed tuning the energies of the FEL pulses to the Ti M-absorption edge clearly demonstrated the time dependence in optical constant in Ti varying the FEL-pump intensity and probe time delay. The next planned CDI experiments in February 2013 will explore transient states in multicomponent nanostructures and magnetic systems, using the controlled linear or circular polarization of the two-color FEL pulses with temporal resolution in the fs to ps range.

## Slide 34
THANK YOU