## Slide 1: Profiler Mechanics Update
INSIDE Pisa Meeting
9/10 June 2015
V.Patera

## Slide 2: General status
Tracker mechanics almost finished ( frame & fibers)
Waiting for electronics PCB (beginning July) to finalize cooling system design
Calorimeter mechanics started
Dose Profiler complete tracking system with the calorimeter support plus 2 spare tracking planes

## Slide 3: Mechanics: tracker status
All the tracker plane (6+2 spares) ready: final frames and machined fibers in place
Waiting for electronics PCB (beginning July) to finalize cooling system design

## Slide 4
fiber planes have been machined to match the profile of SiPMs and passive components soldered on the BASIC-board

## Slide 5: Tracker mech. and cooling
asimmetric (0,5 mm) spacers among planes have
been drilled; they will help heat transport
Final configuration with PCB must be tested for heat flow

## Slide 6: Calorimeter Mechanics Status
External frame, to be fixed to the tracker, finalized
Developed a fixing system of the crystals+MAPMT elements
Integration with electronics ( and cooling) on going

## Slide 7: Holding LSF matrices
connectors on H8500 will create a space in which an insulated 4 mm x 6 mm Al bar, a spring and a screw will press the MAPMT against the crystal matrix
stiff 10 mm Al structure
1/16: crystal + H8500
2 Al bars will
press the crystals sideways

## Slide 8
0,25 mm phosphor bronze foil inserted matrix and MAPMT elements will be pressed against it

## Slide 9: Stiffness of the system
Complete setup of the 16 Matrices: 20 cm x 20 cm2 LFS calorimeter
Test of stability: put the calorimeter orizontally -> all the weight leans on the foil and monitor the bending of the foil

## Slide 10: Stability test
After a week, gravity did not succeed to move the crystals
phosphor bronze foil could be thinned (250 mm  150 mm)

## Slide 11: Calo electronic update
LNF electronic service is taking care of calorimeter electronics
Preliminary layout ready -> building phase
HV PCB modules for H8500 ordered (->Centro Fermi)
front-end for calorimeter order is being prepared (12k€+IVA->INSIDE)
Concentrator FPGA board design ok-> order will follow

## Slide 12: spares

## Slide 13
6 X-Y fiber planes + 2 spares ready
calorimeter structure almost ready
210x210x0,3 mm3 foil to be inserted here
crystal fixation system
waiting for electronics to finalize cooling
system
thanks to MARCO MAGI