## Slide 1
UPDATES on INSIDE MECHANICS
All design of mechanical parts of Inside are defined and frozen.
Construction of mechanical parts started (Torino INFN workshop)
Cooling panel  ready
Chariot and shoulder  need external workshop (welded parts). Waiting for quotation.
Heads  in progress
Delivery of some commercial parts delayed due to the new invoicing method.
Purchase of other commercial parts needs new market recognition. Regular suppliers reject the new invoicing method.
B. Giraudo
INFN torino

## Slide 2
G. Giraudo
Roma 18/12/2014
Taglio sulla base
Estensione corsa max ±400 mm
Dimensione longitudinale Testa +5 mm
Disegno Globale

## Slide 3
G. Giraudo
Roma 18/12/2014
Disegno Globale
Posizionamento Profiler
Minima Distanza tra le Teste

## Slide 5
Thermal heat exchanger
Aluminium casting with stainless steel tube embedded.
Pre-machining view.
RX of the thermal heat exchanger. Survey of tube position.

## Slide 6
G. Giraudo
Roma 18/12/2014
Disegno Impianto di Raffreddamento

## Slide 7
Cooling panel parts ready
In/Out manifolds
Flowmeter
Support panel
Ring-nut for tube transition
Fittings and chiller delivery  end of June
Polyurethane tubes delivery delayed (?)

## Slide 8
6 X-Y fiber planes + 2 spares ready
calorimeter structure almost ready
210x210x0,3 mm3 foil to be inserted here
crystal fixation system
waiting for electronics to finalize cooling
system design (beginning July)
thanks to MARCO MAGI
Profiler

## Slide 9
0,25 mm phosphor bronze foil inserted
calorimeter matrix assembly; multianode PMT will be pressed against it
Profiler