## Slide 1
Advances on the
µ-RWELL gas detector
M. Poli Lener (a)
G. Bencivenni (a) , R. de Oliveira (b), G. Felici (a) , M. Gatta (a), G. Morello (a)
    (a) LNF-INFN, Italy, (b) CERN, Meyrin, Switzerland
LABORATORI NAZIONALI DI FRASCATI
www.lnf.infn.it

## Slide 2
Introduction
The µ-RWELL technology & features
Detector performances
Large size device for future project
Cylindrical shape detector
Summary
Outline

## Slide 3
Introduction
MicroPattern Gas Detectors (MPGD) due to their performance (high rate capability and fine space resolution) are ideal tools for :
  fundamental research (Compass, LHCb, Totem, KLOE, Jlab, LHC experiments upgrades)
  applications beyond science (medical, industrial, neutron ...)
In spite of the recent relevant progress in the field, still a long way to go by dedicated R&D studies towards:
  stability under heavy irradiation (discharge containment)
  simplified construction technologies, a MUST for
      very large scale applications in fundamental research
      technology dissemination beyond HEP

## Slide 4
Small Wheel
Rates in Hz/cm2
Rates at inner rim
1–2 kHz/cm2
MPGDs @ LHC (Upgrades)
 | # chambers / size (w/out spares) | Total GEM foil area
M2R1 M3R1 | n.48 –> ~ 30x25 cm2 n.48 –> ~32.x27 cm2 | ~12 m2 ~13 m2
LHCb upgrade
GE1/1
GE2/1
ME0
Alice-TPC

## Slide 5
The biggest “enemy” of MPGDs are the discharges.
Due to the fine structure and the typical micrometric distance of their electrodes, MPGDs generally suffer from spark occurrence that can eventually damage the detector and the related FEE.
S. Bachmann et al.,
NIMA A479(2002) 294
241 Am  souce
Strongly reduced but not completely suppressed
GEM
MPGDs: stability
discharge probability
Efficiency & discharge probability
MM
10 GeV/c proton
A. Bay et al.,
NIMA 488 (2002) 162
Efficiency

## Slide 6
Technology improvements: resistive Micromegas
The resistive layer is realized as resistive strips capacitive coupled with the copper readout strips.
by R.de Oliveira TE MPE CERN Workshop
voltage drop due to sparking
For MM, the spark occurrence between the metallic mesh and the readout PCB has been overcome with the implementation of a “resistive layer” on top of the readout itself . The principle is the same as the resistive electrode used in the RPCs: the transition from streamer to spark is strongly suppressed by a local voltage drop.

## Slide 7
MPGDs: the challenge of large area
A further challenge for such MPGDs is the complexity of their assembly procedure, in case of large area devices.
The construction of a GEM requires some time-consuming (complex) assembly steps such as the stretching (with quite large mechanical tension to cope with, 1 kg/cm) of GEM foils. The splicing/joining of smaller detectors to realize large surfaces is difficult unless introducing not negligible dead zones (2÷3 mm). The width of the raw material is limited to 60 cm.
Similar considerations hold for MM: the splicing /joining of smaller PCBs is possible, opening the way towards the large area covering (dead zone of the order 0.2÷0.3 mm).
The fine metallic mesh, defining the amplification gap, is a
“floating component”, because it is stretched on the cathode
(1 kg/cm) and electrostatically attracted toward the PCB
 Possible source of gain non-uniformity.
NS2(CERN): no gluing but still stretching …
Handling of a stretched
mesh

## Slide 8
Muon Track
Cathode
RWELL_PCB
50 µm
The µ-RWELL: a novel architecture (I)
The goal of this study is the development of a novel MPGD by combining in a unique approach the solutions and improvements proposed in the last years in the MPGD field (RD51).

## Slide 9
The simplest scheme of µ-RWELL detector
1
2
3
The µ-RWELL: a novel architecture (I)
The goal of this study is the development of a novel MPGD by combining in a unique approach the solutions and improvements proposed in the last years in the MPGD field (RD51).
The detector is compact, simple to build & cost effective :
only two mechanical components: µ-RWELL_PCB + cathode
no critical & time consuming assembly steps: no gluing, no stretching, easy handling
no stiff & large frames
large area with PCB splicing technique
The µ-RWELL is easy to operate:
very simple HV supply: 2 independent channels or a trivial passive divider
The µ-RWELL is realized by coupling:
a “suitable patterned GEM foil” for the “amplification stage”  OK;
a “resistive stage” for the discharge suppression & current evacuation
a simple readout PCB board (rigid or flexible) OK

## Slide 10
The µ-RWELL: a GEM-MM mixed solution
GEM detector sketch
MM detector sketch
µ-RWELL

## Slide 11
The µ-RWELL: a GEM-MM mixed solution
The µ-RWELL has operational features in common either with GEMs or Micromegas:
from GEM it takes the amplifying scheme with the peculiarity of a “well defined amplifying gap”, thus ensuring very high gain uniformity (even better because of the absence of transfer/induction gaps)
from Micromegas it takes the resistive readout scheme that allows a strong suppression of the amplitude of the discharges
Ref. 2015_JINST_10_P02008
FWHM/MEAN= 6.9 %
Gain (a.u)
5.9 keV X-ray & 3MHz/cm2
10x10 cm2 proto with double resistive layers
Discharges for µ-RWELL of the order of few tens of nA (<100 nA @ max gain)
5.9 keV X-ray & 1MHz/cm2
5x5 cm2 proto with single resistive layer
Discharge Amplitude (nA)

## Slide 12
The µ-RWELL (Garfield simulation)
Signal from a single ionization electron in a µ-RWELL:
The absence of the induction gap is responsible for the fast initial spike, about 200 ps, induced by the motion and fast collection of the electrons then followed by a ~50 ns ion tail.
The µ-RWELL signal is similar to the MM one.
µ-RWELL – Ar:CO2 70:30 gas mixture

## Slide 13
The µ-RWELL performance (I)
The prototypes have been tested with Ar/CO2 =70/30 & Ar/i-C4H10 =90/10 gas mixtures and characterized by measuring the gas gain, rate capability and discharge in current mode.
The devices has been irradiated with a collimated flux of 5.9 keV X-rays generated by a PW2217/20 Philips Tube.
The gain has been measured vs potential applied between the top of the electrode of the amplification stage and the resistive layer.
GAIN UP TO 104
Ar/i-C4H10 =90/10

## Slide 14
The µ-RWELL performance (III)
Normalized gain vs X-ray flux for GEM and µ-RWELL for irradiation at the center of the active area, with three different collimator diameters: 10 mm, 5 mm and 2.5 mm.
X-ray Ar/CO2 – GRWELL = 3000
100 M/
A drawback correlated with the implementation of a resistive layer is the reduced capability to stand high particle fluxes: larger the radiation rate, higher is the current drawn through the resistive layer and, as a consequence, larger the drop of the amplifying voltage.
Taking into account that ionization of a m.i.p. is a factor 7 smaller than X-rays, the rate capability of the detector can be tuned with a suitable current evacuation scheme:
“Low particle rate” (LR) << 100 kHz/cm2 (mip): single resistive layer  surface resistivity (100 M/)
“High particle rate” (HR) >> 100 kHz/cm2 (mip): more sophisticated resistive scheme must be implemented (performed by MPDG_NEXT- LNF financed by GR51-INFN)
equivalent mip

## Slide 15
15
GEMs Trackers
BES III-GEM chambers
-RWELL prototype 80 MΩ /□
400 µm pitch strips
APV25 (CoG analysis)
Ar/iC4H10 = 90/10
Muon beam momentum: 150 GeV/c
Goliath: B up to 1.4 T
H4 beam test

## Slide 16
H4 beam test: orthogonal tracks
RWELL = (52+-6) µm
@ B= 0T after TRKs contribution substruction
-RWELL vs HV (B = 0.5 T)
G2k with APV
98 %
-RWELL vs B (G = 4000)
Ref. To be published in NIM A, contrib ELBA conf 2015

## Slide 17
Three PCB RWELL spliced with the same technique used for large ATLAS MM + only one cathode closing the detector
600
Splicing zone
< 0.5 mm wide
600
600
µ-RWELL for CMS-Muon system (I)
YE2
YE1
88 mm
Stiff structure with honeycomb sandwiched r/o & cathode PCBs to prevent possible deformation due to gas over-pressure
Possible detectors arrangement in GE2/1 region
60
Readout & µ-RWELL
Cathode
Honey-comb
Honey-comb
Detector gas gap
5
3
1
1
3
1
1
5
5
15
Detector cross section

## Slide 18
As a first step, the prototype will be based on the GE1/1 PCB readout:
PCB r/o 1.2x0.5 m divided in 8 r/o sectors
One single resistive layer with DLC technique with edge current evacuation scheme (expected part. rate10 kHz/cm2 )
One amplification stage (50 µm or 125 µm thick)
1200 mm
8 r/o sectors
A very simplified
detector scheme
µ-RWELL for CMS-Muon system (II)

## Slide 19
A Cylindrical µ-RWELL scheme
Flexible Cathode
Flexible RWELL+r/o
Gas gap
Copper dot
Flexible Readout
Cathode
Resistive layer
Copper top layer
Gas gap
The simplest scheme of cylindrical µ-RWELL detector
Flexible r/o should be implemented in the RWELL scheme & the same technique used by cylindrical GEM (mould, vacuum bag, ect) are employed in the RWELL detector assembly
A more easier
production assembly & greater gain uniformity

## Slide 20
SUMMARY
The µ-RWELL seems to be a very promising MPGD technology:
very compact device
very simple assembly
effective spark quenching (quantitative test tbd)
gas gain ∼104
high gain uniformity
rate capability ∼1 MHz/cm2 for m.i.p
good space resolution
R&D required to become a reliable solution for applications such as
large area tracking & compact digital calorimetry

## Slide 22
Electrons:
Diffusion Losses
I-out = I-in . G . T
(gain x transparency)
Ion Feedback =
I+drift / I-out
Ions
Ion trap
Cathode
Anode
Drift
Field
Induction
Field
~50%
~50%
signal only due to electron motion
Principle of operation: single-GEM

## Slide 23
Resistive-MicroMegas with floating mesh
(positioning rely only on the electrostics of the cell)
not to scale detector opened
not to scale detector opened
Rohacell
Aluminum support plate
Stiffening panel
Drift electrode
Pillars (128 µm)
PCB1
PCB2
PCB1
PCB2

## Slide 24
not to scale detector closed
Resistive MicroMegas with floating mesh
(positioning rely only on the electrostics of the cell)
Stiffening panel
Rohacell
Aluminum support plate
5.00
PCB1
PCB2
PCB1
PCB2

## Slide 25
ΔV (V)
The µ-RWELL performance (I)
The prototype has been tested with Ar:CO2 (70:30) gas mixture and characterized by measuring the gas gain, rate capability and discharge behavior in current mode.

## Slide 26
The µ-RWELL vs GEM (Garfield simulation)
Signal from a single ionization electron in a GEM:
The duration of the signal (purely electronic), about 20 ns, depends on the induction gap thickness, drift velocity and electric field in the gap.
Signal from a single ionization electron in a µ-RWELL:
The absence of the induction gap is responsible for the fast initial spike, about 200 ps, induced by the motion and fast collection of the electrons then followed by a ~50 ns ion tail.
The µ-RWELL signal is similar to the MM one.
GEM – Ar:CO2 70:30 gas mixture
µ-RWELL – Ar:CO2 70:30 gas mixture

## Slide 27
The µ-RWELL performance (III)
The max. ΔV achieved for the gain measurement is correlated with the onset of the discharge activity, that, comes out to be substantially different for the two devices:
discharges for µ-RWELL of the order of few tens of nA (<100 nA @ max gain)
for GEM discharges the order of 1µA are observed at high gas gain
Qualitative discharge study: µ-RWELL vs single-GEM
Systematic and more quantitative studies must be clearly performed
Single-GEM
µ-RWELL

## Slide 28
The Ohmic model for the Gain of a µ-RWELL
The gain variation of a µ-RWELL depends on the radiation flux and the observed drop is supposed to be due to the resistive layer. The gain of a µ-RWELL can be written as follows:
A gain drop corresponds to a decrease of the voltage V0:
Following the Ohm first law:
where “i” is the current measured on the resistive layer and Ω is the average resistance faced by the charges to reach the ground frame. The current “i” can be written as follows:
expanding the exponential using the Maclaurin serie up to the first order we obtain:
and thus:
which admits the following solution:

## Slide 29
The µ-RWELL performance (III)
Normalized gain vs X-ray flux for GEM and µ-RWELL for irradiation at the center of the active area, with three different collimator diameters: 10 mm, 5 mm and 2.5 mm.
The curves are fitted with the function (purely Ohmic model):
The function allows the evaluation of the radiation flux for a given gain drop of 3%, 5% and 10% for all the collimators.
Ar/CO2 – GR-WELL = 3000, GDROP <1000
100 M/
X-Ray

## Slide 30
The µ-RWELL performance (IV)
The particle flux that the µ-RWELL is able to stand, in agreement with an Ohmic behavior of the detector, decreases with the increase of the diameter of the X-ray spot on the detector.
matrix of resistive pads
for m.i.p. × 7
150-200 kHz/cm2 with X-Rays & 10 mm of “equivalent“ segmentation
Taking into account that ionization of a m.i.p. is a factor 7 smaller than X-rays, the rate capability of the detector, for a fixed surface resistivity, can be tuned with a suitable evacuation scheme of the current: a sort of a“matrix of vias” connected to ground through the readout every 1x1 cm2.
With this scheme a ∼1 MHz/cm2 for m.i.p. should be achievable
“HR scheme”

## Slide 31
The µ-RWELL performance (II)
The gain (vs particle flux) depends on the beam position: the larger is the distance covered by electrons in the resistive layer (green curve) to reach the ground, the greater is the average resistance and the lower is the rate capability.
Gain vs beam position
A drawback correlated with the implementation of a resistive layer is the reduced capability to stand high particle fluxes: larger the radiation rate, higher is the current drawn through the resistive layer and, as a consequence, larger the drop of the amplifying voltage.
“LR scheme”

## Slide 32
µ-RWELL: Energy Resolution
The prototype of µ-RWELL (100 M/□) has been tested with X-rays tube (6keV) (Ar/CO2=70/30) & the signal has been readout with an ORTEC amplifier

## Slide 33
µ-RWELL: Ion Feed-Back measurement
MM IBF Measurement NIMA 535 (2004) 2006

## Slide 34
Gas mixtures properties for
triggering & tracker detectors
T  1 /nclu * veldrift
Gas Mixture | Cluster/cm (µ 10 GeV) | Vd @ 2 kV (µm/ns)
Ar/ISO = 90/10 | 42.52±0.06 | 36 (flat)
AR/CF4/ISO = 65/28/7 | 52.00±0.07 | 113 (max)
Ar/CO2 = 70/30 | 37.22±0.06 | 64 (max)
Ar/CO2/CF4 = 45/15/40 | 52.85±0.07 | 74 (rise)
C2H2F4/CO2/SF6/ISO = 70/24/1/5 | 89.49±0.09 | 4.9 (rise)
CF4/ISO = 80/20 | 84.66±0.09 | 99 (rise)

## Slide 35
Gas Mixture | Cluster/cm (µ 10 GeV) | Vd @ 2 kV (µm/ns) | t = 1/nv (ns) @ 2 kV | long @ 2 kV (µm/cm) | tra @ 2 kV (µm/cm) | Lorentz Angle (degree) @ 2 kV | Town@ 80 kV (1/cm) | Att @ 80 kV (1/cm) | e-/clu
 |  |  | MAGNETIC FIELD = 0. T |  |  |  |  |  | 
Ar/ISO = 90/10 | 42.52±0.06 | 36 (flat) | 6.57 | 163 (flat) | 376 (flat) |  | 1695 | 0.0716 | 2.073±0.001
AR/CF4/ISO = 65/28/7 | 52.00±0.07 | 113 (max) | 1.69 | 73.6 (drop) | 133.8 (flat) |  | 1565 | 13.9 | 1.815±0.001
Ar/CO2 = 70/30 | 37.22±0.06 | 64 (max) | 4.24 | 150 (flat) | 228 (rise) |  | 1229 | 2.17 | 1.966±0.001
Ar/CO2/CF4 = 45/15/40 | 52.85±0.07 | 74 (rise) | 2.55 | 90.6 (drop) | 91.3 min |  | 1207 | 18.9 | 1.884±0.003
C2H2F4/CO2/SF6/ISO = 70/24/1/5 | 89.49±0.09 | 4.9 (rise) | 22.9 | 60.4 (drop) | 55.9 (drop) |  | 797 | 23.1 | 2.361±0.006
CF4/ISO = 80/20 | 84.66±0.09 | 99 (rise) | 1.2 | 58.0 (drop) | 76.0 (flat) |  | 1300 | 47.45 | 2.400±0.005
Gas mixtures properties for
triggering & tracker detectors