## Slide 1: Neutrons@BTF
Paolo Valente*, Roberto Bedogni, Bruno Buonomo, Luca Foggetta, Claudio Di Giulio, Lina Quintieri§
con lo staff del linac di DAFNE
Maurizio Belli, Riccardo Ceccarelli, Alberto Cecchinelli, Renato Clementi, Moreno Martinelli, Graziano Piermarini, Serena Strabioli, Luis Antonio Rossi, Raffaele Zarlenga
e con lo staff di supporto BTF
Francesca Casarin, Maria Rita Ferrazza, Manuela Giabbai
INFN Laboratori Nazionali di Frascati
*INFN Sezione di Roma
§ENEA INMRI, Casaccia (Roma)

## Slide 2: What is BTF
A facility part of the DAFNE accelerator complex, that allows to:
  Extract, attenuate, energy select, focus and collimate electrons and positrons accelerated by the linac
  Measure in real-time and tune the beam parameters (particle species, energy, intensity, beam spot size and position)
  Provide a series of services: power supply, networking, gas, DAQ, vacuum and cryogenics, alignment, magnetic fields
It generally works in “parasitic” mode to the operations of the DAFNE collider
Commissioning performed in 2002, users routinely since 2004
Mainly used by the high-energy physics and astro-particle communities
Parameter | Parasitic mode |  | Dedicated mode | 
 | With target | Without target | With target | Without target
Particle species | e+ or e- Selectable by user | e+ or e- Depending on DAFNE mode | e+ or e- Selectable by user | 
Energy (MeV) | 25–500 | 510 | 25–700 (e-/e+) | 250–730 (e-) 250–530 (e+)
Energy spread | 1% at 500 MeV | 0.5% | 0.5% | 
Rep. rate (Hz) | Variable between 10 and 49 Depending on DAFNE mode |  | 1–49 Selectable by user | 
Pulse duration (ns) | 10 |  | 1.5–40 Selectable by user | 
Intensity (particles/bunch) | 1–105 Depending on the energy | 107–1.5 1010 | 1–105 Depending on the energy | 103–3 1010
Max. average flux | 3.125 1010 particles/s |  |  | 
Spot size (mm) | 0.5–25 (y) × 0.6–55 (x) |  |  | 
Divergence (mrad) | 1–1.5 |  |  | 

## Slide 3: Neutron electro-production
Evaporation peak + fast neutrons shoulder
Tungsten target
At full linac power: 1013 e/s
  to be compared e.g. with nELBE, N=6·1015 e/s
Swanson estimate
  9.3·1010 Z(0.73±0.05) n/s kW-1
  2.15 ·1012 n/s kW-1 for Tungsten
Optimizing the target configuration can (slightly) improve the yield:
  n@BTF optimized target: 2.75 ·1012 n/s kW-1
  0.218 n/pr (over 4p and all spectrum)
In our case the main limitation will always be the intensity delivered onto the target

## Slide 4: N@BTF target
Optimized shielding, lead + polyethylene
Optimized Tungsten target: 70 mm diameter cylinder, 60 cm long

## Slide 5: Neutron spectrum
Bonner Sphere Spectrometer based on Dysprosium activation foils
1.5 m distance from optimized target
Good agreement with simulations

## Slide 6: Neutron flux
With full rate at high intensity = 4×105 n/cm2/s on a 10 cm sphere at 1.5 m distance
  BTF beam bunch rate = 49 bunches/s
  Npr = 1010 e-/bunch
  Powertarget = 40 W (absorbed by target)
With the present setup (1 Hz) = 8×103 n/cm2/s
20× photon flux

## Slide 7: Photon spectrum

## Slide 8: Neutrons vs. Photons

## Slide 9: Lead cover effect

## Slide 10: High intensity operation
Up to 2×1010 at 1 Hz
A mix of authorization (3.125×1010 average maximum) and operation problems
    Running parasitic to DAFNE collider operations, not optimized optics
    Beam losses triggering the linac interlock
Beam pulse length extended to 40 ns
  Linearly increasing beam charge (constant current from gun cathode)
  1013 electrons/s
  Plans to further increase to 160-200 ns

## Slide 11: Upgrade shielding
Added 50 cm concrete roof to the BTF bunker
Started authorization procedure to exceed 3.125×1010 particle/s

## Slide 12: Neutron diagnostics
Fast neutron Borated GEM monitor at 50 cm from target
GEM counts
Electron current
Problems: calibration, integration

## Slide 13
Work in progress
On maximum electron beam intensity
On neutron diagnostics
Waiting for users to improve experience

## Slide 14: Spares

## Slide 16
Isotropic production

## Slide 17
rem counter at ≈5 m distance from target