## Slide 1: CHIPIX65 Sviluppo di un pixel chip innovativo in tecnologia CMOS 65nm per altissimi flussi di particelle e radiazione agli esperimenti di HL_LHC e futuri collider di nuova generazione Progetto CALL 2013 CSN5
Fabrizio Palla – Consiglio di Sezione Pisa
9 luglio 2015
Web-site: http://chipix65.to.infn.it

## Slide 2: The HL_LHC challenge
HL-LHC accelerator: new frontier for particle physics after year 2024
    200 pp collisions at the same time !
    Experiments: taking data at higher L1-Trigger rate
    Read-out data: x5 particles, x10 trigger
    ALL THIS to get:
      3000 fb-1
      study rare-phenomena in Higgs sectors or other exotic decays
Events with pile-up=66; (HL-HLC will be 200 !)

## Slide 3: Pixel Detector at HL-LHC
Requirements from HL-LHC (ATLAS & CMS)
Small pixels: 50x50µm2
Large chips: 2cm x 2cm ( ~1 billion transistors)
Hit rates: 3 GHz/cm2
Radiation: 1Grad, 1016 n/cm2 (unprecedented)
Trigger: up to 1MHz with 12.5us latency
                (~100x buffering and readout)
Low power - Low mass systems
Data readout : up to 4-5 Gbs/s
TRIGGER Latency up to 12.5µs (x3) ==> deeper storage buffer

## Slide 4: CHIPIX65 Project
Proposal approved and funded by INFN in fall 2013, started 2014
Participant Research Units: Bari, Milano, Padova, Pavia, Perugia, Pisa, Torino
Project Outline :
  One goal of this project is the development of an innovative CHIP for a PIXel detector, using a CMOS 65nm technology for the first time in HEP community, for experiments with extreme particle rates and radiation at future High Energy Physics colliders. For this is part of RD53 Collaboration
  Another goal is the efficiently propagation across INFN of CMOS 65nm technology providing close collaboration and coordination of experts across different INFN sites in Italy
chipix65.to.infn.it.ch
About 40 members of which more than 50% are ASIC designers
new-2016: LECCE

## Slide 5
The CHIPIX65 Project : (about 11 FTE)
N.Demaria, G.Dellacasa, G.Mazza, A.Rivetti, M.D.Da Rocha Rolo, E.Monteil, L.Pacher, F.Ciciriello, F.Corsi, C.Marzocca, G.De Robertis, F.Loddo, C.Tamma, M.Bagatin, D.Bisello, S.Gerardin, S.Mattiazzo, L.Ding, P.Giubilato, A.Paccagnella, F.De Canio, L.Gaioni, M.Manghisoni, V.Re, G.Traversi, E.Riceputi, L.Ratti, C.Vacchi,
R.Beccherle, G.Magazzu, M.Minuti, F.Morsani, F.Palla, V.Liberali , S.Shojaii , A.Stabile , G.M.Bilei , M.Menichelli , E.Conti , S.Marconi, D.Passeri , P.Placidi
new-2016: S.D’Amico, C.Veri, A.Donno

## Slide 6: RD53 collaboration
20 Institutes (Seville has joined)
  Bari, Bergamo-Pavia, Bonn, CERN, CPPM, Fermilab, LBNL, LPNHE Paris, Milano, NIKHEF, New Mexico, Padova, Perugia, Pisa, Prague IP/FNSPE-CTU, PSI, RAL, Seville, Torino, UC Santa Cruz.
  140 on collaboration Email list
    ~70 actively contributing
    2015 FTE: ~23
  Spokes persons: Maurice Garcia-Sciveres, LBNL (ATLAS), Jorgen Christiansen, CERN (CMS)
  IB chair: Lino Demaria
  WG conveners: Marlon Barbero, Roberto Beccherle, Jorgen Christiansen, Maurice Garcia-Sciveres, Tomasz Hemperek, Valerio Re
  2 year terms coming up to renewal within 3 months
  Next Collaboration meeting: Pisa October 14-16, 2015
Activity | FTE 2015
Radiation | 4
Analog | 3
IP | 7
Simulation | 3
Top | 3
I/O | 1
Organization | 2
Total | ~23

## Slide 7: CHIPIX65 activities …at a glance
Design in 65nm
5 silicon dyes 2x2mm2 submitted
CHIPIX65 IP-blocks
  DAC-curr, ADC, SRAM,
  SER/DES, sLVDS(TX/RX)
  BandGap, D2RA digital cells
  JTAG
CHIPIX65 Analog Very Front End
  Synchronous chain
  Asynchronous chain
Integration of other RD53 IPs
  DAC-volt (Prague)
  SER (Bonn), BandGap (CPPM, CERN)
Radiation characterisation
x-ray machine at LNL / Pd-INFN
  Total Ionising Dose (TID)
  1 GRad in ~ 2 weeks
Low-p at CN accelerator LNL
    TID and Total Displacement damage
TANDEM / SIRAD
  Single Event Effects - with Heavy Ion
Studies on n-MOS, p-MOS
Irradiation of IP-block, Noise-measurements vs Irradiation
Digital Electronics:
Simulation Framework
  System-Verilog-UVM (VEPIX53)
Digital Architecture Studies
Input protocols definition
  fast/efficient/continuos (while readout)
  SEE robust
CHIPIX_SRAM, CHIPIX_IP_3, CHIPIX_VFE_2
CHIPIX_BIAS CHIPIX_VFE_1

## Slide 8: Radiation WG
Radiation test and qualification of 65nm technology: 1Grad and 2 1016 neu/cm2
  Radiation tests with X-rays, Cobalt source and 3Mev protons
  Significant radiation damage above ~100Mrad
  New radiation effects has made it difficult/slow to reach final conclusions
    Strong dependence on temperature during radiation: Cold is better
    Strong dependence on both length and width of transistors: Large is better
    Strong dependence on biasing during high temperature (100oC) annealing: High temperature anneal bad
  Realistic to reach ½ Grad with conservative design approach
    Radiation cold: -20oC
    No high temperature (100oC) annealing (needs careful verification as this limits our ability to do accelerated aging test)
    NMOS: Small degradation: 10% – 20%
    PMOS: Significant degradation: 25% (Large transistors) – 50% (very small transistors)
    Analog: Design recommendations (“large” transistors normally used in analog)
    Digital: PMOS might need to be larger than minimum size (e.g. W > 300nm, possibly too conservative) and digital cells to be characterized for speed degradation.
    Inner barrel layer to be replaced after 5 years
  Further tests of devices, circuits and full chips will determine if 1Grad can be accomplished

## Slide 9: Radiation effects (PMOS)
Requires an extended
seminar to explain
all this

## Slide 10: IO WG (R. Beccherle)
Readout and control interfaces
  Proposed control protocol @160Mbits/s
    Clock, trigger, resets, commands, configuration
    Single line (differential)
    DC balanced
    Appropriate for system synchronization
    Error correction
    Compatible with LPGBT optical link chip
    Simulated and verified
Plans
  Define readout protocol
    Rate: 1.28 – 2.56 – (5.12) Gbits/s Inner layer pixel chip: ~4Gbits/s raw data (can be reduced with intelligent formatting/compression)
    Data merging across chips Outer layer pixel chip: ~400Mbits/s
    Appropriate for electrical links: 2 – 5m (cable driver)
    Formatting, Encoding
    Compatible with LPGBT or direct optical modulation
  Implement/verify IO blocks for pixel chip
  Standardize and implement pixel test systems

## Slide 11: Lossless data compression
K. Androsov, M. Minuti, S. Poulios
  Hit rate estimation for inner barrel layer at 140 Pile-Up is about 2 GHz/cm2
  Expected high readout rate (~ 4.8 Gbits/s per chip for 1MHz trigger rate)
  2.4 Gbits/s max bandwidth per chip (2 E-links)
First studies on arithmetic data compression shown
  Indications on power consumption and timing
  Synthetized in 130 nm. Scaled to 65 nm, estimated area and power
    0.095 mm2
    20 mW
Currently starting integrating the data compression on pixel cores
  In collaboration with the Simulation group and J. Christiansen at CERN

## Slide 12: IP cores
DESIGN | CHIPIX65 team | RD53 - other
SER | PISA | Bonn
DES | PISA | n.c
SLVS | PISA | 
SLVS | Pavia | 
Clock Dist | Pavia | n.c.
BandGap | Pavia | CERN, CPPM
BandGap | Milano | CERN, CPPM
DualRail Digital cells | Milano | 
DICE RAM | Milano | CPPM
DAC-curr | Bari | Prague (Volt)
ADC | Bari | 
PLL | Torino | Bonn
PLL | Padova | Bonn
JTAG | Torino | nc
DC-DC | Lecce | 
VFE-synch | Torino | LBNL-asynch
VFE-asynch | Pavia | LBNL-asynch

## Slide 13: IPcores Pisa (G. Magazzù)
Differential transceiver complaint with Scalable Low-Voltage Signaling (SLVS) standard
Specs: 1.2 Gbps, with 200mV common mode voltage and 200mV swing.
Dimensions and Power :
  TX : 160 x 160 µm2 ; ~2 mW (estim)
  RX: 70 x 80 µm2 ; ~ 0.2 mW (estim)
small with 2 RX and 1 TX submitted in May 2015
Data parallel port at 20 bit
Standard cells with TMR
SER / DES: speed 2 Gbps
  SER: 100x56 µm2; 2.3 mW, Data strobe Output as read clock for input data buffers
  DES: 180x 56 µm2; 17,8mW; Data Valid Output as write clock for output data buffers
sLVDS TX/RX
SER / DES

## Slide 14: SERDES65_V1
SER (PISA)
DES (PISA)
Embedded Test Bench
CML-RX
High-Speed Clock
SER (PISA)
DES (PISA)
Low-Speed Clock
SERDES65_V1 Architecture
SERDES65_V1 Layout

## Slide 15: SERDES65_V2
SER (PISA)
SLVS-TX
DES (PISA)
SLVS-RX
SER (BONN)
SLVS-TX
SLVS-TX
SLVS-RX
ADC (BARI)
I/O LOGIC
Analog I/O Voltages
High-Speed Digital I/O
Data Port & Controls
SLVS-RX
Clock
SERDES65_V2 Architecture
SERDES65_V2 Layout

## Slide 16: IP Cores Pisa - planning
Test and characterization of SERDES_V1 prototypes (including TID test at CERN and SEE test at LNL in July 5)
  September 2015
Development of a test bench for the Test and characterization of SERDES_V2 prototypes
  November 2015
Development of an IP-Core library including SERDES and SLVS Driver and Receiver modules
  November 2015
Design of SERDES_V3 (possible improvements w.r.t. power management and radiation tolerance in SERDES and SLVS driver and Receiver modules)
  December 2015 – February 2016
Test and Characterization of SERDES_V3
  April 2014 – June 2016
Design of SERDES_V4 (final SERDES and Driver and Receiver integrated with ESD protection in differential pads)
  May 2016 – July 2016

## Slide 17: Attivita’ a Pisa per la sottomissione Ottobre 2014 e successivo test Fabio Morsani
progetto logica di controllo del TimeOverThreshold
readout e configurazione del pixel
layout e check pixel/matrice “1x2”, ½ BG e ½ TO
progetto testboard compatibile PIXFEL-CHIPIX65 per tutti i 3 tipi di chip e carrier per ognuno di essi
montaggio, test e distribuzione TB+CARRIER a TO e BG
test preliminari sulla configurazione di “1x2”, modifiche al layout per correzione problemi riscontrati

## Slide 18: Simulazione, 5 eventi singolo pixel in vari casi, si vede bene il clock del ToT e il caso di timeout nel conteggio del ToT

## Slide 19: Test board (F. Morsani)
Testboard developed to be compatible between PIXFEL and CHIPIX65

## Slide 20: Main RD53 milestone: RD53A
2016 : RD53 Design of RD53A prototype
  2-3 cm2 prototype
  Joined effort of the whole RD53 collaboration
  Now definition / discussions o:
    Technical Specs, Funding,
    Milestone, Design team organization
  submission end-2016
  THIS WILL BE THE OUTPUT of RD53 Collaboration, closing the major part of R&D, communities will concentrate more into the chip for the experiments then.
  Expect big contribution from R. Beccherle
CHIPIX65 contributions
  Provide Analog Front End(s)
  Provide IP-blocks
  Digital architectures (shared work)
  CHIP integration (shared work)
  IP-block whould be in a stable ‘final’ version by middle/end of 2016
  Finance contribution:
        about 1/5 of cost
        cost from 600ke to 1ME

## Slide 21: CHIPIX65 demonstrator 2015
Design of a small pixel array – in view of definition
  64x64 pixels, 50µm x 50 µm; chip size ~ 4x4 mm2
  Exercising a digital-architecture (CHIPIX65/Pg + CERN)
  Implementing IP-blocks available
    G. Magazzù involved
  Integration in Digital-on-Top methodology
  BUMP bondable to a sensors from next RD-phase 2
  full integration using Digital-on-Top approach

## Slide 22: RD53 Meeting in Pisa
Collaboration meeting in Pisa
  14-16 October
  ~50 people
  Hot topic is the definition of the RD53A chip
  Good occasion to listen on progresses on R&D

## Slide 23: Anagrafica e richieste 2016
Fisici | FTE (%)
K. Androsov | 10
M. T. Grippo | 10
F. Palla | 15
Tecnologi | 
R. Beccherle | 50
G. Magazzù | 30
F. Morsani | 10
M. Minuti | 
Consumi: 3 (5?)KE per test boards

## Slide 24
BACKUP

## Slide 25: RD53 Collaboration
Collaboration born in 2013 after a workshop among experts in CMS and ATLAS interested to develop a new generation pixel chip
Base technology chosen is CMOS 65nm
~125 members, 20 Institutes (from CMS , ATLAS or BOTH): 40-50% are ASIC designer
Bari, Bergamo-Pavia, Bonn, CERN, CPPM, Fermilab, LBNL, LPNHE Paris, Milano, NIKHEF, New Mexico, Padova, Perugia, Pisa, Prague IP/FNSPE-CTU, PSI, RAL, Sevillia, Torino, UC Santa Cruz
www.cern.ch/RD53

## Slide 26: DAC
10-bit current-steering Digital-to-Analog converter; LSB = 100nA (nominal) -Architecture: 8+2 segmented DAC (2 binary weighted + 8 unitary decoded cells)
No-minimum size transistors used (radiation)
TESTED: MonteCarlo simulation agree with data
dimensions: 140 x 240 um2

## Slide 27: ADC
12-bit ADC for monitoring of slowly varying signals;
range of 1V; serving 16-muxed inputs.Conversion rate of 5kSample/s
Architecture: Voltage-to-current , charging an integration capacitance for 212 clocks. Measurements of clock cycles needed to discharge the capacitance using a fixed current.
Large capacitance for better precision (see layout)
Design finished and submitted in May 2015.

## Slide 28: Band Gap
Normally a Band Gap should provide a DC voltage independent of Process, supply Voltage and Temperature.
  for HEP: independent of radiation damage; critical for HL_LHC
To achieve this an all-MOSFET designs have been chosen
CHIPIX65 IP-blocks submitted together with others labs
  INFN, CERN, CPPM structures

## Slide 29: Dice S-RAM
DICE memory design to prevent SEU.
  Duplicated data in nodes D e D1. If Transient happens cell does not show SEU.
  Simulation with RC parasitic, injecting fault charge release ==> DICE recovers in 2.5ns, well enough for LHC
Array of 256x256 cells in three different layout:
    simple
    with guard rings (better SEL)
    as (2) but interleaved (better resistance to Multi-Bit SEU)
Area affected by charge release
is larger than single diode
Dim: 1,8x3,3um2

## Slide 30: TORINO : Synchronous Analog Chain
PREAMPLIFIER
  One stage CSA with Krummenacher feedback
Synchronous DISCRIMINATOR
  (AC coupled to CSA)
  off-set compensated diff.amplif. + latch;
  FAST Time-over-Threshold
    Local oscillator strobing Latch (to 800MHz
Calibration circuit
  digital signal + DC calibration leve
Performance SUMMARY
Compact: ~25um x 40 um
Low power: < 5.5 uW (with ToT logic)
Low noise: ENC=100e- @Cdet=100 fF
Leakage compensation: up to 50nA/pixel
Fast Charge measurement:
  30 ke- in <300ns (or 800ns)
  up to 7-8bit (125-250e-/ADC) - no ext clock
NO Threshold-Trimming:
  autozeroing made by hardware
8x8 pixel matrix submitted and tested
Analog readout of CSA and Discriminator (via buffers)

## Slide 31: Asynchronous Analog Chain
PREAMPLIFIER
  Single amplification stage for minimum power dissipation
  Krummenacher feedback to comply with the expected large increase in the detector leakage current
DISCRIMINATOR
  High speed, low power current comparator
  Local Threshold correction via 4-bit current DAC
  5 bit counter – 400 ns maximum time over threshold
Performance SUMMARY
Compact: <25um x 50 um
Low power: ~ 5 uW
Low noise: ENC~110e- @Cdet=100 fF
Leakage compensation: up to 50nA/pixel
ToT Charge measurement:
  30 ke- in 400ns
  5-bits for 80 MHz external clock
NO Threshold-Trimming:
  autozeroing made by hardware
Test Structures produced and tested

## Slide 32: Radiation Characterization
No full review here, for that see RD53-talks at recent conference (no time to cover all today…)
Here just some hints and measurements done by CHIPIX65 (contribution to RD53)
for minimum-size p-MOS degradation significant above 100 MRad and very significant at 1 Grad (see plot). Mitigation actions:
  larger sizes (W>300-500nm)
  operation at low temperature
High T annealing is bad
Total Displacement Damage does not take a role also for 65nm
Impact on digital circuitry, analog is fine since low-mismatch and performance require already larger size than minimum
Ids-Vgs characteristics of a core small size
p-MOS for diffrent dose up to 1 Grad

## Slide 33: Digital Architecture and Simulation FrameWork
Architecture Main concept:
  Pixel organized in Regions
    local storage
    trigger matching at L1
    shared resources
  Emphasis on Analog isolation from Digital (low threshold should be reached)
Digital-on-Top approach to design large area pixel chip (~2x2 cm2)
Development of a System Verilog-UVM Simulation Framework (VEPIX53) - CHIPIX65 / CERN
IO protocols, protection from SEU, balancing and possible continuous configuration of pixel chip / cells

## Slide 34: Dual-Rail digital cells
Redundant logic which processes both the bit and the inverse bit (D2RA)
  (01) and (10) : valid data
  (00) and (11) : invalid data
Combinatorial logic gate realised:
  AND / NAND; OR / NOR; XOR / XNOR, NOT ; MUX
Sequencial logic gates:
  Edge-Triggered delay flip-flop (D-FF)
  Clock edge detector
NB: two parts of N2RA must be distant 5um
Test structure with AND/NAND tree, D-FF in series;

## Slide 35: Delta representation
Pixel ordering | H Dx | H Dy | H pixel position
By rows | 2.25 | 3.70 | 5.95
Bits per chip per event (ordering by rows)