## Slide 1: The INFN COSA project
Tommaso Boccali
(alcune slides riadattate da Daniele Cesini)

## Slide 2: INFN-CSN5 COSA project
COSA: Computing On SOC Architecture
Duration: 2 years from January 2015
Departments: 7 INFN
  CNAF, PI, PD, ROMA1, FE, PR, LNL
BUDGET :51.5 kEuro Year I

## Slide 3: Where do I find a SoC?
Mobile
Embedded

## Slide 4: Ok, but then....an iPhone cluster?
NO, we are not thinking to build an iPhone cluster
We want to use these processors in a standard computing center configuration
  Rack mounted
  Linux powered
  Running scientific application mostly in a batch environment
..... Use development board...

## Slide 5: Some nice boards
Texas Instruments EVMK2H
DragonBoard
SabreBoard
PandaBoard
...and counting...
WandBoard
Rock2Board
CubieBoard
http://elinux.org/Development_Platforms
Arndale OCTA Board

## Slide 6: NVIDIA JETSON TK1
First ARM+CUDA programmable SoC based Linux development board
4 cores ARM A15 CPU
192 cores NVIDIA GPU  300 GFLOPS (peak sp)
~ 21 GFLOPS/W (sp
... for less than 200 Euros
32bit
  64bit version announced

## Slide 7: COSA Clusters
CNAF
ROMA1
PD
4 board ARM+FPGA based
+ 1 server
16 board ARM+FPGA based
+ 4 server
ex cluster COKA (2 server)
+ nuove acquisizioni (1 server)
+ nuove acquisizioni (1 server)
(server = cpu + acceleratori)
Anno I
+ ~10 nuove board
~25 board SoC Based
(GFLOPS nominali di 2 server
tradizionali con GPU)
Anno I
Anno II
Anno II
Anno I
Anno II
Ex cluster HEPMARK
+ nuove acquisizioni (~ 3 server)
+ nuove acquisizione (~ 3 server)
Anno I
Anno II

## Slide 8: Activities & WPs
WP1: Management
WP2: Technology Tracking and Benchmarking
WP3: Implementation of the CNAF prototype
WP4: Development of dedicated network connections
WP5: Application Porting
  PISA/Boccali WP leader
WP6: Technology Transfer and Dissemination

## Slide 9: Project Timeline
Benchmarking
Tests of new boards
Cluster implementation
Cluster setup at CNAF (25 boards)
Application Porting
Tests under real life condition
Clusters upgrade (+10boards @CNAF, +12 boards @ ROME)
Benchmarks with real life applications and synthetic tests
Tests of first FPGAs for dedicated low latency network
Selection of the final architecture for the clusters
Cluster Setup in ROME (4 FPGA boards)
Application Porting
Jan 2015
Sept 2015
Jan 2016
Dec 2016
Dissemination and H2020 Preparation

## Slide 10: Applications
Theoretical Physics (PR, FE)
  Parallel applications usually run in HPC environments
    Lattice Boltzmann fluid dynamics
    Monte Carlo simulations of Spin-Glass systems
    Lattice Quantum ChromoDynamics simulations
Experimental Physics (PI, PD, CNAF)
  HEP experiments High Level Trigger applications
  Montecarlo and analysis of LHC experiments
  Applications needing portable systems
    Computer tomography
Neural Networks (RM1)
  DPSNN-STDP code

## Slide 11: Some applications examples / benchmarks

## Slide 12: Formation of a galaxy cluster with Gadget2
MULTI BOARD
CPU ONLY
276498 particles, formation of a cluster
of galaxies in an expanding Universe

## Slide 13: Formation of a galaxy cluster

## Slide 14: Neural Networks: DPSNN-STDP

## Slide 15
See Enrico Calore talk

## Slide 16: HS06
HS06 on Exynos5, TegraK1 and Atom C2750 –
Per core loaded
(data from M.Michelotto@HEPIX 2014 https://indico.cern.ch/event/320819/session/3/contribution/30/material/slides/0.pptx )

## Slide 17: Tests from CMS
Pisa

## Slide 18: Test di codice teorico (Torino - Pisa)
Case Study: Higgs Dalitz Decay
Tesi di laurea di P. Viviani (UniTo): parallelizzazione codice NLO di Passarino
Integrazione su spazio delle fasi, tempo scalare per integrazione:
  O(106) punti da integrare: mesi su CPU scalare single thread
  Codice fortran, non immediatamente riscrivibile in C++

## Slide 19
Performance
Utilizzati:
  2x Intel Xeon E5-2660 2.2 GHz (16 cores total)
  4x Intel Xeon E7-4820 2 GHz (32 cores total)
  Intel Atom SoC C2750 2.4 GHz (8 cores, cluster di 4 nodi = 32 cores)
  Una prima nota: il codice scala in modo quasi perfetto, non ci sono lock e/o inter thread communication a parte il reduce finale

## Slide 20
Add Nvidia K1 (OpenMP + FastFlow)
CPU | Seq time | Best parallel time | Multi thread scaling | Single core wrt i5
I5 2.2 GHz | 670 sec | 35.3 sec | 19 | 1
I7 2.0 Ghz | 1060 sec | 30.5 sec | 35 | 1.6
Atom 2.4 GHz | 1960 sec | 285 sec | 6.9 | 2.9
Nvidia K1 | 1680 sec | 530 sec | 3.2 | 2.5
Un po’ sorprendente …

## Slide 21
Pisa

## Slide 22
Pisa

## Slide 23: Richieste 2016
Manpower: andiamo ancora a soglia di 1 FTE
Boccali 20%
Ciampa 20%
Arezzini 20%
Bonati 10%
(nuovo assegno calcolo 30%)

## Slide 24: richieste