## Slide 1: ATF2 International Test Facility @ KEK for Nano-Scale Beam Generation and Measurements
Glen White, SLAC

## Slide 2: Overview
The ATF2 test facility
  Overview of ATF & ATF2
  International collaboration
Project Goals
  Generation, control & measurement of nano-scale beams
  Education of young accelerator physicists
  International operations
Technical Achievements
  ~40nm beam sizes @ low-charge
  Ongoing work to understand and mitigate wakefields

## Slide 3: ATF2 @ KEK

## Slide 4: International Collaboration

## Slide 5: International Collaboration
21 Institutes
11 countries

## Slide 6: Construction Timeline
  Construction started 2007
  First Commissioning of beam 2009-2010
  Operations continue today

## Slide 7: ATF2 Project Goals
Experimental verification of the ILC FFS scheme
  Development of beam tuning procedures and demonstration of operability of “local” chromaticity correction optics
  Learn to measure and control nm-scale beams
  Understand limits of focusing capabilities of this optics design
Development of ILC instrumentation
  BPMs, movers, MHz feedback, 1-um Laserwire, straightness-monitor, OTRs, wirescanners, HA-PS, fast pulser, beam tilt-meter …
Education of young generation for future linear colliders
  Active participation of graduate students and post-docs
Operation of complex accelerator in an international setting with in-kind hardware contributions and joint efforts on commissioning & operation

## Slide 8: Organization
MOU
- 17 organizations initially
ICB 1 mtg / year
TCB 2 mtgs / year
Operations:
~21 wks/year
International collaboration assisted commissioning
KEK staff + experimenters
Usually Mon-Fri
Some multi-week continueous runs
Daily ops mtg + weekly conference mtg

## Slide 9: ATF2 Facility Layout

## Slide 10: Test of ILC FFS Optics – ATF2 Parameters
 | ILC | ATF2
L* / m | 4.1 | 1.0
ξy (~ L* / β*y) | 4100 / 0.41 | 1000 / 0.1
Ebeam / GeV | 125 | 1.3
Q / nC | 3.2 | 0.16 – 1.6
β*x,y / mm | 13, 0.41 | 40, 0.1*
γεx,y / μm-rad | 5.0, 0.035 | 3.5-4.8, 0.025-0.037
σx,y / nm | 365, 7.7 | 7500 – 8700 , 37 (41 measured)
δE / E (%) | 0.15-0.19 | 0.06-0.08
frep / Hz | 5 | 3.2
Scale test of ILC FFS Optics (“Local” Chromaticity Correction)
* beta_y scales down to 0.025 mm ~ CLIC ξy

## Slide 11: ATF2 Facility Layout
Extraction Line (EXT)
Extract beam from DR
Correct for coupling and dispersion errors
Correctly match beam into final focus system.
Final Focus System (FFS)
Scale test of ILC FFS optics

## Slide 12: Beam Tuning – Overcoming V. Tight Tolerances
Optics setup:
BPM Calibration
Steering
BBA
Global Dispersion correction
Extracted emittance measurement
Extracted coupling correction
Beta matching
Model and optics verification
Aberration tuning:
Linear tuning knobs using pre-computed orthogonalised horizontal/vertical moves of 5 FFS Sextupole magnets.
  alpha_x, eta_x, alpha_y, eta_y, <x’y>
Non-linear tuning knobs using strength changes of 5 FFS Sextupoles & 4 skew-Sextupoles
  Y22, Y26, Y44, Y46
Vertical Tolerances similar to ILC – below achievable by survey techniques
Overcome using “sextuple mover knobs”
- e.g. here scan y waist

## Slide 13: Key Hardware – International Contributions
Magnets
22 Quadrupoles – IHEP, China
5 Sextuples – SLAC
3 Bends – SLAC, IHEP
23 Magnet movers (SLAC, from FFTB, um-accuracy)
“High-availability” power supplies (SLAC, ILC test)
Final doublet vibration isolated table – LAPP, France
BPMs
All quads & sexts have cavity-type BPM (<100nm res)
  c-band: PAL, S.Korea, SLAC & UK
Stripline BPMs (few um res)
  KEK & SLAC
Ring button BPM high-bandwidth readout system - Fermilab
Profile Measurement
IPBSM – KEK & Tokyo (~35 nm measurements)
Laserwire – UK (1 um measurements)
OTR/ODR (high res ~um) – KEK, UK
Diamond sensor Halo measurements – France
Multi-OTR emittance measurement (SLAC & IFIC, Spain)
High-bandwidth feedback
2-bunch nm-scale position feedback, <300ns latency – S.Korea (IP nm-BPMs), UK
IPBSM “Shintake Monitor”
Magnet Movers & BPMs

## Slide 14: Software & Beam Tuning “Apps”
“Flight Simulator” Concept
Multi-OTR Emittance Measurement
User-friendly IPBSM controls
  Core accelerator tuning software developed by KEK staff & international community
  “Flight simulator” concept developed as a way to develop & test apps remotely and easily implement @ KEK

## Slide 15: IP Beam Size Achievements
Beam size reduced over time as experience gained, hardware problems found and resolved, techniques improved etc
Great East Japan Earthquake, March 2011

## Slide 16: Intensity Dependence & Wakefields
  Wakefield effects became dominant for σy < 100 nm
    c-band cavity BPMs & bellows @ high-beta locations
    Smallest beam sizes only achieved at N < 1E9
  Static component 10-> 5 nm/1e9
    Some BPMs removed, bellows shielded, active compensation used
  Dynamic component 10 nm/1e9
    Demonstrated mitigation possible with 2-bunch feedback
  Effects understood through detailed wakefield simulation work
  Scaled to ILC parameters, expected NOT a problem
Measurements

## Slide 17: Beam Stabilization
Vertical position jitter @ IP: 106 nm -> 41 nm
2 bunch feedback (Δt = 280 ns)
Stabilize second bunch using detection of first & stripline kicker
Extrapolate IP position from 2 cavity BPMs near IP
Performance limited by BPM resolution & inability to get small beams @ high Q

## Slide 18: Education

## Slide 19: Education

## Slide 20: Summary and Thanks
  Content and slides courtesy of ATF2 collaboration and experimental contributors
  ATF2 has been, and continues to be, a very productive proving ground for LC technology and for training accelerator physicists who will hopefully go on to be responsible for the real thing…
  Main goal of ATF2 achieved: the local-chromaticity correction FFS optics works!
  Work continues to increase beam charge and reduce beta function @ IP to test CLIC-level correction scheme
    20-nm beams, Octopole correction devices…