## Slide 1: “Crystal high quality positrons extraction from the DAΦNE accelerator ring”
Marco Garattini
CERN / Imperial College London
UA9 Collaboration
DAΦNE-TF Workshop
“DAΦNE as an open Accelerator Test Facility in year 2020”
INFN-LNF (Frascati), Italia (17 December 2018)

## Slide 2: Outline
- The proposal
- Crystal physics
- Crystal-extraction history
- Sub-GeV leptons crystal beam steering
- Extraction solutions for DAΦNE
- Applications
- Conclusions

## Slide 3: The proposal
This proposal aim to implement, test and operate the extraction by a bent crystal of a positron beam from one of the Frascati DAΦNE collider rings
The proposal is supported by the UA9 Collaboration that will provide the know-how and some of the technical solution required
The goals:
prove the possibility to extract slowly a e+ beam from an accelerator ring
obtain a high-quality spill and duty-cycle
Advantages: relatively simple and cheap solution with excellent extracted beam features
Spill features pursued:
  Energy spread: Δp/p < 10-3
  Emittance: ε < 10-6 rad⋅m
  Length: ms < Δt < s

## Slide 4: Coherent processes in bent crystals
From test beam on the CERN-SPS extraction line H8:
(in the framework of the UA9 experiment)
Θout
ΔΘ
Θin
AM
AM
VR
VC
DC
CH
Θc
3
DC
Dechanneling
4
VR
Volume reflection
5
VC
Volume capture
2
CH
Channeling
crystal
[1-2]

## Slide 5: Crystal extraction history
  (1990-95) - RD22 at the CERN-SPS as a test bed of beam extraction at LHC: crystal high-efficiency extraction of multi-GeV p+ [3-4]
  (1993-98) - E853 at the FNAL-Tevatron as a test bed for the SSC: crystal high efficiency extraction of 900 GeV p+
  (2001) - The CERN-INTAS programmes on crystal technology: crystal high efficiency extraction of 70 GeV p+ by a short crystal (in IHEP U-70) [5]
  (2016) - UA9 at CERN-SPS: crystal assisted non-resonant & non-local slow extraction of 270 GeV p+ in the TT20 north area extraction line [6]
  (2018) - UA9 at CERN-SPS: crystal “virtual” non-resonant local beam extraction of 270 GeV p+ in channeling mode
  (2018) - UA9 at CERN-SPS: crystal shadowing of the ES-septum and assisted resonant slow extraction of 400 GeV p+

## Slide 6: CERN-SPS crystal extraction by UA9
2016 - slow non-local extraction of a 270 GeV p+ in channeling mode [6] [7]
beam into the TT20 extraction line towards the North Experimental Area of the SPS was demonstrated using the extraction septa and a bent crystal
UA9 CpFM
(“Cherenkov for proton Flux Measurements”)
detector for SPS and LHC has seen the extracted beam
Extraction in 2 turns
2018 - “Virtual” non-resonant local beam extraction of 270 GeV p+ in channeling mode
Joint activity with TE/ABT and EN/STI
Circulating beam
270 GeV p+
NDCH(xi)/dx
NCH
Extracted beam
0.2 mm thick virtual septum
Edge of the circulating beam core
loss ratio R ≈ NDCH / NCH= ~6 ‰
Halo density in channeling mode along the horizontal axis
(self-normalized to the total No of impinging particles)
Timepix

## Slide 7: Sub-GeV lepton crystal beam steering
In the depth of the crystal the fraction of channeled particles decreases exponentially
where LD is the dechanneling length, that is proportional to the particle energy
Moreover, the LD for e+ is 103 times shorter than for p+
In Silicon LD is ~100 μm for ~500 MeV e+
very thin crystals has to be used to reduce the dechanneling effect and increase the channeling efficiency. This could be challenging, but feasible
A so thin crystal will not affect so much the circulating beam, but study the effects of beam-crystal interactions (e.g. multiple scattering and energy deposition) is necessary to adjust the accelerator parameters and to optimize the extraction performances
The crystal robustness is guaranteed by several test performed with multi-GeV hadrons, but must be considered and evaluated
Some encouraging results have been already obtained with sub-Gev particles using thin crystals

## Slide 8: Sub-GeV crystal beam steering: e+ & p+
The idea is to use the solid expertise developed in the UA9 framework to scale crystal extraction from multi-GeV hadron beam to < 1GeV positron beam
- Few MeV p+ crystal beam steering
2012 – Mirroring and Volume-reflection of 2 MeV p+ [10] (nanometric crystal!!!)
- ultrathin silicon crystal (100 nm, half wavelength of the planar channeling oscillation),
- Deflection: ~ 5 mrad (CH), ~1 mrad (VR)
- Efficiency: 58% (CH), 42% (VR)
- Sub-GeV e+ crystal beam steering in two different configurations at the BTF (Beam Test Facility, INFN-LNF):
2006 – Channeling of 480 MeV e+ [8]
- 1 mm thick silicon crystal
~10 mrad with ~10% of efficiency
2013 – Multi-Volume reflection of 100 MeV e+ [9]
5 bent silicon crystals in a raw
5 x ~100 µm thick silicon crystal
5 mrad with ~30 % of efficiency

## Slide 9: Sub-GeV crystal beam steering: e-
2014 – (MAMI) Channeling of 855 MeV e- [11]
30 μm Silicon crystal (111),
Deflection: 910 μrad
Efficiency: 20%
2014 – (MAMI) Volume reflection of 855 MeV e- [11]
30 μm Silicon crystal (111),
Deflection:191 μrad
Efficiency: 77%
2016 – (SAGA-LS) mirroring of 255 MeV e- [12]
ultrathin silicon crystal (0.74 µm, half wavelength of the planar channeling oscillation), deflection Deflection: 450 µrad
Efficiency: 29%
Also e- crystal beam steering has been performed in different conditions, giving useful references for leptons coherent effects in bent crystals and on thin crystal technology

## Slide 10: Extraction for DAΦNE
The most common and effective approach to extract slowly from a circular accelerator is to use a resonant technique: Resonant multi-turn slow extraction
(see S. Guiducci’s talk)
The proposed crystal scenario, instead, foreseen a non-resonant technique:
Non-resonant multi-turn crystal slow extraction
- It might provide a continuous multi-turn extraction with high-efficiency and a better spill quality in a simpler and cheaper way than resonant extraction
- This can allow getting a better control of the extraction duration, a more collimated extracted beam and the septum could be not strictly necessary
- At the same time, crystals could support the resonant approach strongly contributing to extract particles towards the extraction septum  crystal-resonant hybrid extraction
Unstable region in the phase space acting on sextupoles
driving the tune towards the resonant value
(e.g. 3rd order)
gradually eject particles along the unstable separatrix of the
phase-space
The beam halo population is steadily sustained by injecting random noise (transverse or longitudinal) properly tuned
A bent crystal properly oriented intercepts the diffusive halo and kicks it by coherent deflection through the inter-planar potential

## Slide 11: Crystal extraction solutions
 | Muti-Volume Reflection | Planar Channeling | Mirroring
 | - Larger angular acceptance - Higher efficiency - More standard crystal technology | - Larger deflection angle - Multi-turn extraction | - Multi-turn extraction - No bending needed - Simpler operation procedure??? (T.b.i.)
 | - Smaller deflection angle - No multi-turn extraction - More complex crystal system | - Smaller angular acceptance - Lower efficiency - Thin crystal technology (<100 µm) | - Smaller angular acceptance - Extreme thin crystal technology (~1 µm)
 | Basic solution | Upgraded solution | Exotic but appealing
Pro
Cons
Crystal general parameters
Angle: ~mrad
Critical angle (0.5 GeV): ~300µrad
Material: silicon (or Germanium)
Thickness: 1 – 100 µm

## Slide 12: Milestones
1) Crystal extraction design and first crystal system prototypes
- Choice of the crystal extraction basic parameters
- Investigation of exotic extractions approaches
- Design and construction of different crystal system
prototypes
2) Crystal system optimization - Crystal systems prototypes characterization
in terms of performances and stability at the BTF
- Design and construction of the final prototype
- Test of the final prototype at the BTF
3) Extraction test and extracted beam commissioning
- Integration of the crystal system at the DAΦNE ring
extraction point
- First extraction test and beam monitoring
- Extraction optimization
- Crystals + holder
- Tank for the crystal system
- Angular actuator for DAΦNE - Detectors for beam
monitoring
- Angular actuator for the BTF
- Detectors for crystal
characterization

## Slide 13: Crystals, mechanical actuators and beam detectors
The UA9 solid expertise in crystal beam steering can provide know-how about:
- Thin crystal technology and characterization (e.g. [10])
Cutting edge crystal angular actuators:
  LHC piezo-goniometer (~0.1 µrad res.)
  SPS mechanical goniometer
Beam monitoring detectors:
  MediPix, Timepix, Diamondpix
  (developed together with BTF team)
  Cherenkov detectors (CpFM) [6]
CpFM Cherenkov
LHC-type piezo-gonio
Timepix
SPS position actuator
There are all the basic scientific and technological ingredients to succeed
But the devil is the details…

## Slide 14: Applications
Resuming the main goal:
Spill features pursued:
- Energy spread: Δp/p < 10-3
- Emittance: ε < 10-6 rad⋅m
- Length: ms < Δt < s
- The most immediate application of such beam is PADME (Positron Annihilation Dark Matter Experiment) [13] already running at the BTF, but currently strongly limited by the duty cycle (see M. Raggi’s talk)
- With the e+ beam from the LINAC, the maximum rate on the target is <102 e+/ns, keeping the event pile-up and the background at an acceptable level.
- Using the proposed extraction, PADME could increase the statistics by a factor 104 and its sensitivity by a factor 102, extending the discovery potential at the forefront level.
- But, also an unrealistic very bad extraction efficiency of 5% and making the worst-case scenario for the beam pulse length of 100 μs, still improve the experiment sensitivity of 50-100 times with respect to the plain LINAC beam
Current spill features from LINAC:
- Energy spread: Δp/p ~ 10-3
- Emittance: ε < 10-5 rad⋅m
- Length: Δt ~ 200 ns

## Slide 15: Conclusions
The proposal, supported by the UA9 Collaboration, foresees to implement, test and operate the extraction by a bent crystal of positron beam from one of the Frascati DAΦNE collider rings
Hadron and lepton crystal beam steering is already well known and the crystal extraction has been proved with hadrons several times and in different conditions
The proposal is based on multi-turn non-resonant extraction, but crystals could also support the resonant approach
The 3 crystal process proposed extraction are: Channeling, Multi-Volume-Reflection and Mirroring
The solid expertise developed in the UA9 framework can provide the knowhow as well as the technological support for thin crystals, angular actuators and beam monitoring detectors.
The PADME experiment might be the first user of the beam, obtaining enormous advantages in terms of duty cycle and sensitivity
In addition to providing an extracted beam with unprecedented features, this project is scientifically interesting per se: indeed no crystal-assisted extraction of positrons has been used so far

## Slide 16: References
[1] M. Biryukov, Y. A. Chesnokov, and V. I. Kotov, “Crystal channeling and its application at high-energy accelerators”. Springer Science & Business Media, 2013
[2] W. Scandale et al, PRL 98, 154801 (2007)
[3] F. Ferroni for the RD22 Collaboration, Nuclear Instruments and Methods in Physics Research A 351 (1994) 183-187
[4] The RD22 Collaboration, Phys. Lett. B 357 (1995) 671-677
[5] A. G. Afonin et al., Phys. Rev. Lett. 87.9 (2001): 094802
[6] Fraser, M. A., et al. “Experimental results of crystal-assisted slow extraction at the SPS.” arXiv preprint arXiv:1707.05151 (2017).
[7] F. Addesa et al., “The SE-CpFM Detector for the Crystal-Assisted Extraction at CERN-SPS”, 6th Int. Beam Instrumentation Conf.(IBIC’17, Grand Rapids, MI, USA, 20-24 August 2017. JACOW, Geneva, Switzerand, 2018
[8] S. Bellucci et al., Nucl. Instrum. Meth. Phys. Res. B 252 (2006) 3–6
[9] S. Bellucci et al., JETP Lett. 2013, Vol. 98, No. 11, pp. 649–651
[10] Guidi V. et al., Phys. Rev. Lett. 108.1 (2012): 014801
[11] A. Mazzolari et al., Phys. Rev. Lett. 112 (2014) 135503
[12] Y. Takabayashi et al., Phys. Lett. B 751 (2015) 453
[13] W. Scandale et al., Phys. Lett. B 734 (2014): 1-6
[14] M. Raggi, EPJ Web Conf. 142 (2017) 01026

## Slide 17
Thank you for your attention !

## Slide 18: Crystal assisted non-resonant and non-local slow extraction
2016 - slow non-local extraction of a 270 GeV p+ beam into the TT20 extraction line towards the North Experimental Area of the SPS was demonstrated using the extraction septa and a bent crystal provided by the UA9 collaboration [6]
UA9 CpFM
(“Cherenkov for proton Flux Measurements”)
detector for SPS and LHC
has seen the extracted beam
Extraction in 2 turns

## Slide 19: “Virtual” non-resonant local beam extraction in channeling mode
TIMEPIX-based measurement of the beam loss at the ES septum for non-resonant extraction
Timepix
Halo density in channeling mode along the horizontal axis
(self-normalized to the total No of impinging particles)
NDCH(xi)/dx
NCH
Extracted beam
0.2 mm thick virtual septum
loss ratio R ≈ NDCH / NCH= ~6 ‰
Circulating beam
270 GeV p+
Edge of the circulating beam core

## Slide 20: Shadowing of the ES-septum with a bent crystal
Xn
Channeled particles
not impacting the septum
Septum
Phase space during resonant extraction
Xn’
Schematic crystal shape for shadowing
A loss reduction at the ZS of 40%
was recorded on 1-second 400 GeV spill
Protons are deflected 5m upstream of the ES, to avoid loss with the anode wires
Joint activity with TE/ABT and EN/STI
Angular position actuator
180 𝜇rad bent crystal

## Slide 21: What it is also needed
By-pass of the dumping ring
Modify one of the two DAΦNE main rings to be used as a pulse stretcher of the LINAC beam
Adjust the DAΦNE ring optics to fit with the crystal system
An extraction line