## Slide 1
DAFNE as a test bench for vacuum equipment
and innovative surface treatments
V. Baglin, P. Chiggiato, R. Kersevan, and M. Taborelli
Technology Department
Vacuum, Surfaces and Coatings Group

## Slide 2
CERN vision and strategy:
- Long shutdown 2 (LS2) and Run 3
- High-Luminosity LHC
Heat load in LHC cryo-magnets
Measurements of ecloud characteristics and mitigation efficiency at CERN
How could DAFNE contribute to the understanding of heat load in LHC?
CERN vision and strategy:
- R&D programs
DAFNE contribution in the measurements of impedance.
Synchrotron radiation studies at DAFNE
An example: FCC-ee

## Slide 3
CERN Vision & Strategy Three main scientific pillars
Full exploitation of the LHC:
  Successful Run 2, LS2*, and Run 3 start-up.
  Upgrade of LHC Injectors; on-track construction of HL-LHC.
Scientific diversity programme serving a broad community:
  ongoing experiments and facilities at Booster, PS, SPS and their upgrades.
  participation in accelerator-based neutrino through CERN Neutrino Platform.
Preparation of CERN’s future:
  vibrant accelerator R&D programme exploiting CERN’s strengths and uniqueness.
  design studies for future accelerators: CLIC, FCC (includes HE-LHC).
  future opportunities of diversity programme: “Physics Beyond Colliders”.
Important milestone: update of the European Strategy for Particle Physics (ESPP) in 2020.
*LS = Long Shutdown
The update of the ESPP in 2020 will hopefully:
identify the priority for a future collider at CERN
recommend a compelling, complementary set of projects at the injectors
support accelerator R&D (superconducting high-field magnets, AWAKE, etc.)
etc.
Fabiola Gianotti
8th HL-LHC collaboration
Meeting, October 15th, 2018

## Slide 4
Our priorities: LS2
Perform major Maintenance and Consolidations
Increase intensity/brightness in the injectors to match HL-LHC requirements (LIU Project)
Increase injector reliability and lifetime to cover HL-LHC run (until ~2035) closely related to consolidation programs (in synergy with LIU Project)
Anticipate HL-LHC work
F. Bordry
8th HL-LHC Coll. Meet.
15-10-2018
LS2 period

## Slide 5
2021: beam commissioning in the injectors after LIU upgrade
LHC 14 TeV commissioning and operation
2022-2023: production years at 14 TeV ;
Lpeak ~ 2.0-2.2 1034 cm-2s-1 ; luminosity levelling
10-15 fb-1
~75-80 fb-1
~75-80 fb-1
∑(Run1 + Run2 + Run 3)
~350 fb-1
Courtesy of F. Bordry
Our priorities: LHC Run 3

## Slide 6
At present, HL-LHC is the most important CERN’s project. Its objective is an annual LHC integrated luminosity of 250 fb-1 in ATLAS and CMS for 12 years of operation.
To achieve this ambitious goal:
The LHC injector chain will be upgraded:
  Bunch population from 1.15 to 2.2x1011.
  Emittance reduction from 3.4 to 2.0 mm at the SPS extraction.
The beam optics in IP1 and IP5 will be improved:
  b* reduction from 0.55 to 0.15 m.
  Bunch rotation by crab cavities.
The new parameters coupled together imply, among other modifications, larger aperture insertion magnets (triplet magnets, D1, D2 and Q4, Q5 magnets) in P1 and P5.
The insertion magnets of P2 (ALICE) and P8 (LHCb) are not replaced nor modified.
Our priorities: HL-LHC

## Slide 7
Heat load in LHC cryo-magnets
The heat load in the LHC’s arcs remain a concern.
  Heat load is higher than expected (most probably due to e-cloud) in 4 arcs.
  The generation of the uneven distribution is probably simultaneous with LS1.
  The heat load is erratically distributed in the high heat-load arcs.
  In the same half cell, different heat load in dipole magnets.
  In single beam pipes, longitudinal variation of heat load.
Limited statistics
Courtesy of G. Iadarola CERN BE-ABP

## Slide 8
Concern for LS2 and LS3 until the cause for the higher load is not fully understood.
And the situation is not going to be better with HL-LHC beams…
Heat load in LHC cryo-magnets

## Slide 9
In-situ deposition of a-C coatings in the LHC: the coating system & process are validated.
Beam screen after coating
Optical inspection
During deposition
Assembling
Coating system & SSS243
Cables
Carbon coatings for HL-LHC

## Slide 10
Existing contract
ADDENDUM No. 4 KE3084/TE/HL-LHC to FRAMEWORK COLLABORATION AGREEMENT KN3083
Carbon coatings for HL-LHC

## Slide 11
In the SPS: strip detector (room temperature, weak dipole magnetic field).
      Electron current distribution.
In the SPS: COLDEX (cryogenic temperature, no magnetic field, gas injection)
      Electron current.
      Heat deposition (>100 mW/m)
      Pressure and gas composition.
In the LHC: Vacuum pilot sector (room temperature, no magnetic field)
      Electron current.
      Heat deposition.
      Pressure and gas composition.
Measurements of e-cloud characteristics and mitigation efficiency at CERN

## Slide 12
Slots
RF fingers
COLDEX (BA4)
Measurements of e-cloud characteristics and mitigation efficiency at CERN

## Slide 13
Vacuum pilot sector (LSS8)
Q5
Q4
18 meters
Measurements of e-cloud characteristics and mitigation efficiency at CERN

## Slide 14
  Disentangle electron multipacting and photoelectron contributions for different surfaces.
Vacuum pilot sector (LSS8)
Measurements of e-cloud characteristics and mitigation efficiency at CERN

## Slide 15
Main limitations of the three systems:
Dedicated studies are limited to small fractions of MD time.
During the LHC runs, access to the tunnel is rare and limited in time.
Only few samples can be studied.
Measurements of e-cloud characteristics and mitigation efficiency at CERN

## Slide 16
The measurement features of the three CERN’s set-ups can be exported at DAFNE profiting of:
A more flexible access, resulting in a larger variety of samples that can be measured.
Variable and tuneable beam parameters for e-cloud studies.
Hopefully, more dedicated beam time.
A better understanding of the LHC heat load origin and of its mitigation are essential.
How DAFNE can contribute?

## Slide 17
Preparation of CERN’s future:
  vibrant accelerator R&D programme exploiting CERN’s strengths and uniqueness.
  design studies for future accelerators: CLIC, FCC (includes HE-LHC).
  future opportunities of diversity programme: “Physics Beyond Colliders”.
Impedance measurements
Synchrotron rad. studies
E-cloud understanding and mitigation
DAFNE
Our priorities: R&D and studies

## Slide 18
A cryogenic system for impedance measurement of accelerator components.
We have started a program that aims to measure impedance of components at high magnetic field and cryogenic temperature in laboratory.
Even mode
Odd mode
Through measuring , , one can deduce for both modes
If the inner rods’ resistance is assumed to be identical, can be obtained
First laboratory simple prototype based on a Cu tube + inner rods.
Courtesy of S. Calatroni

## Slide 19
Examples of samples for impedance measurement.
Laser treated surfaces: tuning of laser parameters for trade-off between e-cloud and impedance reduction.
New concepts in vacuum chambers and RF fingers
Very thin NEG coatings for future synchtron light facilities and FCC-ee.
HTS coatings for FCC-hh beam screens
Impedance measurement at DAFNE

## Slide 20
Rare Earth element, Barium and Copper Oxyde Coated Conductor
FCC-hh < 1 GHz: expected further improvement compared to Cu as
Courtesy of S. Calatroni

## Slide 21
Today, CERN has collaboration for synchrotron radiation studies at:
BINP (variable e- beam energy, wide spectrum, cryogenic condition, high magnetic field)
KEK Photon Factory (fixed energy, room and LN2 temperatures)
KIT-KARA (FCC-hh, fixed energy, room temperature, LN2 temperature in the near future)
INFN-LNF-DAFNE (variable energy, wide and monochromatic spectra, irradiation of small samples and beampipes, cryogenic temperatures).
CERN is investing on both KARA and DAFNE facilities. They are complementary. Funds are ensured until 2021.
My wish is to continue the development of synchrotron radiation study at DAFNE.
DAFNE can become the reference lab for synchrotron radiation studies in vacuum technology.
Synchrotron radiation studies

## Slide 22
An example: FCC-ee
Courtesy of A. Milanese, CERN
(see his contribution at Proc. FCC Week 2017, Berlin)
Combined-yoke dipoles and quadrupoles –
 Magnetic models  and 1m-long prototypes
Ref.: R. Kersevan, “FCC-ee beam vacuum concept: the beam pipe of FCC-ee”, FCC Week 2018, Amsterdam

## Slide 23
SUPERKEKB-type cross-section, with lumped SR absorbers (“V-shaped”), spaced by 5.8 m on average.
The pumping plenum hosts vacuum pumps.
An example: FCC-ee

## Slide 24
FCC-ee Arc Vacuum Chambers Concept, R. Kersevan, CERN-TE-VSC/M. Gil Costa, CIEMAT, July 2018

## Slide 25
FCC-ee Arc Vacuum Chambers Concept
R. Kersevan, CERN-TE-VSC/M. Gil Costa, CIEMAT
July 2018
An example: FCC-ee

## Slide 26
FCC-ee Arc Vacuum Chambers Concept
R. Kersevan, CERN-TE-VSC/M. Gil Costa, CIEMAT
July 2018
An example: FCC-ee

## Slide 27
FCC-ee Arc Vacuum Chambers Concept
R. Kersevan, CERN-TE-VSC/M. Gil Costa, CIEMAT
July 2018
An example: FCC-ee

## Slide 28
3D-printed prototypes (1 m-long) (LEFT), and CAD view of the BPM blocks (LEP-type, BOTTOM)
Photo courtesy C. Duclos, CERN
An example: FCC-ee

## Slide 29
Suitable experimental measurement campaign to be carried out at DAFNE
CERN shall produce one SR absorber prototype, brazed inside a short SUPERKEKB-type chamber cross-section (1 m), on which the following measurements should be carried out:
Measure photon-stimulated desorption (PSD);
Measure/estimate photon trapping efficiency of V-shaped SR absorbers;
Measure reflectivity vs angle and energy;
Estimate effect of NEG-coating on impedance; “thin” NEG coating, preferentially (120 nm);
In addition, measurements on circular Cu chamber with a-C coating for FCC-ee booster, which will accelerate both e- and e+ and cannot be baked, could be required.
An example: FCC-ee

## Slide 30
Conclusions
DAFNE can help CERN in fulfilling its main objectives in the short-medium term:
      Providing dedicated electron cloud measurements to understand the cause of the high heat load measured in some locations of the LHC.
      Improving the knowledge of a-C coatings, which are the baseline mitigation for the excessive heat load in the beam screens of the HL-LHC’s triplets magnets.
In the long run, DAFNE will be an unavoidable test facility for future studies/projects:
      to characterize new components and surface treatments in term of impedance;
      to measure the synchrotron radiation impacts on vacuum systems;
      to clarify the effects of surface modifications and beam parameters on electron clouds;
      to provide simulation codes with reliable experimental inputs.

## Slide 32
DAFNE as a test bench for vacuum equipment and innovative surface treatments
DAFNE offers a unique opportunity to test vacuum components and surface modifications with beams. Thanks to its flexible beam parameters, a large spectrum of applications can be covered and a multitude of experiments could be conceived.
A typical example is the study of photon interaction with surfaces exposed to synchrotron radiation. Indeed, DAFNE may provide photons, in either a large or narrow spectrum of energy, that can be focused on samples or distributed along metre-long vacuum vessels. In the framework of HL-LHC and FCC, CERN’s Technology Department has a running collaboration with INFN on this theme.
The effect of specific surface treatments (thin-film coating and modified morphology) on electron clouds can be measured with positively charged beams. In that respect, DAFNE would be the ideal test bench to assess surface modifications and validate new concepts for electron pickups and other sensors.
New designs and materials could be tested for impedance reduction at different temperatures with beams having distinct characteristics.
In addition to the exceptional beam quality of DAFNE, LNF is equipped with key infrastructures, e.g. cryogenic facilities, and the expertise of skilled technical and scientific colleagues.
Abstract

## Slide 33
FCC-ee reminder:
The critical energy of SR generated by the arc dipoles of FCC-ee Z-pole (45.6 GeV) is ~ 19.5 keV, Flux=7.5 1018 ph/s/mrad, Power=7.9 kW/mrad;
The power value is less important, should focus more on flux, since the critical energy is well below the Compton edge (~ 200 keV for Cu);
Each absorber covers, on average, 0.45 mrad

## Slide 34
Mitigation techniques based on reduction of secondary electron emission by surface modifications.
Beam scrubbing: the arcs of LHC rely on that.
NEG coating (CERN,1996): extensively used in the LSS of LHC.
TiN thin film coatings and grooved surfaces (for example as in KEKB Al vacuum chambers).
Sputtered carbon coatings developed (CERN, 2007), implemented in tens of beam pipes in the SPS, and soon in two stand alone magnets of LHC and, possibly, in the final focusing magnets of LHC in LS3.
Increased surface roughness by laser, developed by ASTEC-STFC and University of Dundee.

## Slide 35
HL-LHC arc heat loads - scaling with bunch intensity
  HL-LHC
  8 kW/arc (~160W/hcell)
e-cloud in quadrupoles
e-cloud in dipoles
e-cloud in drifts
Impedance
Synchrotron radiation
  Present situation in the low-load sectors
  HL-LHC
  8 kW/arc (~160W/hcell)
Present state of the low-load sectors
(Sec. 34, 45, 56, 67 - SEY = 1.25)
Present state of the high-load sectors
(Sec. 12, 23, 78, 81, SEY = 1.35)
Heat load [kW/arc]
Bunch intensity [1011 p/bunch]
Heat load [kW/arc]
Bunch intensity [1011 p/bunch]
Courtesy of G. Skripka and G. Iadarola

## Slide 36
FCC-hh at KARA
Characterisation of FCC-hh like beam screen prototypes with sawtooth and laser treated surface at KARA.
Slots
Saw tooth
LASE surface

## Slide 37
Photon stimulated molecular desorption of
a-C coating for HL-LHC
Collaboration with BINP
Commissioning of BINP beam line with SR at ~ 45 eV critical energy
Comparison between a-C and Cu as a function of the synchrotron light critical energy
Slots
RF fingers
Synchrotron light facilities for characterization of vacuum equipment at BINP
R&D

## Slide 38
UFO