## Slide 1: Some Issues in Modern Dosimetry
Yair Grof

## Slide 2
Ph.D in Nuclear Physics – LANL, USA
1995-2008 – Head, dosimetry department, NRC – SOREQ
2008-2009 – Sabbatical at NMSU, USA
2009 – now – NDC and safety in SOREQ.
2004-now – visiting professor. Ben Gurion University.

## Slide 4: Background Dose

## Slide 5: What do we change by working underground?
Total - ~ 3.8 mSv/y
Cosmic – 0.4 mSv/Y
Terrestrial – 0.5 mSv/y
Radon – 1.5 mSv/y
Industrial & Medical….
What do we have to deal with? – less then 0.1 mSv/y (WIPP), (not measurable)

## Slide 6: Dosimetry
The measurement by a dosimeter of the dosage of radiation a person has received (dictionary)
Radiation dosimetry is the measurement and calculation of the absorbed dose in matter and tissue resulting from the exposure to indirect and direct ionizing radiation.
A scientific subspecialty in the fields of health physics and medical physics that is focused on the calculation of internal (Internal dosimetry) and external doses from ionizing radiation.

## Slide 7: Dosimetry
Dose is reported in gray (Gy) for matter or sieverts (Sv) for biological tissue, where 1 Gy or 1 Sv is equal to 1 joule per kilogram.
Non-SI units are still prevalent as well, where dose is often reported in rads and dose equivalent in rems.
By definition, 1 Gy = 100 rad and 1 Sv = 100 rem.

## Slide 8: Absorbed dose
How much energy is absorbed by the body?
1 Gy = 1J/Kg
Gy does not describe the biological effects of the different radiations.
If we want to know the influence on the human body we have to use other units: Sv or rem

## Slide 9: Dose of K-40 from a single cell
Basic :
K-40:
half life – 1.277E9 y
S.A= 2.54E5 Bq/g
Natural abundance = 0.0117 %
Decay Mode =
Beta (89.3%) , Max energy – 1.3 MeV
Gamma (10.7%), Energy – 1.461 Mev

## Slide 10: So, what we going to do?
MCNP (Monte Carlo N-Particle code ) – cannot work in this distance.
Microshield Code – “not possible to run so close”, please check again 
We have to go back to basics:
How much K-40 in 1 cell?
What is its influence?

## Slide 11
40K is 0.0117% of natural K. K-40 specific activity: 0.0000071 Ci / g(Argonne Lab.2005)
SO, 17.6 pg K / cell x 0.000117 = 2.06 fg of 40K / cell * 0.0000071 fCi / fg = 0.0000146 fCi in 1 cell.
0.0000146E-15Ci = 5.402e-10 Bq in 1 cell

## Slide 12: From the litrutare
Let:
A = the activity concentration in Bq g-1, of the radionuclide in the tissue
E = the average alpha or beta particle energy, in MeV per disintegration
The rate of energy absorption per gram tissue is A E (MeV g-1 s-1).
The absorbed dose rate is:
D=AE[MeV/gs]x1.6E-13[J/MeV]x1E3[g/Kg] =
1.6E-10AE[Gy/s]
(cember at.al)
So it seems to be very very small. How can we get a better estimate?

## Slide 13: Let’s go to Wikipedia
Amount of potassium element in body: 140 grams (1.5 pCi/g or 55 Bq/kg of body weight)
Typical K-40 activity in body: 0.1 uCi; This means that there are over 200,000 atoms of K-40 that decay in the body each minute!
The dose to a typical member of the population is approximately 15-20 mrem/year due to the K-40 in the body .
K-40, decay produces about 4,400 disintegrations per second (becquerels) continuously throughout the life of the body.

## Slide 14
20 [mRem/y]@body = > about 50E12 cells in the body
20/50E12 = 4e-13 mRem/y=4E-18Gy/y=
= 5E-23 Gy/s
And is it good for us? 

## Slide 15: Compare to other exposures
Annual limit for radiation workers: 50 mSv/Y
Annual limit for the public: 1 mSv/y ~3E-11 mSv/s
The main reaction that a beta particle can do in the body are excitation and ionization.
The main source for damage is the ionization.
In every interaction of beta particle from k-40, will be approximately 100 ionizations per cm.
The human cell can survive about 300 defects
Natural mechanism.
We are far away from any influence of the beta from k-40 to the body.

## Slide 16: Short lived isotopes and internal dosimetry
Workers with open sources should be check every 3 month for internal exposure (urine fetus, WBC). – the Israeli law.
The lodic – if you work with isotopes regularly, you will find any miss use or exposure.
We have a big nuclear pharmaceutical place
They work with high level of radioacrive materials:
Tc-99 – 20 Ci/shift
I-131 – 2 Ci/shift
F-18 – 10 Ci/shift
Ga-67 – 1Ci/shift
Tl-201 – 1 Ci/shift
Ga-68 - 1 Ci/shift

## Slide 17
The workers give urine every 3 months or after they have an accident/incident .
Is it enough?

## Slide 18: Half life of main isotopes all have beta decay
Half life | isotope
8.02 Days | I-131
3.04 days | Tl-201
3.26 Days | Ga-67
6.007 H | Tc-99m
1.83 H | F-18
68 m | Ga-68

## Slide 19
Is there a way to find this short lived isotopes in a routine measurements?
No way – they will disappear until the measurement will end.
What can we do?

## Slide 20: What happened in the world?
US – nothing. Call it “miss dose”
Canada – they have new regulation but no method to work with.
Hungary – urine test every day!
Swiss , Portugal –have new research, regulations, but! Most of the recommendations cannot be used (instrument doesn't fit this measurements)

## Slide 21: What we done?
We gave 4 workers a personal air pump.
We check there urine every day.
We calculate the exposure from the measurements.
We use IMBA, to find out about the internal exposure of the workers.
We found out that the workers expose to low/medium levels of exposure in regular work.
This accumulates to levels of exposure beyond regulation limits.

## Slide 22: recomendations
2 stages of dealing with the problem:
1 – early warning : we use 2 types of measurements:
continues air monitoring
Handheld contamination monitoring
This can give us early signs of a problem but we cannot use them as an official results.
Second stage: official monitoring:
For some isotopes we recommend urine tests twice in a shift. In the lab!
If something is over a limit – they send the urine to the main dosimetry unit.

## Slide 24
Thank you