## Slide 1
PhD Seminar
Oct 16, 2017 - Rome
Impedance model and collective effects
for FCC-ee
E. Belli
Supervisors: M. Migliorati, G. Rumolo

## Slide 2
      European Strategy statement (2013):
      “There is a strong scientific case for an electron-positron collider, complementary to the LHC, that can study the properties of the Higgs boson and other particles with unprecedent precision and whose energy can be upgraded.”
The FCC-ee project
E. Belli - Impedance model and collective effects for FCC-ee
1
      Within the FCC studies, FCC-ee would be the first step towards the 100 TeV hadron collider FCC-hh
RF
RF
IP
IP
9.4m
12m
Middle straight
1570m
30mrad
      FCC-ee layout compatible with FCC-hh

## Slide 3
      European Strategy statement (2013):
      “There is a strong scientific case for an electron-positron collider, complementary to the LHC, that can study the properties of the Higgs boson and other particles with unprecedent precision and whose energy can be upgraded.”
FCC-ee parameter list
E. Belli - Impedance model and collective effects for FCC-ee
2
Beam energy [GeV] | 45.6 (Z) | 80 (W) | 120 (H) | 175 (tt)
Circumference [km] | 97.75 |  |  | 
RF frequency [MHz] | 400 |  |  | 
Arc cell optics | 60º/60º | 90º/90º |  | 
RF voltage [GV] | 0.1 | 0.44 | 2.0 | 9.5
Momentum compaction [] | 1.48 | 0.73 |  | 
Betatron tunes / | 269.138/269.22 | 389.154/391.22 | 389.129/391.199 | 389.104/391.176
Synchrotron tune | 0.0248 | 0.0229 | 0.0357 | 0.0672
SR energy loss/turn [GeV] | 0.036 | 0.34 | 1.72 | 7.8
Beam current [mA] | 1390 | 147 | 29 | 6.4
Bunches/ring | 16640 | 2000 | 393 | 48
Bunch population [] | 1.7 | 1.5 | 1.5 | 2.7
Horizontal emittance [nm] | 0.27 | 0.28 | 0.63 | 1.34
Vertical emittance [pm] | 1.0 | 1.0 | 1.3 | 2.7
Energy spread [%] | 0.038/0.132 | 0.066/0.153 | 0.099/0.151 | 0.147/0.192
Bunch length [mm] | 3.5/12.1 | 3.3/7.65 | 3.15/4.9 | 2.45/3.25
Luminosity /IP [/cm2s] | 230 | 32 | 7.8 | 1.8
Beam energy [GeV] | 45.6 (Z) | 80 (W) | 120 (H) | 175 (tt)
 | 97.75 |  |  | 
 | 400 |  |  | 
Arc cell optics | 60º/60º | 90º/90º |  | 
 | 0.1 | 0.44 | 2.0 | 9.5
 | 1.48 | 0.73 |  | 
 | 269.138/269.22 | 389.154/391.22 | 389.129/391.199 | 389.104/391.176
 | 0.0248 | 0.0229 | 0.0357 | 0.0672
 | 0.036 | 0.34 | 1.72 | 7.8
 | 1390 | 147 | 29 | 6.4
Bunches/ring | 16640 | 2000 | 393 | 48
 | 1.7 | 1.5 | 1.5 | 2.7
 | 0.27 | 0.28 | 0.63 | 1.34
 | 1.0 | 1.0 | 1.3 | 2.7
 | 0.038/0.132 | 0.066/0.153 | 0.099/0.151 | 0.147/0.192
 | 3.5/12.1 | 3.3/7.65 | 3.15/4.9 | 2.45/3.25
 | 230 | 32 | 7.8 | 1.8

## Slide 4
Motivation of these studies
E. Belli - Impedance model and collective effects for FCC-ee
3
      Performance limitations due to collective effects
      Wakefields and impedances
Interaction of the beam with external environment
Beam-self fields
Fields from another beam
Fields from an electron/ion cloud
      Beam-beam
      Electron cloud
      Collective effects can produce instabilities
        Study instabilities
        Predict the effects on the beam dynamics
        Find possibile solutions for their mitigation

## Slide 5
First some theory…
E. Belli - Impedance model and collective effects for FCC-ee
4
Wake fields (time domain): electromagnetic fields generated by the interaction of the beam with the vacuum chamber
Beam coupling impedances (frequency domain)
      Each device has an impedance to be characterized and minimized
Discontinuity  the source loses energy and the witness feels a force along the length of the discontinuity
Source
Witness
Finite conductivity  Delayed EM fields due to a delay in the induced currents and the witness feels a force all along the length
Perfectly conducting smooth pipe  the witness does not feel any force from the source
Ultrarelativistic limit : no EM field in front of the beam
      Impedance model needed

## Slide 6
Short-range wake field
  Broad-band impedance
  Single-bunch instabilities
Long-range wake field
  Narrow-band impedance
  Coupled-bunch instabilities
5
First some theory…
E. Belli - Impedance model and collective effects for FCC-ee
5
          Microwave Instability (MI) in the longitudinal plane
          Transverse Mode Coupling Instability (TMCI) in the transverse plane
        As bunch intensity increases, frequencies of the intra-bunch modes () shift and merge, giving rise to the instability
        Above the threshold:
        Transverse case
          Bunch loss
        Longitudinal case
          Increase of the bunch length and energy spread
          Bunch internal oscillations (dangerous in beam-beam collisions)

## Slide 7
Resistive wall impedance
E. Belli - Impedance model and collective effects for FCC-ee
6
      Produced by the finite conductivity of the pipe walls
Longitudinal
Transverse
      For a circular vacuum chamber with radius and conductivity
Three layers
(No Coating)
      Cu
        2 mm
        Ωm
      Dielectric
        6 mm
        Ωm
      Iron
        Infinity
        Ωm
35mm
      Coating thickness plays a fundamental role in the reduction of the RW impedance
Non Evaporable Getters (NEG)
      Ωm
      Electron cloud mitigation and pumping
      Very critical RW contribution

## Slide 8
E. Belli - Impedance model and collective effects for FCC-ee
RW single bunch effects : microwave instability
7
      Microwave regime for 1 𝜇𝑚 thickness
      Thin NEG films to increase the microwave instability threshold
      Other machine components to be included!
Nominal bunch population

## Slide 9
E. Belli - Impedance model and collective effects for FCC-ee
RW single bunch effects : microwave instability
8
      Beamstrahlung allows to have stable beams for thicker coatings
Nominal bunch population

## Slide 10
E. Belli - Impedance model and collective effects for FCC-ee
Experimental activity: NEG thin film coatings
9
      Ongoing measurements for NEG thin film coatings with thicknesses 250 nm
      NEG deposition via DC magnetron sputtering
        1 𝜇𝑚, 200 nm, 100 nm and 50 nm
      Surface analysis by X-ray photoelectron spectroscopy (XPS) to study the material activation
      SEY measurements
Final goal
Find an optimal thickness of the coating satisfying impedance, pumping and electron cloud requirements at the same time

## Slide 11
TMCI for 100 nm thickness
E. Belli - Impedance model and collective effects for FCC-ee
      Analytic simulations with DELPHI code including the bunch lengthening due to the longitudinal wake
      TMCI threshold 2.5x higher than nominal intensity w/o BS
      Other machine components to be included!
10
w/o BS
w/ BS
Nominal bunch population
Nominal bunch population

## Slide 12
Longitudinal impedance budget
E. Belli - Impedance model and collective effects for FCC-ee
11
Resistive Wall (Cu, r=35mm) | 223.2
RF Cavities | 18.16
RF Tapers | 13.11
BPMs | 31.82
H collimators | 17.92
V collimators | 20.57
Resistive Wall (Cu, r=35mm) | 223.2
RF Cavities | 18.16
RF Tapers | 13.11
BPMs | 31.82
H collimators | 17.92
V collimators | 20.57
      55 400MHz RF cavities with tapers
      10000 SR absorbers
      4000 four-button BPMs (45 rotation)
      20 collimators (10 for each plane)
3.5 mm
2
3
1
4

## Slide 13
emitter
absorber
12
Lost
t
Bunch spacing
Beam pipe
Bunch
Positively charged bunches passing through a section of an accelerator
Primary or Seed Electrons
  Residual gas ionization
  Photoemission due to synchrotron radiation (photoelectrons)
Primaries attracted and accelerated by the beam to energies up to several hundreds of eV
Emission of secondary electrons (energies up to few tens of eV)
1
Absorbed or reflected (no secondaries generation)
Accelerated by the following bunch (secondaries production)
Avalanche electron multiplication
(multipacting effect)
Property of the surface
emitter
absorber
2
3
4
5
Electron cloud
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 14
13
Energy [GeV] | 45.6 |  |  |  | 
Bending radius [km] | 11 |  |  |  | 
Bunch population [] | 1.7 |  |  |  | 
Horizontal emittance [nm] | 0.27 |  |  |  | 
Vertical emittance [pm] | 1 |  |  |  | 
Bunch length [mm] | 3.5 |  |  |  | 
Arc elements |  | L[m] | B[T] or G[T/m] | [m] | [m]
 | B1L | 23.44 | 0.014 | 50 | 55
 | B1 | 21.94 |  |  | 
 | QF2/QD1 | 3.1 | 5.65 | 34/92 | 92/34
Energy [GeV] | 45.6 |  |  |  | 
Bending radius [km] | 11 |  |  |  | 
 | 1.7 |  |  |  | 
Horizontal emittance [nm] | 0.27 |  |  |  | 
Vertical emittance [pm] | 1 |  |  |  | 
Bunch length [mm] | 3.5 |  |  |  | 
Arc elements |  | L[m] | B[T] or G[T/m] |  | 
 | B1L | 23.44 | 0.014 | 50 | 55
 | B1 | 21.94 |  |  | 
 | QF2/QD1 | 3.1 |  | 34/92 | 92/34
Magnets in the ring
  Dipoles 71.6%  69.75 km
  Quadrupoles 10.1%  9.84 km
  Sextupoles 0.6%  584.5 m
  Drifts 17.7%  17.24 km
Total length of the FODO structure 55.89 m
EC build up in the arcs
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 15
14
Parameter scans
  Secondary Emission Yield (SEY)
  Photoelectron Yield Y = [0.02, 0.04, 0.3]
  Reflectivity R = [1%, 30%, 80%]
Hydrogen
  10-9 mbar (0.75 nTorr) pressure in the vacuum chamber at 300K
  Ionization cross section
Number of SR photons per particle per meter
Number of photoelectrons per particle per meter
Vacuum chamber with 35mm
Three times higher than LHC
      Photoemission due to SR
      Ionization
Simulation studies
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 16
Maps for the electron cloud
E. Belli - Impedance model and collective effects for FCC-ee
15
Map formalism as alternative to detailed build up simulations
Exponential growth of the electron density during the train of bunches (rise time)
Saturation due to space charge in the cloud itself
Decay of the number of electrons after the passage of the train (decay time)
Possible application: find the optimal filling scheme which minimizes the heat load
Map coefficients are function of the pipe and the beam parameters

## Slide 17
Maps for the FCC-ee dipoles
E. Belli - Impedance model and collective effects for FCC-ee
16
Arc Dipole for Y = 0.04, R = 80%
PyECLOUD simulations for long bunch train and gap to evaluate the map coefficients
Use the map coefficients to simulate the electron density and the heat load evolution for different bunch filling patterns
Inserting additional gaps in the bunch train allows to mitigate the ecloud build up in the machine

## Slide 18
17
Small variations in the geometry of the pipe can generate accidental cavities and produce trapped modes
These modes cannot propagate into the pipe and therefore they remain localized near the discontinuity, producing narrow resonance peaks of the impedance.
Possible source of heating
Model: BB resonator
Worst case scenario when
Trapped modes in the Interaction Region
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 19
18
Time domain simulations (Gaussian bunch with =5mm) show the existence of a trapped mode at frequency 3.5 GHz
Longitudinal slots perpendicular to the HOM field
Frequency domain simulations confirmed the presence of this mode
CST
CST
Electric field lines perpendicular to the beam trajectory
A. Novokhatsky
Water-cooled absorber on these slots
Trapped modes in the Interaction Region
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 20
19
Wake fields induced by the finite resistivity of the beam vacuum chamber
Three layers
  Cu/Be (2/1.2 mm, Ωm)
  Dielectric (6 mm, Ωm)
  Iron (Infinity, Ωm)
Energy [GeV] |  | 45.6 | 80 | 120 | 175
Bunch population [] |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
[mW/m] | Cu | 1.4 | 1.5 | 4.9 | 30.7
 | Be | 2.22 | 2.3 | 7.5 | 47.4
[W/m] | Cu | 102.2 | 11.04 | 4.04 | 2
 | Be | 157.08 | 16.7 | 6.2 | 3.03
Energy [GeV] |  | 45.6 | 80 | 120 | 175
 |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
 | Cu | 1.4 | 1.5 | 4.9 | 30.7
 | Be | 2.22 | 2.3 | 7.5 | 47.4
 | Cu | 102.2 | 11.04 | 4.04 | 2
 | Be | 157.08 | 16.7 | 6.2 | 3.03
IW2D
Analytic formula for a circular beam pipe with radius
Resistive wall in the Interaction Region
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 21
20
Energy [GeV] |  | 45.6 | 80 | 120 | 175
Bunch population [] |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
[mW] | Q1 | 19.5 | 20 | 68.2 | 393.5
 | Q2 | 5.6 | 5.9 | 21.5 | 122.4
[W/m] | Q1 | 1379.8 | 145.6 | 56.3 | 25.2
 | Q2 | 396.2 | 42.9 | 17.7 | 7.8
Energy [GeV] |  | 45.6 | 80 | 120 | 175
 |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
 | Q1 | 19.5 | 20 | 68.2 | 393.5
 | Q2 | 5.6 | 5.9 | 21.5 | 122.4
 | Q1 | 1379.8 | 145.6 | 56.3 | 25.2
 | Q2 | 396.2 | 42.9 | 17.7 | 7.8
r
l
ltr
h
ABCI
175 GeV
SR masks
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 22
Conclusions
E. Belli - Impedance model and collective effects for FCC-ee
21
Electron cloud studies
  Electron cloud build up evaluated in the arc and IR magnets
    Map formalism for filling patterns optimization
  Instability threshold to be evaluated with macroparticle simulations
Impedance studies
  Resistive wall
    MI regime for thicker coating
      for MI threshold below the nominal bunch intensity
    Stable beams with NEG thin films and/or beamstrahlung
    TMCI threshold seems to be not a limitation
    Experimental studies to find the optimal thickness satisfying impedance, pumping and electron cloud requirements
  Include other components in the impedance model for single bunch instabilities
Interaction Region studies
  Heat load due to RW and SR masks impedances estimated
    Higher losses at low energy
        One unavoidable trapped mode found at 3.5 GHz
          Insertion of longitudinal slots and design of HOM absorbers needed

## Slide 23
Thanks for your attention

## Slide 24
Backup
E. Belli - Impedance model and collective effects for FCC-ee

## Slide 25
RW impedances
E. Belli - Impedance model and collective effects for FCC-ee
1

## Slide 26
The importance of the RW for FCC-ee
E. Belli - Impedance model and collective effects for FCC-ee
2
Beam energy [GeV] | 45.6
Circumference [km] | 97.75
RF frequency [MHz] | 400
Arc cell optics | 60º/60º
RF voltage [GV] | 0.1
Momentum compaction [] | 1.48
Betatron tunes / | 269.138/269.22
Synchrotron tune | 0.0248
SR energy loss/turn [GeV] | 0.036
Longitudinal damping time [ms] | 414
Beam current [mA] | 1390
Bunches/ring | 16640
Bunch population [] | 1.7
Horizontal emittance [nm] | 0.27
Vertical emittance [pm] | 1.0
Energy spread [%] | 0.038
Bunch length [mm] | 3.5
Luminosity /IP [/cm2s] | 230
Beam energy [GeV] | 45.6
 | 97.75
 | 400
Arc cell optics | 60º/60º
 | 0.1
 | 1.48
 | 269.138/269.22
 | 0.0248
 | 0.036
 | 414
 | 1390
Bunches/ring | 16640
 | 1.7
 | 0.27
 | 1.0
 | 0.038
 | 3.5
 | 230
      Example : the longitudinal plane
        Very low momentum compaction and energy spread
          Boussard criterion to obtain a scaling with beam parameters
        The machine length

## Slide 27
NEG coatings
E. Belli - Impedance model and collective effects for FCC-ee
3
Getters are material that can absorb gas molecules.
Clean surface needed!
In non-evaporable getters (NEG) the clean surface is obtained by heating in vacuum so that the oxide layer grown on the surface can be diffused into the bulk
T = RT
T = RT
T = Tactivation
Oxide layer
No pumping
High SEY
High DY
Activation (oxide dissolution)
Pumping
Low SEY