## Slide 1: SuperKEKB Vacuum System
ECLOUD’12 (the 5th electron-cloud workshop)
2012.6.6
Kyo Shibata (on behalf of KEKB Vacuum Group)
KEK Tsukuba site
SuperKEKB
Linac
Mt. Tsukuba
Damping Ring

## Slide 2: KEKB was shut down on Jun 30th 2010, and upgrade of KEKB has started.
KEKB B-factory :
  Electorn-positron collider with asymmetric energies of 8 GeV (e-) and 3.5 GeV (e+).
  Made a great contribution to confirmation of CP violation in the neutral B meson system.
  Operation period : 1998 to 2010
  Peak luminosity : 2.1×1034 cm-2s-1
  Total integrated luminosity : 1040 /fb
To pursue research on flavor physics, much more luminosity is required and the SuperKEKB project was begun in 2010.
  Commissioning of SuperKEKB will start in the second half of FY2014.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 2
Prof. Suzuki (Director General of KEK) pressed the beam abort switch of KEKB.
Shut down ceremony (Jun 30th 2010, AM9:00 @ KEKB control room)

## Slide 3: Mission of SuperKEKB
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 3
Next-generation
B-factories
Design Luminosity of SuperKEKB is 81035 /cm2/s, which is about 40 times than the KEKB’s record.
The total integrated luminosity will reach 50 /ab just over ten years after inauguration.

## Slide 4: Design Concept of SuperKEKB 1 How to Increase Luminosity by 40 Times
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 4
y* at IP : 5.9 -> 0.27/0.30 mm (e+/e-)
  Nano-beam scheme (first proposed for SuperB by P. Raimondi)
  Luminosity gain : 20
Beam current : 1.7/1.4 A -> 3.6/2.6 A (e+/e-)
  Luminosity gain : 2
Beam-beam parameter : 0.09 -> 0.09
  Luminosity gain : 1
Total Luminosity Gain : 20  2  1 = 40
Beam-Beam parameter
Beam current
Vertical beta function at IP
Geometrical reduction factors
(crossing angle, hourglass effect)
Beam aspect ratio at IP
Lorentz factor

## Slide 5: Collision Scheme Nano Beam Scheme
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 5
d = x*/
SuperKEKB
Nano Beam scheme
Half crossing angle : f
2f = 83 mrad
overlap region << bunch length
5-6 mm
10-12 mm
100-150 mm
6-7 mm
Hourglass requirement
KEKB
Head-on (crab crossing)
overlap region = bunch length
y*  z  6 mm
y*  x*/  300 m
In nano-beam scheme:
Vertical beta function at IP can be squeezed to 300 m.
Small horizontal beam size at IP is necessary.
Low emittance, small horizontal beta function at IP

## Slide 6: Design Concept of SuperKEKB 2
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 6
To reduce the construction costs
  Use the KEKB tunnel
  Use the components of KEKB as much as possible.
    Preserve the present cells in HER.
    Replace dipole magnets keeping other main magnets in LER arcs.
Other features
  No option for polarization at present.
  Changing beam energy: 3.5/8.0 -> 4.0/7.0 GeV (e+/e-)
    LER : Longer Touschek lifetime and mitigation of emittance growth due to the intra-beam scattering
    HER : Lower emittance and lower SR power

## Slide 7: Comparison of Parameters between KEKB and SuperKEKB
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 7
 | KEKB Design | KEKB Achieved : with crab | SuperKEKB Nano-Beam
Energy (GeV) (LER/HER) | 3.5/8.0 | 3.5/8.0 | 4.0/7.0
by* (mm) | 10/10 | 5.9/5.9 | 0.27/0.30
bx* (mm) | 330/330 | 1200/1200 | 32/25
ex (nm) | 18/18 | 18/24 | 3.2/5.3
ey /ex (%) | 1 | 0.85/0.64 | 0.27/0.24
sy(mm) | 1.9 | 0.94 | 0.048/0.062
xy | 0.052 | 0.129/0.090 | 0.09/0.081
sz (mm) | 4 | 6 - 7 | 6/5
Ibeam (A) | 2.6/1.1 | 1.64/1.19 | 3.6/2.6
Nbunches | 5000 | 1584 | 2500
Luminosity (1034 cm-2 s-1) | 1 | 2.11 | 80

## Slide 8: Outline of Upgrade to SuperKEKB
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 8
TiN-coated beam pipe with antechambers
Colliding bunches
Damping ring
Low emittance gun
Positron source
New positron target / capture section
Low emittance electrons to inject
Low emittance positrons to inject
New beam pipe
& bellows
Belle II
New IR
New superconducting /permanent final focusing quads near the IP
e- 7 GeV 2.6 A
e+ 4 GeV 3.6 A
Redesign the lattices of both rings to reduce the emittance
Add / modify RF systems for higher beam current
Replace short dipoles with longer ones (LER)
SuperKEKB

## Slide 9: New Beam Pipes for SuperKEKB
To cope with the electron cloud issues and heating problems, antechamber type beam pipes are adopted with a combination of TiN coatings, grooved shape surfaces and clearing electrodes.
Beam
NEG pumps
Concept
LER arc section:
  Beam pipes are replaced with new aluminum-alloy
  pipes with antechambers. (2000 m)
HER arc section:
  Present copper beam pipes are reused.
  Since the HER energy is reduced from 8.0 to 7.0 GeV,
  SR power at normal arc section is more or less the
  same as KEKB.
Wiggler section (both ring):
  Copper beam pipes with antechambers are used.
SR
Arc section (aluminum)
Wiggler section (copper)
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 9
by courtesy of Y. Suetsugu

## Slide 10: Beam pipe with antechamber
Features of new beam pipes with antechamber
  Small effect of photoelectrons, low beam impedance, low SR power density
  The cross section should fit to the existing magnets.
  Aluminum alloy is available for LER arc section due to low SR power. Copper is required for wiggler section and HER.
  NEG strips are installed in one antechamber isolated by the screen for RF shield. (arc section)
Feed-through
Screen
(Φ4mm、6mm pitch)
NEG strip
t6 mm
Q magnet
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 10
by courtesy of Y. Suetsugu

## Slide 11: Flange, Bellows and Gate Valve
Flange, bellows and gate valve applicable to antechamber scheme were also developed.
Bellows chamber
RF-shield (gate valve)
Gate valve
Cu-alloy flange (CrZrCu)
Al-alloy flange (A2219, A2024)
RF-shield (bellows)
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 11
by courtesy of Y. Suetsugu

## Slide 12: Countermeasures against Electron Cloud Effect
Electron cloud instability can be a serious problem for LER (e+)
  The threshold of electron density to excite the head-tail instability is 1.6×1011 e-/m3.
  By using these countermeasures, the average electron density on the order of 1010 e-/m3 will be obtained.
  Various mitigation techniques were evaluated at KEKB LER.
Sections | L [m] | L [ %] | Countermeasure | Material
Total | 3016 | 100 |  | 
Drift space (arc) | 1629 m | 54 | TiN coating + Solenoid | Al (arc)
Steering mag. | 316 m | 10 | TiN coating + Solenoid | Al
Bending mag. | 519 m | 17 | TiN coating + Grooved surface | Al
Wiggler mag. | 154 m | 5 | Clearing Electrode | Cu
Q & SX mag. | 254 m | 9 | TiN coating | Al (arc)
RF section | 124 m | 4 | (TiN coating +) Solenoid | Cu
IR section | 20 m | 0.7 | (TiN coating +) Solenoid | Cu or ?
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 12
by courtesy of Y. Suetsugu

## Slide 13: Electron cloud mitigation 1 Antechamber
Antechamber is effective to mitigation of photoelectrons which can be source of the electron cloud.
1/1284/3.07 (1284)
6~8 ns spacing
R = 4７ mm (Circular)
Vr = 30 V
Ph = 81015 Ph/s/m/ms
With
antechamber
Circular chamber
Effect of antechamber
~1/5
~1/100
Rough surface at the side wall (Ra 20) reduces the photon reflection.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 13
by courtesy of Y. Suetsugu

## Slide 14: Electron Cloud Mitigation 2 Solenoid Field
It was confirmed that the solenoid field at drift section (50 G) is effective to both photoelectrons and secondary electrons.
B = 0 G
B = 50 G
8/100/2 (800)
4 ns spacing
R = 47 mm (Circular)
<1/1000
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 14
by courtesy of K. Kanazawa

## Slide 15: Electron Cloud Mitigation 3 TiN Coating
TiN coating is effective to reduction of the secondary electrons.
It was confirmed that TiN coated surface has a same property irrespective of base material.
Al
Cu
Al + TiN
Cu + TiN
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 15
by courtesy of K. Kanazawa

## Slide 16: Electron Cloud Mitigation 4 Grooved Surface (in Bending Magnet)
B
  by L. Wang et al.
  Rt
  d
  (Roundness)
  (Depth)
  It was tested in KEKB and CesrTA.
  It is expected to reduce the electron density by factors.
  It can be formed by extrusion method.
  In SuperKEKB LER, it will be used with TiN coating.
  Grooved surface with TiN coating will be also adopted for positron damping ring.
Valley ：R0.1~0.12
Top ：R0.15
Angle：18~18.3°
Grooved surface in the bending magnet can reduce effective SEY structurally.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 16
by courtesy of Y. Suetsugu
Beam pipe (SuperKEKB LER)
Beam pipe (Damping ring)

## Slide 17: Electron Cloud Mitigation 5 Clearing Electrode (in Wiggler Magnet)
Clearing electrode attracts the electrons by electrostatic field.
  Very thin electrode was developed. (0.1 mm tungsten on 0.2 mm Al2O3)
  It was tested in KEKB and CserTA.
  It is expected to reduce the electron density around beam up to 1/100.
Electron density
Electrode (+)
L. Wang et al, EPAC2006, p.1489
+500 V
+75 V
0 V
  ~3kV/m
Antechamber
Beam channel
(f 90mm)
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 17
by courtesy of Y. Suetsugu

## Slide 18: Electron Cloud Mitigation 5 Evaluation on Groove and Electrode
Effectiveness of the grooved surface and the clearing electrode was evaluated at KEKB LER.
  TiN-coated
  flat surface
  Grooved
  surface
  (b~20)
  Clearing
  electrode
  1/6~1/10
  ~1/10
TiN
Groove
Clearing electrode
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 18
by courtesy of Y. Suetsugu

## Slide 19: TiN Coating Facility 1
We have to coat 1100 beam pipes within 2 years.
  TiN coating tests had been performed and the coating method was established.
TiN coating is done by a DC magnetron sputtering of Ti in Ar and N2 atmospheres.
  A Ti cathode rod (-400 V) is hung from the top on the center axis.
  Gases are supplied into the beam pipes uniformly though the Ti rod.
  Magnetic field (16 mT) is supplied by a solenoid coil.
Test stand
Mass Spectrometer
Ar gas (2.0 Pa)
N2 gas (0.5 Pa)
Ti Cathode Rod (-400 V)
16 mT
Solenoid Coil
Mass Flow Controller
Solenoid Coil’s Power Source
Discharge Power Source
Gauge
Gauge
Pumping System
Beam pipe
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 19

## Slide 20: TiN Coating facility 2
TiN coating facility for large-scale production are under construction now.
  5 vertical equipments for straight beam pipes.
  3 transverse equipments for bent pipes (of which one is test station).
  Two line of the beam pipes can be mounted side-by-side in one equipment.
  Beam pipe with a length up to 5 m can be coated.
  Combination of hot-air oven and circulators are adopted to avoid the trouble of having to cover and uncover the aluminum foils and insulators.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 20

## Slide 21: TiN Coating facility 3
magnetic field in solenoid coils
Target value
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 21

## Slide 22: TiN Coating facility 3
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 22

## Slide 23: TiN Coating facility 4
Coating test is about done.
  Coating on the beam pipes will be started in this month.
  1100 beam pipes will be coated within 2 years by this facility.
Now coating (view from the bottom)
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 23

## Slide 24: Construction works are undergoing now.
Fabrication of beam pipes:
  LER beam pipes are being made on mass production lines.
Baking of beam pipes (after coating):
  All beam pipes will be baked with a temperature up to 150 C at the laboratory before installation.
  To cope with the large number of beam pipes (1200), hot-air oven is used.
  Baking works started in April. (Output : 6-8 pipes/week at present)
Installation of beam pipes:
  Installation works will start in the second half of this year.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 24
by courtesy of Y. Suetsugu

## Slide 25: Summary
Construction works of SuperKEKB are going on now.
  Commissioning of SuperKEKB will start in the second half of FY2014.
Almost all LER and part of HER beam pipes become new.
  To cope with the electron cloud issues and heating problems, antechamber type beam pipes are adopted.
As the countermeasures against the electron cloud, various mitigation techniques are adopted.
  Solenoid field
  TiN coating
  Grooved surface
  Clearing electrode
TiN coating are done in KEK Tsukuba site.
  Coating facility are under construction now.
  Coating test is about done and coating on the beam pipe will start this month.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 25

## Slide 26: END
Thank you very much for your attention.
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 26

## Slide 27: Backup
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 27

## Slide 28: Backup
2012/6/6 ECLOUD’12 (the 5th electron-cloud workshop) @ La Biodola (isola d’Elba) Italy 28