## Slide 1: Laser driven ion beam for multidisciplinary applications at ELIMAIA beamline
Valentina Scuderi
on behalf of the ELIMED collaboration
IoP-ASCR, ELI-Beamlines Prague, Czech Republic &
INFN-LNS, Catania, Italy
European Advanced Accelerator Concepts Workshop
La Biodola, Isola d’Elba
24-30 September 2017

## Slide 2
Wide energy and fluence range
Small energy spread (quasi-monoenergetic beams)
Homogeneous transverse beam distribution
Shot-to-shot stability (energy and fluence)
Variable beam spot size
Full beam control (fluence and dose) with < 5% error
Possibility of in-air irradiation (e.g. bio-samples)
Use of different ion species (H, He, Li, C)
Typical user requirements
Applications of Laser-driven Protons

## Slide 3
ELIMAIA: a User Beamline

## Slide 4
1 PW 10 Hz repetition rate beamline
All laser amplifiers pumped by DPSSL technology:
High pulse-to-pulse stability, robustness, low maintenance, high level of automation, scalability to higher peak power and rep rate
Supplier: LLNL Collaborative effort of ELI-Beamlines on development of the PW compressor, PW diagnostics, control & timing systems
Planned to become PW workhorse of the ELI-Beamlines facility
L3
Laser system for ELIMAIA
High-Repetition-Rate Advanced Petawatt Laser System (HALPS) arrived on 06/09/2107 in 62 crates at ELI Beamlines
Installation starts this week!

## Slide 5
Laser system for ELIMAIA
10 PW kJ CPA laser: mixed Nd:glass providing spectral bandwidth for direct pulse compression to 150 fs
Nanosecond pulses with programmable temporal shape for sophisticated laser-plasma experiments
PW auxiliary beam for plasma probing
Possible future use as OPCPA driver for generation >10 PW power
Supplier: NE-EKSPLA (Texas) ELI-Beamlines co-develops 10 PW compressor + diagnostics + timing system
L4

## Slide 6
Advanced targetry R&D

## Slide 7
Ion Acceleration R&D
(energy, n. particle and beam quality)
Max. proton energy increment
Conversion efficiency increment
D. Margarone et al. PRL 109 (2012) 234801
D. Margarone et al. PRST 18 (2015) 071304
Exp at APRI-GIST: Scaling laws and improvement of proton beam spatial profile!

## Slide 8
p acc. from solid-H2 ribbon (ELISE)
(rep rate)
H2 target
CH2 target
Pilot experiment at PALS: preliminary test with a kJ laser
Only protons on TP spectrometer
Directional proton emission: 25 degrees cone aperture
Higher flux
D. Margarone et al. Phys. Rev X 6, 041030 (2016)
Laser and target:
• 600J
• 300 ps (FWHM)
• 1315 nm
• 3x1016 W/cm2
• 60 mm

## Slide 9
Beam-line development for laser-driven ion beams
Beam transport solutions
Diagnostics
Dosimetry

## Slide 10
  Beam transport and delivery of ions up to 60 MeV/n:
Tunability (deliver ion beams from 5 up to 60 MeV/u) with a controllable energy spread (5% up to 20%) and 106-1011 ions/pulse
Large acceptance
Flexibility to meet different User’s requirements
Acceleration, Collection & Diagnostics
Selection, Standard transport elements & Diagnostics
In air Dosimetry
&
Irradiation
ELIMAIA design: finalized

## Slide 11
Hybrid multi-array:
Inner Halbach trapezoidal sectors
2 external rectangular hybrid arrays
Outer diameter: 325 mm
36 mm magnetic bore
(3 mm shield + 30 mm net bore)
F. Schillaci et al., JINST 10 T12001 (2015)
Magnetic field features:
● 3 main magnetization directions
● Gradients: ≈ 100 T/m
● Gradient uniformity: < 2% @ R = 12 mm (80% bore)
● Integrated gradient uniformity < 0.3% @ R = 12 mm (80% bore)
Collection system: Permanent Magnet Quadrupoles

## Slide 12
PMQs optics test @ INFN-LNS
PMQ delivered last July @ LNS
p beam
2
1
4
3
60 MeV p optics characterization
Quad 1 out
Quad 2 out
Quad 3 out
Quad 4 out
2 mm
3.4 mm
17 mm
6.1 mm
2.8 mm
6 mm
0.8 mm
0.8 mm
3 mm
1 mm
6 mm
1 mm
2 mm
4.5 mm
18 mm
8 mm

## Slide 13
Selection system: energy selector
F. Schillaci et al., JINST 11 P08022 (2016)
30 mm collimator upstream and downstream (200 mm far from dipoles)
Variable slit aperture size
(4 to 20 mm)
Expected delivery @ INFN-LNS December 2017
Reference orbit
Path length: 3,17 m

## Slide 14
ELIMED beam-line diagnostics
Main diagnostics goals
Online
Energy spectrum
Flux
Shot to shot reproducibility
Repetition rate mode:
On line beam diagnostics based on TOF technique using Diamond and SiC detectors
2 m
9 m
TOF1
TOF2
TP

## Slide 15
First TOF results with high energy laser-driven proton beam

## Slide 16
TOF diagnostics test with the VULCAN PW laser @ RAL (UK)
VULCAN Laser parameters
Power: 1 PW
Intensity:1021 W/cm2
Energy: 650 J
Time pulse: 500 fs
Target: 25 um Al
Devices
Diamond detectors
CR39 nuclear track detectors
Thompson Parabola (TP)
Main goals:
Energy cut-off and fluence backward and forward direction
TOF procedure validation by comparing with CR39s and TP
Shot to shot reproducibility
V. Scuderi et al., JINST 12 C03086 (2017)
G. Milluzzo et al., JINST 12 C02025 (2017)
G. Milluzzo et al., JINST 12 C03044 (2017)

## Slide 17
TOF diagnostics test with the VULCAN PW laser @ RAL (UK)
pCVD@122 cm +50 um Al filter
TP p energy distribution
2.6*1011
3.3*1011

## Slide 18
SEM
Multi-gap chamber
Irradiation system
Faraday cup
On-line relative dosimetry
Absolute dosimetry
and sample irradiation
Test bed @ INFN-LNS with
“conventional” ions (cyclotron)
ELIMED dosimetry
In air final section of the ELIMED beam line

## Slide 19
ELIMED FC test @ LOA
Test dosimeter response
(SEM, IC and FC) with laser-driven protons @ LOA:
High rep-rate
INFN-LNS PMQs prototype (focusing up to 30 MeV)
to enhance the dose delivered

## Slide 20
band-width filters
900 MHz
600 MHz
100 MHz
Fighting the EMP
≈ 108 p

## Slide 21
Summary and perspectives
New targetry for the user beamline ELIMAIA
PMQ collection system travelling to ELI next month
Energy selector chicane expected to be tested and delivered by March 2018
On-line TOF based diagnostics ready for high energy and high rep-rate
Absolute and relative dosimetry device characterization with laser-driven ion beams

## Slide 22
Thank you for your attention
INFN:
Attili Andrea, Amico Antonio, Cirrone Pablo, Cuttone Giacomo, Giordanengo Simona, Larosa Giuseppina, Leanza Renata, Manna Rosanna, Marchetto Flavio, Milluzzo Giuliana, Petringa Giada, Pipek Jan, Romano Francesco, Russo Antonio, Sacchi Roberto, Vignati Anna
ELI-Beamlines:
Georg Korn, Daniele Margarone, Andrey Velyhan, Lorenzo Giuffrida, Filip Grepl, M. Zakova, J. Psikal, F. Schillaci, V. Scuderi, P. Lutoslawski, S.V. Bulanov