## Slide 1
Kévin PEPITONE
Status of the Electron source and transfer lines for the AWAKE Experiment at CERN

## Slide 2
Acknowledgement
CERN:
Jeremie BAUCHE
Marzia BERNARDINI
Chiara BRACCO
Alan CHAUCHET
Heiko DAMERAU
Steffen DOEBERT
Eric CHEVALLAY
Nicolas CHRITIN
Stephane CURT
Cédric DELORY
University of Lancaster:
Robert APSIMON
Cockcroft institute:
Graeme BURT
University of Manchester:
Oznur METE
Triumf:
Victor VERZILOV
AWAKE Collaboration
CERN colleagues
Valentin FEDOSSEEV
Florence FRIEBEL
Frédéric GALLEAZZI
Edda GSCHWENDTNER
Lars JENSEN
Lucia MARICALVA
Stefano MAZZONI
Ans PARDONS
Janet SCHMIDT
Lars SOBY
UCL:
Fearghus KEEBLE

## Slide 3
Motivations
presented by K.Lotov at 11th AWAKE Physics Board Meeting, CERN 26.06.2015
Preliminary

## Slide 4
The AWAKE Experiment
Laser room
Klystron
Proton beam-line
Electron beam-line
Plasma cell
e-

## Slide 5
Awake electron beam
Parameters | Values
Beam Energy | 16 MeV
Energy Spread (rms) | 0.5 %
Bunch Length (σ) | 4 ps
Synchronisation (laser/RF) | 0.1 ps
Synchronization to experiment | 0.1 ps
Repetition Rate | 10 Hz
Spot Size (rms) | 250 µm
Normalised Emittance (rms) | 2 mm mrad
Nominal Bunch Charge | 0.2 nC
From a photo injector with:
Cs2Te cathode
QE = 12 %
Φw = 4.66 eV

## Slide 6
Instrument | How many | Resolution | Who
Electron line and instruments
BPMs 7 50 um Triumf
Faraday Cup 1 10 pC Triumf
Pepper-pot 1 < mm.mrad Manchester
BTVs for transverse profile 2 ~20 um CERN
FCT 1 10 pC CERN
+ a spectrometer
Proton beam
Electron beam
Laser beam

## Slide 7
Electron beam dynamics
Parmela simulation with r= 0.5mm, E=100 MV/m, Q=0.2 nC
 e = 1.3 mm mrad
(cm)
(cm)
(cm)
(cm)

## Slide 8
Electron line
Laser line
Electron source
Diagnostics and booster structure
Transfer line

## Slide 9
Electron line
Laser line
Waveguides

## Slide 10
Modulator Klystron Waveguides
1.2 Tons 700 L of oil
Power
supplies
Modulator
Control
Klystron tank
and
retention box
Klystron
Oil tank
PFN
PS cabinet
Control
cabinet
Interlocks rack
LLRF rack
Waveguides
RF parameters | Unit | Value
RF frequency | MHz | 2997.9
RF peak power | MW | ≈40
Pulse length (FWHM) | µs (max) | 3
Beam current | A | 360
Maximum repetition rate | Hz | 10
HV Parameters | Unit | Value
Voltage (max) | kV | 42
Current (max) | kA | 5.4
Capacitor | nF | 28 x 25
Inductance | µH | 28 x 0.8
Impedance | Ω | 5.5-6
Pulse length (FWHM) | µs (max) | 3
Maximum repetition rate | Hz | 10
Oil (Shell Diala B) | L | ≈700
Pulse transformer turn ratio |  | 1:15
Average charging capacitor rate | kJ/s | 3

## Slide 11
First BPM and Pepper Pot
Beam emittance measurement

## Slide 12
Booster structure
To be conditioned
Constant gradient 2/3 travelling wave structure at 2.99855 GHz
30 cells is just under 1 metre long
9.6 MW input power gives 15 MV
Average group velocity is 1.23% c. The filling time is equal to 273 ns

## Slide 13
BPM and Faraday Cup
BPMs, Faraday Cup and electronics installed
Beam position monitor, tested on CLEAR
Absolute measurement of charge

## Slide 14
BTVs and Beam stopper
2 screens:
  Chromox
  Ag coated Si (OTR)
Software for 10 Hz operation

## Slide 15
Spectrometer

## Slide 16
Summary
Electron beam commissioned by December 2017
Installation of the electron source took place in 2017
Installation will be finished by the end of October
RF conditioning, installation of a Cs2Te cathode and then laser tests
Commissioning of the electron source and commissioning of the electron line to the plasma cell entrance (with electrical and optical measurements)
Experimental results of the AWAKE experiment
September 2019
4th EAAC workshop

## Slide 17
Thank you for your attention