## Slide 1: Gas Detectors at LNF: What Next ?
LABORATORI NAZIONALI DI FRASCATI
www.lnf.infn.it
M. Antonelli, G.Bencivenni, L. Benussi, S. Bianco, P. Ciambrone, G.Felici, F. Murtas, D.Piccolo, M.Poli Lener, B. Ponzio

## Slide 2: OUTLINE
The Gas Detectors tradition at LNF
The Micro-Pattern Gas Detectors (MPGDs)
Gas Detectors Infrastructures at LNF
External Collaborations
Proposal for a MPGD-PCB Workshop

## Slide 3
The Gas Detectors tradition @ LNF (I)
Few examples concerning the past experience on gaseous detectors in our laboratory:
Plastic Streamer Tubes (1978): installed in various experiments, NUSEX, ALEPH, MACRO, but also in other LEP experiments
(Delphi, OPAL) and SLD
Large Volume Drift Chamber: for the KLOE experiment (1994)
the biggest DC ever built and still in operation
Straw tubes tracking detector (1994 – 2005): for the FINUDA, BTeV(R&D) and PANDA experiments

## Slide 4
The Gas Detectors tradition @ LNF (II)
Resistive Plate Counters: for the OPERA experiment (2002 – 2014),
BABAR, CMS
The MDTs for the ATLAS muon spectrometer
The MWPCs for the LHCb muon apparatus;
toolings for MWPC construction still in
operation for the upgrade of the experiment

## Slide 5: Pros & Cons of Classical Gas Detectors
Wire detectors:
  large area at moderate costs
  large wire spacing (of the order of few mm)  limited position
  accuracy and modest two-tracks resolution
  positive ion buildup (space charge effects):
    limited rate capability: O(100 kHz/cm2 )
Parallel plate devices (RPC):
  very large area covering at very moderate costs
  good time resolution: 1ns (single gap); <100 ps (multi-gap)
  low rate capability: O(kHz/cm2)
105 Hz/cm

## Slide 6: The MPGDs

## Slide 7: The MPGDs (I)
MPGDs have been just introduced to overcome these limitations.
The first device of this family was invented in the 1988 by Oed,
the Micro-Strip Gas Chamber (MSGC):
the amplification elements, replacing the “wires”, are very thin (down to 10 m) metallic strips with a pitch of the order of a few 100 m
the micro-strips are etched, using photolithography, to realize a pattern of alternating anode and cathode on a insulating substrate (glass, FR4); a drift electrode plane closes the device, defining the gas gap
A. Oed, NIMA 263(1988) 351
200 m
Drift electrode
MSGC substrate
alternating anode/cathode pattern
electric field values at the edge between insulator and strips lead to discharges  damages;
later (~ 1999-2000)solved with passivation of the cathode edges

## Slide 8: The MPGDs (II)
Others MPGDs have been introduced after MSGCs in the following years. All realized by means photolithography technology, on rigid or flex substrates, the same used for standard PCBs. The two most important micro-structures are:
Micromegas (Micro-MEsh Gaseous Structure) have been invented in the 1996 by Y.Giomataris and G. Charpak.
A parallel-plate chamber where the amplification (up to 105) takes place in a thin gap, separated from conversion region by a fine metallic micro-mesh, supported by 50-100 µm insulating pillars. Charge is collected on the anode readout board, a suitable segmented standard PCB.
The GEM (Gas Electron Multiplier) has been invented in the 1997 by F.Sauli [NIM A386 (1997) 531].
The GEM foil, is a thin (50 μm) metal coated kapton foil, perforated by a high density of holes (70 μm diameter, pitch of 140 μm).
By applying 400-500 V between the two copper sides, an electric field as high as ~100 kV/cm is generated into the holes which act as multiplication channels for electrons produced in the gas by an ionizing particle.
Gas gain up to 104 and safer working conditions are obtained by cascading three GEM foils.

## Slide 9: The MPGDs (III)
Many other MPGD architectures have been successively introduced for different fields of applications in basic and applied researches (tracking, TPC,
single-electron detection and cryogenic devices):
GEM derived
MM derived
Hybrid/novel architectures
MHSP
COBRA
Glass
GEM
THGEM (Trieste)
Re-GEM: electrodes by resistive kapton
Microbulk:
Low material
budget,
radioactive pure
Piggy Back: read-out separated
from the active volume
Timepix chip + SiProt + Ingrid
MM w GEM pre-amplification
GAS PMT
mPIC
GRIDPIX

## Slide 10: MPGDs in the world (RD51)
    A large fraction of these micro-structures are realized by the CERN PCB-Workshop (lead by Rui de Oliveira):
    Small area production  of the order of 100 devices/year.
    Large area “mass production”  COMPASS, LHCb, TOTEM, KLOE, CMS (GEM) + ATLAS (MM)
The MPGDs community, in 2009, decided to converge their own R&D efforts in a very fruitful collaboration: RD51.
RD51 aims at facilitating the development of advanced gas-avalanche detector technologies and associated electronic-readout systems, for applications in basic and applied research.
~ 500 Collaborators
80 Institutes
30 Countries
Micromegas
GEM
THGEM
MHSP
Micro-PIC
Ingrid
see Rui de Oliveira talk
11 INFN sections

## Slide 11: MPGDs @ LNF (HEP applications)
The LHCb-LNF group (in coll. Cagliari) started a pioneering work
on GEM in the 2000. LHCb has been the first LHC experiment
to use GEM detectors (24 GEM chambers)
Cylindrical-GEM Inner Tracker (4 layers) for the KLOE experiment;
BESIII- LNF (+ Ferrara & Torino) is developing a similar detector for
the upgrade of the IT of their experiment
more recently:
The CMS GEM upgrade project: LNF is one GE1/1 assembly site,
where 20 large area GEM chambers (~ 130x50 cm2/chamber)
will be produced (the 2nd assembly site is BARI)
The ATLAS-LNF is involved in the New Small Wheel upgrade
where large area Micromegas ( 128 chambers, 2 – 2.5m2)
will be installed (@ LNF 30 % of the global production –
RM1,RM3, Na, Le, Pv, Cs)

## Slide 12: MPGDs @ LNF (applied research)
GEM detectors (developed at LNF by F. Murtas - GEMINI, BEAM4FUSION, INFN-E, ARDENT) have been used in several fields of applied research:
Neutron detection, conversion on Boron coated cathode (good candidate for He3 detector replacement):
  Imaging capability
  good time resolution (5 ns),
  high gamma rejection (>105)
  high rate capability O(10 MHz/cm2)
  good spatial resolution O(1mm)
Medical applications with triple-GEM and GEMPIX :
  2D Beam monitor for daily quality check at CNAO
  3D energy relased measurement in water phantom (Bragg peak finder)
  Beam monitor in radiotherapy at Pol. Tor Vergata
GEMPIX, a triple-GEM with Timepix chip (50 x 50 m pixels) readout :
  3D particle track reconstruction with O(100 µm) space resolution
  Very Low flux : Radioactive waste and microdosimetry
  Very High flux : Burning Plasma monitor at Tokamak
12

## Slide 13: Infrastructures for gas detectors @ LNF

## Slide 14
    Clean Rooms for detector construction
Clean rooms (globally > 300 m2) with different class (100  10000) equipped for gas detectors construction and quality tests are available at LNF (ATLAS, BESIII, CMS, LHCb – MWPC, LHCb-GEM, PANDA …)
Optical System
HV tests of MPGD components
in controlled atmosphere
vacuum assembly/gluing system
laser tracking system (AD)
Notes: Foto camera pulita ASTRA

## Slide 15
Detector Test Facilities
(BTF, , X-rays, CR-stands, new Radiation Facility, …)
DDG –X-ray test facility (5.9 keV):
test LHCb-GEM, KLOE-IT, MSGC, R-WELL
Cosmic ray stand (GEM – based)
test KLOE-IT, BESIII-IT
X-Y movable - 137Cs 0.661 MeV -  source test LHCb-MWPC
Cosmic ray stand (MDT – based)
test ATLAS Micromegas
MM microTPC
BTF parameters | 
Energy Range | 25-750 MeV e-/e+
Repetition Rate | 1-50 Hz
Pulse Duration | 1.5 - 40 ns
Particles/Pulse | 1 to 1010 particles
Notes: Foto HUT ASTRA
Slide BTF

## Slide 16: Collaboration with LNF Services
Electronic Workshop (SEA)
  PCB design and development (analog, digital or mixed) for detector and electronics
  Circuit simulation
  Electronics for detector prototyping
    Front-end electronics (amplifier, analog filter, discriminator, …)
    Readout electronics (ADC, TDC, digital filter, FPGA or μcontroller based)
    Power supply (High and Low voltage, linear or switching)
    Custom measurement devices (voltage, current, …)
  Custom automatic equipments and tools for detector development
Mechanical Design Service (SPAS)
  mechanical design of detectors for both large experiments and R&D prototypes
Mechanical Workshop (SPCM)
  construction & assembly of large support structures for detector apparatuses
  3-D printing prototyping of mechanical items
  metrology w/3-D machine

## Slide 17
External Collaborations

## Slide 18
MOIRE` INTERFEROMETRY
FBG OPTOSENSORS
DGEM=(3.3 ± 0.1)10-­‐10 cm2/s
Sapienza and ENEA associates of the CMS Frascati group are interested in a MPGD Lab
Materials characterization, testing and certification
(Opto)electronic Sensors for T, RH, gas contaminants, planarity monitoring
SEM, XRD, etc
microanalysis
Materials & Optosensors (external collaboration)
Collaboration with Sapienza (Materials Engineering Dept.) and ENEA Frascati: Deformation monitoring and characterization of GEM films

## Slide 19
Proposal for a MPGD-PCB Workshop

## Slide 20: MPGDs: the course (I)
In spite of the extremely relevant recent progress in the field of MPGDs, dedicated R&D studies are needed to go forward:
the ultimate performance of MPGDs:
    Time and space resolution, rate capability, very high gain for single electron detection (PMT – MPGDs based)
high reliability & simplified construction technologies, a MUST for
    very large scale applications in fundamental research
    technology dissemination beyond HEP

## Slide 21: MPGDs: the course (II)
  A large number of innovative architectures can be proposed:
    GEM-derived
    MICROMEGAS-derived
    Hybrid structures
  … requiring for new PCB substrates and fulfilling …
    compactness (diffusion reduction)
    simple implementation of the amplification element  easy detector construction/assembly (no stretching)
    resistive coupling (spark suppression)
    finely segmented readout (high space resolution)
    multi-μgap (high time resolution)

## Slide 22: Proposal for a MPGD-PCB Workshop
A new infrastructure for gas detector R&D devoted to the prototyping of substrates for new MPGD architectures:
 the MPGD-PCB Laboratory (MPGD-PCB-LAB)
Goal:
    small/medium size (max size 60x60 cm2)
    single/multi - layer PCB (MM like),
    flexible structures (GEM like)
    hybrid architectures
    with resistive deposition (screen printing, sputtering … )
  NO mass production
  INFN internal market (+ … ???)

## Slide 23
The technology: photolithography
Base material
(substrate + metal)
Photoresist deposition
UV photoresist exposure
through a mask
Photoresist development
Metal etching
Photoresist stripping
performed in a medium class dark/clean room
flex or rigid substrate
chemical baths acid waste disposal

## Slide 24
Photolithography process steps (I)
Gerber File  CAD/CAM processing
data export for CNC drilling/routing machine
photo-plotter for masks
electric test
Base material preparing
cut to size
polishing
washing
drying
Reference hole & vias drilling
reference holes for alignment
vias for electrical contact (for multi-layer)
drilling/milling machine
polishing machine
CAD/CAM processing SW
oven

## Slide 25
Photolithography process steps (II)
Photoresist dry lamination (dark/clean room)
Application of a photoresist dry film on the base material
UV exposure (dark/clean room)
Image transfer from the mask to the photoresist by UV exposure
Photoresist development (dark/clean room)
and removal of non polymerized photoresist
UV exposure unit
Hot roll dry laminator
photoresist developer

## Slide 26
Photolithography process steps (III)
Metal etching
Copper etching machine
Kapton etching

## Slide 27
Machines for additional processes
Resistive paste deposition by screen printing technology
screen printing machine
Pressing process for multi-layer rigid/flex PCBs
pressing machine

## Slide 28
MPGD-PCB Workshop set-up (preliminary estimate)
2 – 3 staff to be trained at CERN
100-150 m2 area needed with at least 30-40 m2 dark/clean room
required investment :  500 kCHF

## Slide 29
INFN sections(**) involved on MPGDs development
- pioneering groups: Pisa*, LNF*, Cagliari*, Trieste*
- 2nd generation: Bari*, Milano-Bicocca*, Siena*,
Genova, Roma1*,Roma3*, Napoli,* Ferrara, Pavia, Lecce, Cosenza, Torino*, ISS*
- EOI: Bologna, Catania
17 -19 groups from INFN Sections:
  * INFN sections in RD51
In particular:
11 INFN sections (those labelled with “*”) are directly involved in the RD51 activities.
5 INFN groups (Bari, Bologna, LNF, Roma3, Trieste) are also involved in AIDA2020: WP “JRA1 Innovative Gas detectors”.
From 3 INFN sections, Bari, Trieste and Frascati, there was an initial proposal for AIDA2020 for a “Distributed Infrastructure for MPGD Development”, covering the know-how on many of the classical MPGD technologies (GEM, THGEM, MM) and associated Electronics.
(**) to the best of knowledge !!!

## Slide 30
Summary
Very long tradition in gas detectors R&D and construction
Consolidated know how in the advanced technology of MPGDs in the Excellence Science & Applied Research
Specific infrastructures of excellent quality already existing
Large potential of R&D in the fast growing field of MPGDs
Potential INFN users already working or starting to work on MPGDs
We propose a new infrastructure for the manufacturing of PCBs for innovative MPGD substrates
In full synergy with the PCB-Workshop at CERN (see de Oliveira talk)

## Slide 31
Spares Slides

## Slide 32
The RPC of the OPERA experiment (2002 – 2015)
HPT
XPC
RPC sketch
OPERA RPC system in numbers:
Total surface of the system ~ 3200 m2
Number of digital electronics channels ~ 28000
Number of chambers ~ 1000
Operated from 2006 to 2012 with moderate aging
Measured underground rate: 20 Hz/m2
Contribution to OPERA analyses
speed precision
re-measurement
candidate event
Notes: 1 Slide RPP CMS

## Slide 33
The Glass Spark Counters: the glass electrode version of RPC
developed in Frascati, used as veto counter in OPERA – C.Gustavino;
for the ALICE-TOF – as MRPC version by C. Williams;
in the BELLE Calorimeter …
ALICE TOF MRPC (1995-96)
GSC at LNF (1990-91)
Notes: Citare Gustavino

## Slide 34: MPGDs @ LNF (CMS)
The CMS GEM Upgrade project
Phase 2 LS3
Station GE2/1: 20 degrees precision chamber up to η=2.45 to improve trigger momentum selectivity & reconstruction (same GE1/1 technology)
To be installed in Phase1 LS2
GE1/1: precision chambers to improve trigger momentum selectivity and reconstruction and triggering Phase2
Phase 2 LS3 GEM ME0 module to provide muon tag in highest η region w/ 10-20 kHz (needs R&D of GEM technology)
GE1/1
GE2/1
ME0
LNF is one GE1/1 assembly site
Total number of chambers to be produced @ LNF = 40
Chamber with a size ~ 130x50 cm2

## Slide 35
Electronic Workshop (SEA)
  Skill:
    PCB design and development (analog, digital or mixed) for detector and electronics
    Circuit simulation
    Electronics for detector prototyping
      Frontend electronics (amplifier, analog filter, discriminator, …)
      Readout electronics (ADC, TDC, digital filter, FPGA or μcontroller based)
      Power supply (High and Low voltage, linear or switching)
      Custom measure equipment (voltage, current, …)
    Custom automatic machineries and tools for detector development
  Equipments
    Electronic CAD
      Altera: QuartusII
      Cadence: Combined IC & Systems Package ; RF SiP and Digital SiP
      Dolphin integration: Smash
      Mentor Graphics: full suite
      Synopsys: Combined FEV & Implementation
      Xilinx: ISE Design Suite
  list of major achievements
    LHCb
      GEM foil design for M1 detector
      Serializable HV power supply for GEM detector
      HV didtribution with integrated filter for M1 GEM detector
      LV system for M1GEM detector
    KLOE2
      Large area GEM detector development
      Design of readout strips and GEM foil for the inner detector prototype
      Design of frontend electronics for prototype studies
      Development of front end custom chip for the inner detector
      Development of readout electronics
    IMAGEM, Gemini, Amadeus
      Small triple-gem detector development (detector + readout electronics)
      Anular GEM detector for DAFNE luminosity monitor
      GEM TPC prototype
Synergies: SEA
FE electronics
Anular GEM detector
TripleGEM detector
GEM foil and readout strip
HV & LV for GEM detector
Large area GEM detector
TPC-GEM detector
Readout electronics

## Slide 36
L’IDEA INIZIALE

## Slide 37: Un esempio di utilizzo dell’infrastruttura tecnologica: il consolidamento tecnologico THGEM a TS
Polishing and Cleaning
polishing (Pumice Powder)
ultrasonic bath (~1 h) @ 50-60 oC in Sonica PCB
Initial: 50-60% Paschen curve
Final: > 90% Paschen curve
GAIN
Max/Min
= 2.9
GAIN
Max/Min
= 1.6
Selecting uniform fiberglass plates
GAIN & THICKNESS
Gain map
Effiency map