## Slide 1: Supermicro New Generation HPC Solutions
INFN Workshop May 2017
Gian Luca Meroni Enzo Romeo Marro

## Slide 2: Outline
New CPU Generations
High Performance Server Products
  Compute Server
  Accelerated Computing
High Performance Network
Administration- and Management Networks
Scalable Parallel Filesystem
Success Story

## Slide 3: New CPU Generations Intel Skylake
Notes: We are starting with new servers developments, as said before I will limited myself to HPC related products

## Slide 4: Broadwell and Skylake Comparisons
Spec | Grantley with Broadwell-EP CPU | Purley with Skylake CPU
CPU TDP (with IVR) | 55-145W, 160W WS only | 45-205W
Socket | Socket R3 | Socket P
Scalability | 2S | 2S, 4S, 8S
Cores | Up to 22C with Intel® HT Technology | Up to 28C with Intel® HT Technology
Memory | 4 channels DDR4 per CPU RDIMM, LRDIMM | 6 channels DDR4 per CPU RDIMM, LRDIMM
 | 1DPC=up to 2400, 2DPC= up to 2400, 3DPC=up to 1866 | 2133, 2400, 2666 2DPC No 3 DPC support
Intel® UPI | Intel® QPI: 2 v1.1 channels per CPU 9.6 GT/s max | UPI: 2-3 channels per CPU (9.6, 10.4 GT/s)
PCIe* | PCIe* 3.0 (2.5, 5.0, 8.0 GT/s) | PCIe* 3.0 (2.5, 5.0, 8.0 GT/s)
 | 40 lanes per CPU | 48 lanes per CPU Bifurcation support: x16, x8, x4
PCH | Wellsburg: DMI2 – 4 lanes; Up to 6xUSB3, 8x USB2 ports, 10xSATA3 ports; GbE MAC (+ External PHY) | Lewisburg: DMI3 – 4 lanes; 14xUSB2 ports Up to: 10xUSB3; 14xSATA3, 20xPCIe*3 New: Innovation Engine, Integrated Intel® Ethernet 4x10GbE ports, Intel® QuickAssist Technology
AVX |  | AVX512 Support
Notes: Important new features: 6x 2666MHz Memory speed (1.66x memory speed) and AVX512 (2x Peak Performance)

## Slide 5
New Brand and Processor Number scheme starting with Skylake-SP processor
The family will be referred to as the Intel Xeon Processor Scalable Family
The Intel® Xeon® processor Scalable family will have 4 named shelves – Platinum, Gold, Silver, Bronze - that signal increasing capability as you move from Bronze to Platinum level SKUs
Introducing the New Intel Xeon Scalable Processor Family
Processor Generation
1 = 1st Gen (Skylake)
Processor SKU
(ex. 20, 34…)
Integrations and Optimizations
(if applicable)
P = FPGA
F = Fabric
T = High Tcase/Extended Reliability
Memory Capacity
No Suffix = 768GB per socket
M = 1.5TB per socket
SKU Level
8 = Platinum
6, 5 = Gold
4 = Silver
3 = Bronze
Intel® Xeon® Platinum
8
1
#
#
Intel® Xeon® Gold
5
1
#
#
6
1
#
#
Intel® Xeon® Silver
4
1
#
#
Intel® Xeon® Bronze
3
1
#
#
processor
processor
processor
processor
processor
Intel® Xeon® Gold
a
a
a
a
a
a
a
a
a
a
Notes: New Naming scheme

## Slide 6: New CPU Generations AMD Naples
Notes: We are starting with new servers developments, as said before I will limited myself to HPC related products

## Slide 7: AMD Naples Processor Spec
Lowering TCO through an optimal balance of compute, memory, I/O and security
  COMPUTE
  16 to 32 AMD “Zen” x86 cores (32 to 64 threads)
  512KB L2 cache per core (16 MB total L2 cache)
  64MB shared L3 cache (8MB per 4 cores)
  TDP range: 120W-180W
  MEMORY
  8 channel DDR4 with ECC up to 2666 MHz
  RDIMM, LRDIMM, 3DS, NVDIMM, Flash
  2 DIMMs/channel capacity of 2TB/socket
  SECURITY
  Dedicated Security Subsystem
  Hardware Root of Trust-ability to run certified (signed) firmware
  INTEGRATED I/O – NO CHIPSET
  128 lanes PCIe Gen3
    Used for PCIe, SATA, and Coherent Interconnect
    Up to 32 SATA or NVMe devices
  Server Controller Hub (USB, UART, SPI, LPC, I2C, etc.)
PCIae3
SATA3
10GbE
Server Controller Hub
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
512k
L2
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
512k
L2
Zen Core
Zen Core
512k
L2
Zen Core
Zen Core
8M L3
512k
L2
512k
L2
512k
L2
8M L3
DDR4 Memory Controllers
AMD Secure Processor
COHERENT INTERCONNECT
Notes: Important Features: 8x 2666 MHz Memory Speed (25% more than Skylake) and 128 PCI Lanes. In case of Dual CPU, 64x PCI Lanes go to interconnect, such that 2x 64 PCI lanes are available

## Slide 8: H11 Server A+ Product Family
Product Family
Ultra Architecture 1U & 2U Ultra systems Optimize Thermal design & Flexible I/O
Twin Architecture The original Twin architecture innovator
WIO Platform Resource optimized systems
GPU Optimized Solutions Full line of GPU vs Nvidia / AMD
UP Systems UP Mainstream, Storage systems
GPU optimized
Ultra Server
WIO
Big Twin
UP Systems
Notes: We are supporting different server family. HPC relevant are BigTwin and GPU server

## Slide 9: HPC Server Models Compute Server
Notes: We are starting with new servers developments, as said before I will limited myself to HPC related products

## Slide 10: 2U TwinPro2-SIOM
Node 1 Node 2 Node 3 Node 4
Individual power control
2000W Redundant PSU Titanium Level
Dual CPU
16 DIMMs
SIOM
 | 3.5” drives | 2.5“ drives
SAS3 3108 | √ | √
SAS3 3008 | √ | √
SATA | √ | √
Available SKUs:
2.5” drives x6 / Node
3.5” drives x3 / Node
1x PCI-e x8
1x PCI-e x16
4 node in 2U rackmount space
Notes: TwinPro for Broadwll and Skylake.

## Slide 11: SIOM - Supermicro Super I/O Module
AOC-MTG-i4S
Quad port 10G (SFP+)
Intel XL710-AM1 controller
AOC-MTGN-i2S
Dual port 10G (SFP+)
Intel 82599ES controller
AOC-MGP-i4T Quad port 10G (RJ45)
Intel X550 controller
AOC-MH25G-m2S2T
Dual-port 25G SFP28
Dual-port 10G RJ45
AOC-MHIBF-m2Q2G
Dual-port FDR IB QSFP+
Dual-port GbE RJ45
Supermicro optimized flexible Networking for 1 -100 Gb/s
AOC-MGP-i2T
Dual port 10G (RJ45)
Intel X550 controller
Notes: Modules for HPC networks Omni-Path and EDR under development

## Slide 12: 2U BigTwin
  Each BigTwin Server Supports up to
  4 hot-swappable DP nodes in 2U
  24 DIMMs per node
  6 NVMe / SAS / SATA drives per node
  1 SIOM card support per node
  2 low-profile PCI-E x16 slots per node
  Redundant Titanium Level (96%) Power Supplies
  Intel Skylake or AMD Naples
BigTwin’s 96% Efficiency 2200W Power Stick Design
Notes: BigTwin supports Broadwell, Skylake and AMD Naples. 24x DIMM slot for Broadwell (3DPC*4 Channels) and Skylake (2DPC*6 channels).

## Slide 13: Supermicro Superblade Solutions
  Flexible Blade Solutions
  High Density
  10/14/20 Blade Nodes per Enclosure
  Compute-, GPU-, Storage Blade Options
  Integrated Networking
  Multiple Network Option (GbE, 10G, IB)
  Integrated Management Module
Notes: Broadwell and Skylake product lines

## Slide 14: 8-Way Server
CPU Module
Key features
7U 8/6/4 Way System Supports 8x E7-8800/4800 v3/v4
Up to 12TB DDR4 Memory Capacity
Up to 23x PCI-E 3.0 slots support
Up to 12x 2.5” hot swap SAS3 HDD
Up to 5x 1600W 80Plus Titanium Level Power Supply
Storage Module
SYS-7088B-TR4FT
Applications:
SMP, In-Memory Database, ERP, CRM, BI systems, Scientific Research Organizations, Virtualization
Notes: 8-socket system based on Broadwell EX CPUs. Skylake successor will follow.

## Slide 15: HPC Server Models Accelerated Computing
Notes: We are starting with new servers developments, as said before I will limited myself to HPC related products

## Slide 16: Intel KNL Processor
Highlights
Host Processor
  Linux and Windows support
  Socket P (LGA-3647)
Multiple SKUs available
  Up to 72 cores
  Up to 16 GB MCDRAM on package
  Option of integrated Omni-Path
Excellent power efficiency
  Exceeds 10 GF/W
  25% more efficient than discrete components
Cost efficiency over discrete parts
  No need for separate host CPU
  Integrated fabric vs add-on card
Xeon Phi x200 Processor
KNL Processor
KNL-F with dual port Omni-Path fabric
Workload | Compared to x100 | Compared to DP Broadwell
Core Performance Single Thread/Single Core | ~3x | ~1/3
Highly Parallel/Scalar Code Single Thread/Single Core | N/A | ~1/2
Highly Parallel/Vectorized Code SPEC_Int_rate and SPEC_FP_rate | ~2.5x | ~2.5x Higher
Memory Bandwidth “STREAM” Class | 2.5x (MCDRAM) ~1/2 (DDR4) | ~5x (MCDRAM) ~3/4 (DDR4)
Single Node Power Lower is Better | ~1/2x | ~3/4x

## Slide 17: Intel Knight’s Landing Twin² Server
SYS-5028TK-HTR
Density: Uses popular Twin architecture to achieve 4 hot-pluggable nodes in 2U
Processor support: Full range of KNL and KNL-F SKUs supported
Flexible I/O support: Integrated dual-port Omni-Path or two low profile PCIe 3.0 x16 slots
Key features
KNL / KNL-F Processor Support
Intel C612 chipset
6x DIMM slots with up to 384 GB DDR4 at 2400 MHz
2x PCIe 3.0 x16 LP slots (unavailable with KNL-F)
2x Intel i350 Gigabit Ethernet
3x 3.5” hot-swap SATA3 drive bays per node
2x SuperDOM support
2x Redundant 2000 W Titanium power supplies
Notes: Supermicro Twin Solution for Intel Knights Landing

## Slide 18: Intel Knight’s Landing Development Workstation
SYS-5038K-I
KNL / KNL-F Processor Support
Intel C612 chipset
6x DIMM slots with up to 384 GB DDR4 at 2400 MHz
2x PCIe 3.0 x16 LP slots (unavailable with KNL-F) and 1x PCIe 3.0 x4
2x Intel i350 Gigabit Ethernet or 2x Intel X540 10 Gigabit Ethernet
8x SATA ports, 2x SATADOM
750 W Titanium power supplies
Tower Form Factor
Quiet Operation (< 31 dBa under 80% load)
Self-contained cooling system for 215 W CPU
Key features

## Slide 19: High Density GPU Server
SUPERMICRO Value Proposition
● THROUGHPUT: Highest GPU Parallelism
● FLEXIBILITY: Enterprise or Active GPU
● RELIABILITY: 2+2 94% Efficiency Level PSUs
● BALANCED: Balanced GPU architecture
● DESIGN: No GPU preheating
APPLICATIONS:
MACHINE LEARNING TRAINING
RESEARCH
Key Features:
All GPUs and NICs under single CPU root
GPU Peer-to-Peer optimized architecture
GPU Direct RDMA support
Support up to 160W CPU
SYS-4028GR-TR2(T)
MAXWELL/PASCAL READY
Active/Passive GPU Support
Support latest Maxwell/Pascal GPUs
Distributed training across eight GPUs
Notes: New Layout of 4U GPU server: all GPUs + 2x network cards under same CPU, for improved communication latency.

## Slide 20: Nvidia NVLINK Technology
NVLINK
80 GB/s
NVLink
Interconnect at 80 GB/s
(Speed of CPU Memory)
Stacked 3D Memory
4x Higher Bandwidth – 1 TB/s
(2.5x Capacity, 4x more Efficient)
Unified Memory
Lower level of Development
(Available today in CUDA 6)
Stacked HBM
Memory 1TB/s
DDR4 Memory
50-75 GB/s
Unified
Memory

## Slide 21: Nvidia Pascal GPU P100
Notes: Significant acceleration and superior scaling for P100 GPUs in comparison to K80.

## Slide 22: Nvidia Pascal P100 SXM Server
PASCAL GPU READY
Performance – 10 TFLOPs FP32
NVLink – 5x PCIe
3D Memory - 2x Memory Bandwidth
SUPERMICRO ADVANTAGE
● PERFORMANCE: 4/8x PASCAL with GPUs
● NVLINK: 80GB/s High Bandwidth GPU Interconnect
● RDMA FABRIC: 4/8x Direct Low Latency Data Access
● EFFICIENCY: Titanium-rated Power Supply
● DESIGN: No GPU preheating
Notes: Supermicro has solutions for 4x and 8x P100 connected by NVLINK

## Slide 23: HPC Network
Notes: We are starting with new servers developments, as said before I will limited myself to HPC related products

## Slide 24: Supermicro Omni-Path High Performance Network
SSH-C48Q
  High Performance/Low latency
  100-Gigabit Omni-Path Architecture
  Meets most demanding HPC requirements
  Dual Power Supply
  Optional OOB management card
  48x 100Gb/s switching capacity
    1152 ports non-blocking in 2-level fabric
    1536 ports 2:1 blocking in 2-level fabric
  48x 100Gb/s switching capacity
SSH-C48Q
AOC-MHFI-i1C coming soon
  100Gbps link speed
  Single QSFP28 Connector
  PCI Express 3.0 x16
  Standard Low-Profile
  Scalable, low latency MPI < 1µs
  High MPI message rates (160mmps)
  100Gbps link speed
  Single QSFP28 Connector
  SIOM Form Factor
  Scalable, low latency MPI < 1µs
  High MPI message rates (160mmps)
Notes: SMC product portfolio for Intel Omni-Path. SMC propriatary switch (optionally managed), with dual PSU. HCA either as PCIe card or SIOM

## Slide 25: Omni-Path Integrated Fabric
Signal Pass-Through
Intel Fabric Through (IFT) Carrier Card
Intel Fabric Passive (IFP) Cable
CPU with integrated Fabric
Notes: For CPUs with integrated fabric, no OPA AOC is needed any more, only internal cable to server rear ports. The image is Knights Landing with dual OPA lanes, same setup will be used for Skylake with single OPA.

## Slide 26: Omni-Path or EDR?
Comparable Base Performance (Bandwidth, Latencies, Message Rates)
Comparable Application Performance
Achievable Sizes for 2-Level Fabric:
  Based on 36 port switch:
    648 ports non-blocking
    864 ports 2:1 Blocking
  Based on 48 port switch
    1152 ports non-blocking
    1536 ports 2:1 blocking
Connection to existing IB Networks:
  EDR is compatible to QDR/FDR
  OPA requires Gateway Servers
18x Spine
36x Edge
18x EDR
18x EDR
18x EDR
24x Spine
48x Edge
24x OPA
24x OPA
24x OPA

## Slide 27: GbE Networks

## Slide 28
Cumulus Linux NOS
Linux Ecosystem
SSE-G3648, SSE-X3648, SSE-C3632
Application
Operation
Consistent server/network provisioning
Data Center operation
Linux based network deployment
Notes: Supermicro new GbE Bare Metal Switch generation provides a flexible and cost effective solution for GbE data and management networks. The switches run a Linux OS inside, complemented by switching SW stack (e.g. Cumulus)

## Slide 29: 1Gb Ethernet Bare Metal Switch
48x RJ45 1G Ports
4x SFP+ 10G Ports
1x RJ45 Management Port
1x Console Port
Switching Capacity 176 Gb/s
Broadcom Helix4 Switch Chip
Wire-speed Layer 3 Routing
1:1 Non-blocking connectivity
Intel Rangeley CPU
ONIE installed
Compatible with Cumulus Software
Efficient, Hot-Swappable Power Supplies; optional second redundant PS available.
SSE-G3648B/BR

## Slide 30: 10Gb Ethernet Bare Metal Switch
48x SFP+ 10G Ports
6x QSFP+ 40G Ports
1x RJ45 Management Port
1x Console Port
Switching Capacity - 1440 Gbps
Broadcom Trident 2 Switch Chip
Wire-speed Layer 3 Routing
1:1 Non-blocking connectivity
Intel Rangeley CPU
ONIE installed
Compatible with Cumulus Software
Redundant, Efficient, Hot-Swappable Power Supplies (80 Plus-Platinum)
(SFP+)
SSE-X3648S/SR

## Slide 31: 40/100Gb Ethernet Bare Metal Switch
32x 40GbE/100GbE QSFP28 Ports
1x USB Port
1x RJ45 Management Port
1x Console Port
Full Duplex 3.2Tbps Switching Capacity
Broadcom Tomahawk Switch Chip
Wire-speed Layer 3 Routing
1:1 Non-blocking connectivity
Intel Rangeley CPU
ONIE installed
Compatible with Cumulus Software
Redundant, Efficient, Hot-Swappable Power Supplies (80 Plus-Platinum)
SSE-C3632S/SR

## Slide 32: Supermicro Lustre Storage Solution

## Slide 33: Software Defined Storage for Lustre
User Data
Object Storage Server (OSS)
User Data
Object Storage Target (OST)
Meta data
Meta Data Server (MDS)
Meta Data Target (MDT)
Compute Cluster
High Speed Network
Notes: Scalable and Parallel High Performance HPC File System. Dedicated Object and Meta Data server are connected via the highspeed network to the compute cluster

## Slide 34: Supermicro Lustre Solution Metadata Storage
MDS Configuration
Mirrored OS drive (HW RAID1)
Avago 9380-8e Syncro RAID
Highspeed Interconnect HCA
MDT Configuration
Shared 24 bay SAS3 JBOD
RAID 10 using SSD
RAID 10
Highspeed Interconnect
Highspeed Interconnect
Notes: Redundant Metadata configuration, employing two file servers in active/passive mode. Both servers access a SAS3 JBOD with SSDs in RAID10

## Slide 35: Supermicro Lustre Solution Object Storage
OSS Configuration
Mirrored OS drive (HW RAID1)
Redundant ITmode controllers
Highspeed Interconnect HCA
OST Configuration
90 Bay JBOD configured
8x RAIDZ2 parity groups + 2x hot spares
Highspeed Interconnect
Highspeed Interconnect
RAIDZ2 9+2
RAIDZ2 9+2
RAIDZ2 9+2
RAIDZ2 9+2
RAIDZ2 9+2
RAIDZ2 9+2
RAIDZ2 9+2
RAIDZ2 9+2
Notes: Redundant Object Storage Lustre Setup with two fileservers in active-active mode connected to a 90Bay JBOD with 8x RAIDZ 9+2 ZFS groups. Up to 720 TB usable per block, multiple blocks can be used. 7-8GB/s bandwidth per block.

## Slide 36: MDS Configuration based on SBB
Two Serverboards in Single Chassis with shared Storage
2x Dual Socket R3 (LGA 2011 up to 145W) supporting Intel® Xeon® E5-2600 v4 family
2x 16 DIMM, 1TB Reg. ECC DDR4 up to 2400MHz
2x High Speed network (via SIOM) Support
40x NVMe + 8x SAS/SATA
Node-to-Node Heartbeat
2000W Redundant Power Supplies Titanium Level (96%)
SSG-2028R-DN2R40

## Slide 37: Success Story
Notes: We are starting with new servers developments, as said before I will limited myself to HPC related products

## Slide 38: Supermicro Omni-Path Cluster
Supermicro RACK solutions team built a 570 node Super Computer for scientific research. Supermicro Super Computer is now in top 200 HPC World Wide list. The platform uses Intel 100Gbps Omni-path, Supermicro NVMe Drives with FatTwin solution.
The performance is exceeding 600 TFlop/s using Intel Xeon E5-2695 v4 (Counting 560 compute nodes, 20,160 physical cores)

## Slide 40
enzom@supermicro.com