## Slide 1
Dose enhancement and localisation by combining reduced mass targets and a pulsed solenoid for radiobiological effectiveness studies of laser accelerated protons
F. Kroll, T. Kluge, M. Bussmann, T. E. Cowan, T. Herrmannsdörfer, S. D. Kraft, J. Metzkes, R. Sauerbrey, B. Schmidt, U. Schramm, K. Zeil, M. Zier, S. Zherlitsyn

## Slide 2
Our motivation – Laser driven ion therapy
© GSI Darmstadt
Localised dose deposition for precise tumour treatment
Benefitial for 10-20% of patients
Conventional ion therapy
Large scale setup: accelerator, beam guidance & radiation shielding
Laser driven ion therapy
Proton number
Time
1 s
~1 ns
high acceleration gradients TV/m
compact source and laser beam transport
1010 to 1013 ions per pulse
Short ion pulses: fs to ps at source
Divergent, with broad energy spectrum
Facility Image courtesy by Stern, Gruner+Jahr AG & Co KG, Germany
Dose Image courtesy by O. Jäkel, DKFZ Heidelberg, Germany

## Slide 3
Translational research
Clinical practice
Translational research
Discovery
FaDu & SKX
p+ & e-
e-
Laser accelerator progress
Establish dosimetric protocols & cell lines
In vivo irradiation of animals
Clinical trials
In vitro cell irradiations
Clinical practice
Translational research in Radiobiology
Increase maximum proton energy
High particle beam intensity for short irradiation times
A stable, reproducible beam
Suitable field size and a homogeneous dose distribution

## Slide 4
In vivo irradiations with laser protons
*U. Masood, et al.
U. Masood, et al.
Gantry for laser-driven proton therapy
[4] T. Kluge et al., PRL 107, 205003 (2011)
Proton energy scaling
LULI
100 TW, 400 fs
Buffechoux et al., PRL 105, 015005 (2010)
Reduced mass targets
Notes: A possible setup for in vivo irradiations with laser accelerated protons
Use the increased particle number as well as the robust acceleration performance of RMT and transport the particles to the irradiation site

## Slide 5
New lab space (800 m2):
clean rooms – workshop – cell lab
Center for high power radiation sources
laser labs and target areas
MPQ München
HZDR Dresden
Berlin
Jena
Düsseldorf
GSI Darmstadt
DESY Hamburg
HSQ

## Slide 6
High power lasers
laser labs and target areas
Draco
flash lamp pumped
PW diode pumped system
M. Siebold, F. Röser, D. Albach, M. Löser
Yb:CaF2 active medium
150 J in 150 fs on target @ 1 Hz
Ti:sapphire active medium
500 TW ultra-short beam
15 J in 30 fs on target @ 1 Hz
Ti:sapphire active medium
150 TW ultra-short beam
max. 4.5 J in 30 fs on target @ 10 Hz
DRACO experiments

## Slide 7
In vivo irradiations with laser protons
✓

## Slide 8
TNSA from Reduced Mass Targets
TNSA at large foil
electrons laterally spread along the target surface
RMT
electron reflection at target edges
Te and ne increased
electron reflux  further heating
 increased proton energies

## Slide 9
Experimental Setup
Diameters: 20 – 100 µm
Thicknesses: 100 nm – 1 µm

## Slide 10
RMT – Results
Maximum energy gain of 87 %
Proton number increased by almost one order of magnitude
Time-averaged hotter, denser and more homogeneous electron sheath

## Slide 11
RMT – Results
Less pronounced thickness dependence for RMT
Robust against laser contrast fluctuation
 Compensation via electron reflux

## Slide 12
In vivo irradiations with laser protons
✓
✓

## Slide 13
Pulsed solenoid magnet
  ~ 21 T @ 24 kA (24 kV)
  Reliable operation
  Field tested in many LIGHT experimental campaigns
Vacuum tube
Current feed
Coil
Incoming
divergent beam
Air cavity
Transported beam
Steel housing
LASER
Efficient capturing of laser accelerated protons
≤ 21 T fields achieved (I ≤ 24 kA)
120 windings in 4 layers
Field rise time ≈ 500 µs

## Slide 14
Portable pulse generator
3rd generation portable pulse generator
-24 kV
Pulsed Magnet
Thyratron
2 ×165 µF capacitors
95 kJ max energy stored
~ 1 pulse/minute

## Slide 15
3 – Performance of the solenoid
RCF at different focus positions for 9.4 MeV protons
Courtesy of Simon Busold (TU Darmstadt) and the LIGHT collaboration
See also talk [40] by S. Busold, June 5, 16:50
1.07 m
1×109 protons
2.12 m
5×108 protons
20 % transport efficiency
Notes: Rechts: 7.79 T

## Slide 16
In vivo irradiations with laser protons
Profit from robust acceleration performance and enhanced proton number
Generation of localised dose distributions
Predicted dose per shot at mous ear at least 2× higher than in former studies
Notes: A possible setup for in vivo irradiations with laser accelerated protons
Use the increased particle number as well as the robust acceleration performance of RMT and transport the particles to the irradiation site

## Slide 17
Acknowledgement
2007-2012: 11.5 M€ (grant no. 03ZIK445)
20012-2017: 6.7 M€ (grant no. 03Z1N511)
+
Applied Optics and Precision Engineering
Friedrich-Schiller-
Universität Jena
=

## Slide 18
Acknowledgement

## Slide 19
Thank you for your attention
multiple filamentation of freely
propagating 100 TW beam in air

## Slide 20
Target edge & stalk effects

## Slide 21
Target edge & stalk effects
Stalk width [µm]
Max. proton energy [MeV]
Folie
Proton beam profiles,
E ≈ 9 MeV
Fields at target edges and stalks prevent efficient plasma expansion
Further investigations including 3D PIC simulations required