## Slide 1: H1 Squeezing Experiment: the path to an Advanced Squeezer
L. Barsotti (LIGO-MIT)
for the Squeezing Team
(AEI, ANU, CIT, LHO, MIT)

## Slide 2: Outlines
Why we are testing squeezing now?
H1 Squeezing Experiment Status
October 2010 (end of S6) – January 2012 (aLIGO H1 installation)
What are we going to do next?

## Slide 3: Why Squeezing?
Quantum noise
is everywhere!

## Slide 4: Why Now? You might need a squeezer sooner than you think
31 W + 6 dB of Sqz (10 dB of anti-Sqz, Total Losses ~ 20%)
Advanced LIGO sensitivity dominated by quantum noise (shot noise and radiation pressure noise)
With 6 dB of perfect squeezing:
need 4 time less power!
“RISK MITIGATION”
for high power
What about 60 W power + 3 dB squeezing?
Might be faster…

## Slide 5: Advanced Squeezing
Shape the quantum noise
by changing the sqz angle

## Slide 6: Even More Advanced
Frequency dependent squeezing:
beat quantum noise everywhere!

## Slide 7: H1 Experiment Goal: Design the aLIGO Squeezer
Inject 6 dB of squeezing at the asymmetric port of H1
Improve the sensitivity by 3 dB (due to losses) above 400 Hz
Understand the impact of squeezing at low frequency
Find/fix “technical problems”

## Slide 8: Squeezer Experiment Timeline
October 2010
June 2011
December 2011
* Back scattering?
* Losses?
* Anti-Squeezing?
* Control noises?
1) OPO Designed at ANU, squeezer assembled at MIT
2) Reassembling of
the squeezer at LHO
3) Sqz installation
4) Sqz injection with short Michelson and full IFO
August
2011
aLIGO H1 installation starting in January 2012
End of S6

## Slide 9: Squeezer Highlights
Oven/
Temperature
Sensor
Crystal
Squeezing
Out
Pump light In
PZT Actuator
ANU Design
Bow-tie cavity OPO:
less back scattered light than linear cavity
High quality optics:
low scatter, low losses
aLIGO electronics:
low noise, stable,
controllable remotely
aLIGO Electronics

## Slide 10: The Squeezer @ LHO
The OPO
Squeezing Lab in the LVEA

## Slide 11: The H1 Squeezer: Ready to Install
Squeezer laser locked to the H1 main laser
All loops closed:
  needed frequency actuator for the LO loop, not enough range with PZT mirror
1 hour lock last week
Working on making the squeezer fully controllable from the control room
Sample of H1 laser light

## Slide 12: Performance: 6+ db
As measured on the homodyne detector on the squeezer table
Total losses on the squeezer table ~ 20%

## Slide 13: A squeezed H1: By the end of August
June 2011
December 2011
August
2011
We are here
Unlocking of the optics started last week
High legs tested with dummy table
Preparing the squeezer
for the move in June
H1 taken apart

## Slide 14: Squeezing Injection
New Output Faraday (first aLIGO unit)
In-vacuum parts

## Slide 15: Things to worry about
Back Scattering
Mode Matching
Alignment
IFO Stability
…

## Slide 16: Back Scattering
Motion of the scattering surface
Power reflectivity of the scattering surface
HARD to ESTIMATE
IFO light to the squeezer and back to the IFO
Measured at ANU
(Conor’s talk)

## Slide 17: Back Scattering Noise
Motion of the scattering surface
Power reflectivity of the scattering surface
With 100 mW at the AS port and 2 Faradays in the sqz path

## Slide 18: Speculations on the Advanced Squeezer
Two directions:
  Reduce the light back to the squeezer
  (more Faradays, but Faraday=losses)
  Reduce the motion of the scattering surface (OPO)
Advanced LIGO HAM5
Output Faraday
Sqz Faraday
OPO

## Slide 19: Back Scattering Noise
Motion of the scattering surface
Power reflectivity of the scattering surface
With 100 mW at the AS port and 2 Faradays in the sqz path

## Slide 20: The Message
The H1 squeezer squeezes, and it is ready to be installed
Work with the interferometer:
    installation of the squeezer at the end of June
    first test with full IFO July/August
    short Michelson when conflicts with aLIGO arise
The current setup might be not optimal for aLIGO
and aLIGO+, the H1 experiment will give us an answer
We have a couple of years in front of us to build the aLIGO/aLIGO+ squeezer

## Slide 21: Thanks for your time

## Slide 22: Why Squeezing?
0
LASER
AS port
We better understand shot noise as produced by vacuum fluctuations entering the asymmetric port (AS)
Vacuum fluctuations have equal uncertainty in amplitude and phase
Vacuum fluctuations determine the uncertainty in the interval between photons
The minimal phase variation in the arms which can be measured is:
N number of photons incident on the mirrors in the measurement time
Phase
IFO Signal
Amplitude

## Slide 23: Why Squeezing?
0
LASER
AS port
Squeezed Field
Phase
IFO Signal
Amplitude
23
Squeezed fields with less uncertainty in the “phase” quadrature
The minimal phase variation in the arms which can be measured is:
with r squeeze factor
Amplitude
IFO Signal
Phase
ϑ: squeeze angle
Squeeze Angle:

## Slide 24: How Can you Make Squeezed Fields?
Non linear medium which correlates upper and lower quantum sidebands
SHG
Sum of the correlated sidebands:
the squeezed state
Oven/
Temperature
Sensor
Crystal
Squeezing
Out
Pump light In
PZT Actuator
Optical Parametric Oscillator
(ANU prototype)

## Slide 25: Squeezing Injection
About 20% losses
in the output path (OMC, Faraday)
About 10% losses in the sqz injection path
3 dB of Sqz observed with 6 dB of Sqz produced

## Slide 26: Losses
HAM 4
Squeezing Table
IFO
~20% losses in the IFO output path
~10% losses in the sqz injection path
~ 30% TOTAL LOSSES