## Slide 1: The AWAKE Facility at CERN
EAAC 2015, Elba 13 – 19 September 2015
Edda Gschwendtner, CERN
for the AWAKE Collaboration

## Slide 2: Outline
Motivation
AWAKE Experimental Program
Components of the AWAKE Experiment
Installation of the AWAKE Facility
Outlook and Summary

## Slide 3: AWAKE
Advanced Proton Driven Plasma Wakefield Acceleration Experiment
Proof-of-Principle Accelerator R&D experiment at CERN
  First proton driven wakefield experiment worldwide
  Demonstration of high-gradient acceleration of electrons
  Approved in 2013
  First beam expected in 2016
AWAKE Collaboration: 16 Institutes world-wide
3
Novosibirsk
Vancouver
Oslo
Hamburg, Greifswald
Dusseldorf
Munich
CERN
Lisbon
Manchester
London
Glasgow

## Slide 4: Motivation
ILC
Plasma based Linear Collider
500 GeV: 31 km
500 GeV: 3 km (3000 GeV: 8 km)
* J.P.Delahaye, E. Adli et al., White Paper input to US Snowmass Process 2013
 Provide a design for particle physics frontier accelerator

## Slide 5: Laser or Electron Beam Driven PWA
There is a limit to the energy gain of a witness bunch in the plasma:
  Today’s electron beams usually < 100 J level.
  limitation of the energy carried by the drive beam (< 100J) and the propagation length of the driver in the plasma (<1m).
To reach TeV scale with electron driven PWA: also need several stages, but need to have
  relative timing in 10’s of fs range
  many stages
  effective gradient reduced because of long sections between accelerating elements….
Witness beam
Drive beam: electron/laser
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Plasma cell
Plasma cell

## Slide 6: Proton Beam Driven PWA
Proton beams carry much higher energy:
19kJ for 3E11 protons at 400 GeV/c.
  Drives wakefields over much longer plasma length, only 1 plasma stage needed.
Simulations show that it is possible to gain 600 GeV in a single passage through a 450 m long plasma using a 1 TeV p+ bunch driver of 10e11 protons and an rms bunch length of 100 mm.
Witness beam
Drive beam: protons
Plasma cell
A. Caldwell, K. Lotov, Physics of Plasma, 18,103101 (2011)
See Plenary Talk on Wednesday, 16/9, 11:30 Allen Caldwell

## Slide 7: Beam-Driven Wakefield Acceleration: Landscape
Facility | Where | Drive (D) beam | Witness (W) beam | Start | End | Goal
AWAKE | CERN, Geneva, Switzerland | 400 GeV protons | Externally injected electron beam (PHIN 15 MeV) | 2016 | 2020+ | Use for future high energy e-/e+ collider. Study Self-Modulation Instability (SMI). Accelerate externally injected electrons. Demonstrate scalability of acceleration scheme.
SLAC-FACET | SLAC, Stanford, USA | 20 GeV electrons and positrons | Two-bunch formed with mask (e-/e+ and e--e+ bunches) | 2012 | Sept 2016 | Acceleration of witness bunch with high quality and efficiency Acceleration of positrons FACET II proposal for 2018 operation
DESY-Zeuthen | PITZ, DESY, Zeuthen, Germany | 20 MeV electron beam | No witness (W) beam, only D beam from RF-gun. | 2015 | ~2017 | Study Self-Modulation Instability (SMI)
DESY-FLASH Forward | DESY, Hamburg, Germany | X-ray FEL type electron beam 1 GeV | D + W in FEL bunch. Or independent W-bunch (LWFA). | 2016 | 2020+ | Application (mostly) for x-ray FEL Energy-doubling of Flash-beam energy Upgrade-stage: use 2 GeV FEL D beam
Brookhaven ATF | BNL, Brookhaven, USA | 60 MeV electrons | Several bunches, D+W formed with mask. | On going |  | Study quasi-nonlinear PWFA regime. Study PWFA driven by multiple bunches Visualisation with optical techniques

## Slide 8: AWAKE at CERN
AWAKE is installed in
CNGS Facility (CERN Neutrinos to Gran Sasso)
 CNGS physics program finished in 2012

## Slide 9: CERN SPS Proton Beam Parameters
Nominal SPS Proton Beam Parameters | 
Momentum | 400 GeV/c
Protons/bunch | 3 1011
Bunch length | sz = 0.4 ns (12 cm)
Bunch size at plasma entrance | s*x,y = 200 mm
Normalized emittance (r.m.s.) | 3.5 mm mrad
Relative energy spread | Dp/p = 0.35%
Drive beam for AWAKE: 400 GeV/c SPS proton beam
SPS longitudinal beam size (sz = 12 cm) is much longer than plasma wavelength (l = 1mm)

## Slide 10: CERN SPS Proton Beam – SMI Instability
 Immediate use of CERN SPS beam
 AWAKE experiment is based on self-modulation instability
  Modulate long SPS bunch to produce a series of ‘micro-bunches’ in a plasma with a spacing of plasma wavelength lp.
    Resonantly drives wakefields
    Effective length and period of modulated beam is set by the plasma wavelength.
    Strong self-modulation effect of proton beam due to transverse wakefield in the plasma
Plasma electron density rplasma
Proton beam density rbeam
J. Vieira et al PoP 19063105 (2012)
See Presentation on Wednesday, 16/9, 18:40, WG6, Konstantin Lotov

## Slide 11: Outline
Motivation
AWAKE Experimental Program
Components of the AWAKE Experiment
Installation of the AWAKE Facility
Outlook and Summary

## Slide 12: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.

## Slide 13: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.
10m
Plasma cell
Rb vapour source

## Slide 14: AWAKE Experimental Program
SPS
protons
10m
SMI
Proton
beam
dump
p
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Plasma cell
Rb vapour source
Proton beam
drives the plasma wakefield + undergoes self-modulation instability.
LHC-type proton beam, 400 GeV/c, 3E11 protons/bunch, s = 400 ps long

## Slide 15: AWAKE Experimental Program
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
p
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Plasma cell
Rb vapour source
Proton beam
drives the plasma wakefield + undergoes self-modulation instability.
LHC-type proton beam, 400 GeV/c, 3E11 protons/bunch, , s = 400 ps long
Laser beam:
ionizes the plasma + seeds the self-modulation instability of the proton beam.
4.5 TW laser, 100 fs

## Slide 16: AWAKE Experimental Program
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
Proton diagnostics
BTV,OTR, CTR
p
Plasma cell
Rb vapour source
Proton beam
drives the plasma wakefield + undergoes self-modulation instability.
LHC-type proton beam, 400 GeV/c, 3E11 protons/bunch, s = 400 ps long
Laser beam:
ionizes the plasma + seeds the self-modulation instability of the proton beam.
4.5 TW laser, 100 fs
Diagnostics
BTVs, OTR, CTR
Phase 1: Understand the physics of self-modulation instability processes in plasma.

## Slide 17: AWAKE: Experimental Program
Plasma electron density rplasma
Proton beam density rbeam
Self-modulated proton bunch resonantly driving plasma wakefields.
laser pulse
proton bunch
gas
plasma
J. Vieira et al PoP 19063105 (2012)
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
Proton diagnostics
BTV,OTR, CTR
p
Phase 1: Understand the physics of self-modulation instability processes in plasma.
 Start with physics Q4 2016!

## Slide 18: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Phase 2: Probe the accelerating wakefields with externally injected electrons.
Laser
dump
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
p
Plasma cell
Rb vapour source
Proton beam
drives the plasma wakefield + undergoes self-modulation instability.
LHC-type proton beam, 400 GeV/c, 3E11 protons/bunch, , s = 400 ps long
Laser beam:
ionizes the plasma + seeds the self-modulation instability of the proton beam.
4.5 TW laser, 100 fs
Diagnostics
BTVs, OTR, CTR
Electron source and beam
Witness beam to ‘surf’ on the wakefield and get accelerated
16 MeV/c, 1.2 E9 electrons/ bunch, s = 4ps long
Proton diagnostics
BTV,OTR, CTR

## Slide 19: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Phase 2: Probe the accelerating wakefields with externally injected electrons.
Laser
dump
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
p
Plasma cell
Rb vapour source
Proton beam
drives the plasma wakefield + undergoes self-modulation instability.
LHC-type proton beam, 400 GeV/c, 3E11 protons/bunch, s = 400 ps long
Laser beam:
ionizes the plasma + seeds the self-modulation instability of the proton beam.
4.5 TW laser, 100 fs
Diagnostics
BTVs, OTR, CTR
Electron source and beam
Witness beam to ‘surf’ on the wakefield and get accelerated
16 MeV/c, 1.2 E9 electrons/ bunch, s = 4ps long
Electron spectrometer system
Proton diagnostics
BTV,OTR, CTR
e- spectrometer

## Slide 20: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Phase 2: Probe the accelerating wakefields with externally injected electrons.
Laser
dump
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
p
Proton diagnostics
BTV,OTR, CTR
e- spectrometer
Maximum amplitude of the accelerating field Ez as a function of position along the plasma. Saturation of the SMI at ~4m.
laser pulse
proton bunch
gas
plasma
electron bunch

## Slide 21: AWAKE Experimental Program
Phase 1: Understand the physics of self-modulation instability processes in plasma.
Phase 2: Probe the accelerating wakefields with externally injected electrons.
Laser
dump
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
p
Proton diagnostics
BTV,OTR, CTR
e- spectrometer
Energy of the electrons gained along the 10 m long plasma cell.
laser pulse
proton bunch
gas
plasma
electron bunch
 Start with physics Q4 2017!
See Presentation on Wednesday, 16/9, 18:50, WG1, Alexey Petrenko
See Poster Session on Wedneday, 16/9, 20:00 Petr Tuev
K. Lotov et al., arXiv: 1408.4448

## Slide 22: Outline
Motivation
AWAKE Experimental Program
Components of the AWAKE Experiment
Installation of the AWAKE Facility
Outlook and Summary

## Slide 23: Plasma Source: Rubidium Vapor Source
Density adjustable from 1014 – 1015 cm-3
10 m long, 4 cm diameter
Plasma density = vapor density
System is oil-heated: 150˚ to 200˚ C
  keep temperature uniformity
  Keep density uniformity
Required:
Dn/n = DT/T ≤ 0.002
10 m long plasma cell prototype in the AWAKE test area at CERN
See Poster Session on Monday, 14/9, 20:00 Olaf Grulke
See Presentation on Tuesday, 15/9, 15:00, Erdem Oz

## Slide 24: Laser
Laser intensity must exceed ionization intensity at the plasma end (L=10m) over a plasma radius of r > 3s = 600 µm.
Laser system in MPI, Munich
Laser Beam | 
Laser type | Fiber Ti:Sapphire
Pulse wavelength | l0 = 780 nm
Pulse length | 100-120 fs
Pulse energy (after compr.) | 450 mJ
Laser power | 4.5 TW
Focused laser size | sx,y = 1 mm
Rayleigh length ZR | 5 m
Energy stability | ±1.5% r.m.s.
Repetition rate | 10 Hz
Laser will be moved to CERN in February 2016
See Poster Session on Wednesday, 16/9, 19:30, Joshua Moody

## Slide 25: Proton Beam Diagnostics: Direct Measurement of SMI
 transforming the charge distribution information into a radiation distribution using transition radiation
 Measured radiation emitted by the bunch when traversing a dielectric interface or by directly sampling the bunch space charge field.  streak-camera.
sp ~ 400 ps
4 ps
CTR & TCTR
OTR
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
p
OTR, CTR
Laser
dump
See Poster Session on Wednesday, 16/9, 19:30, Karl Rieger
See Poster Session on Wednesday, 16/9, 19:30 Mikhail Martyanov

## Slide 26: Proton Beam Diagnostics: Indirect Measurement of SMI
Laser
dump
SPS
protons
10m
SMI
Proton
beam
dump
Laser
p
1st BTV
2nd BTV
Laser
dump
SMI causes angular divergence of the proton beam at the order of ~1 mrad.
 Measure bunch profile at two different scintillator screens at a distance of ~8m.
Energy deposition in GeV/cm3 per primary proton particle.
Measure saturation point of SMI at a 2% level.
See Poster Session on Wednesday, 16/9, 19:30 Marlene Turner

## Slide 27: Electron Witness Beam – Electron Source
PHIN Photo-injector for CTF3/CLIC:
  Program will stop end 2015  Fits to requirements  used for AWAKE
Length ~ 4 m
FC
E, DE
MS
BPR
Laser +Diagnostics
RF GUN
Emittance
Incident, Reflected Power and phase
Spectrometer
Corrector
MTV
VPI
FCT
Accelerator
MTV,
Emittance
Matching triplet
BPR
BPR
Incident, Reflected, transmitted Power
Klystron from CTF3
electron beam line
1m booster linac
(Cockcroft)
e-beam diagnostics
Electron beam for AWAKE | Baseline | Range for upgrade phase
Momentum | 16 MeV/c | 10-20 MeV
Electrons/bunch (bunch charge) | 1.25 E9 | 0.6 – 6.25 E9
Bunch charge | 0.2 nC | 0.1 – 1 nC
Bunch length | sz =4ps (1.2mm) | 0.3 – 10 ps
Bunch size at focus | s*x,y = 250 mm | 0.25 – 1mm
Normalized emittance (r.m.s.) | 2 mm mrad | 0.5 – 5 mm mrad
Relative energy spread | Dp/p = 0.5% | <0.5%
See Presentation on Monday, 14/9, 18:30, WG1, Steffen Doebert, Kevin Pepitone
Notes: Initially the injected electron bunch will be at least one plasma period long in order avoid precise timing of a much shorter electron bunch with respect to the wakefields

## Slide 28: Electron Witness Beam Acceleration Diagnostics
Probe the accelerating wakefields with externally injected electrons  Electron spectrometer
p
e-
Scintillator screen (GadOx)
Camera
Dispersed electron impact on scintillator screen.
Resulting light collected with intensified CCD camera.
8.5 ton, 1.2 T, 1.3 Tm, L=1.6 m, W=1.3 m
%-level energy resolution can be achieved with a signal to noise ratio larger than 1000:1

## Slide 29: Outline
Motivation
AWAKE Experimental Program
Components of the AWAKE Experiment
Installation of the AWAKE Facility
Outlook and Summary

## Slide 30: AWAKE Installation
AWAKE experiment
dump
~1100m
SPS
LHC
protons

## Slide 31: AWAKE Experimental Facility
Laser
dump
e- spectrometer
e-
SPS
protons
10m
SMI
Acceleration
Proton
beam
dump
RF gun
Laser
p
Proton diagnostics
BTV,OTR, CTR
AWAKE experiment
protons
proton beam
plasma cell
diagnostics
laser
room
electron source, klystron
See Poster Session on Monday, 14/9, 19:30, Ans Pardons

## Slide 32: Proton Beam Line
Proton beam line
Move existing dipole + 4 additional dipoles to create a chicane for laser mirror integration
Window to sectorize SPS and AWAKE vacuum:
best position from the optics point of view
energy deposition, emittance blowup and secondary shower studies with FLUKA
0.2 mm Al window
See Poster Session on Monday, 14/9, 19:30 Janet Schmidt

## Slide 33: Proton Beam Line
Proton beam line
Displace existing CNGS magnets of final focusing to fulfill optics requirements at the entrance of the plasma cell
sx,y = 200 mm, en = 3.5 mm mrad

## Slide 34: Electron Source
Challenging integration of the electron source
Use load lock cathode system to allow for different types of cathodes
PHIN RF-gun
Klystron
See Presentation on Monday, 14/9, 18:30, WG1, Steffen Doebert, Kevin Pepitone

## Slide 35: Electron Beam Line
Protons from SPS
Laser Merging Point
Electron Source
Electron Merging Point
Common Beam Line
Start of Plasma Cell
See Poster Session on Monday, 14/9, 19:30 Janet Schmidt

## Slide 36: Electron Beam Line
Completely new beam line and tunnel:
  Horizontal angle of 60 deg,
  20% slope of the electron tunnel  1.16 m level difference
  5.66% slope of the plasma cell
  ~5 m common beam line between electron and proton
  Vacuum chamber aperture:
    40mm diameter up to merging point
    60 mm diameter in common part
     minimize effect of wakefields, induced by p beam on chamber walls, on e- beam.
Start
BPM03
BPM04
BPM05
BPM06
BPM07
Focal Point
electron source
plasma cell
p-beam

## Slide 37: Electron Injection
Flexible optics for the electron beam in the common beam line upstream the plasma cell is needed.
  Effect of proton beam on the electron beam (wakefield and beam-beam effects)
  Acceptance of the electron injection into the plasma cell
On-axis
Off-set
Plasma cell length
Position along the proton bunch
Position along the proton bunch (z-ct) where the wakefields are both accelerating and focusing for the witness electrons in grey as function of propagation along the 10m long plasma.

## Slide 38: Laser Line
Protons from SPS
Laser Merging Point
Electron Source
Electron Merging Point
Common Beam Line
Start of Plasma Cell
Laser beam line to plasma cell
  l = 780 nm
  t pulse = 100-120 fs
  E = 450 mJ
Diagnostic beam line (“virtual plasma”)
  l = 780 nm
  t pulse = 100-120 fs,
  E ≈ 5 mJ
Laser beam line to electron gun
  l = 260 nm
  t pulse = 0.3-10 ps
  E = 0.5 mJ

## Slide 39: Laser Integration
Latest version of laser room integration
Proposal for hoist rail support
Racks for laser control
and RF equipment

## Slide 40
laser room 2014
Proton tunnel,
Merging with laser beam
Laser Clean Room
laser room today

## Slide 41: Outline
Motivation
AWAKE Experimental Program
Components of the AWAKE Experiment
Installation of the AWAKE Facility
Outlook and Summary

## Slide 42: AWAKE Time Line
AWAKE approved in August 2013
1st Phase: First proton and laser beam in 2016
2nd Phase: first electron beam in 2017+
Physics program for 3 – 4 years
 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Proton and laser beam-line |  |  |  |  |  |  |  | 
Experimental area |  |  |  |  |  |  |  | 
Electron source and beam-line |  |  |  |  |  |  |  | 
Studies, design
Fabrication
Installation
Commissioning
Commissioning
Installation
Modification, Civil Engineering and installation
Study, Design,
Procurement, Component preparation
Study, Design,
Procurement, Component preparation
Data taking
Continue data taking after LS2
Phase 1
Phase 2
Long Shutdown 2
24 months

## Slide 43: Next Steps (Phase 3)
Split-cell mode: SMI in 1st plasma cell, acceleration in 2nd one.
New scalable uniform plasma cells (helicon or discharge plasma cell)
Step in the plasma density  maintains the peak gradient
Need ultra-short electron bunches (~ 300fs)  bunch compression  Almost 100% capture efficiency
Plasma density profile
Maximum wakefield amplitude

## Slide 44: Summary
AWAKE is proof-of-principle accelerator R&D experiment currently being built at CERN.
  First proton-driven wakefield acceleration experiment
  The experiment opens a pathway towards plasma-based TeV lepton collider.
  Strong motivation of the community: long-term prospects for proton-driven PWA exiting
    Provide a design for a particle physics frontier machine by 2022
    Needs extensive experimental program NOW, results with electrons, …
AWAKE program
  Installation of the AWAKE facility
  Study the physics of self-modulation instability as a function of plasma and proton beam parameters (1st Phase, 2016)
  Probe the longitudinal accelerating wakefields with externally injected electrons (2nd Phase, 2017-2018)
  Reach higher gradients, develop long scalable and uniform plasma cells, production of shorter electron and proton bunches (2020)